## Slide 1
Recent Progress of MODIS and VIIRS Lunar Calibration
Truman Wilsona, Amit Angala , Jack Xiongb
aScience Systems and Applications Inc., 10210 Greenbelt Road, Lanham, MD, USA
bSciences and Exploration Directorate, NASA Goddard Space Flight Center, Greenbelt, MD, USA
GSICS Annual Meeting 2024, Darmstadt, Germany March 11-15, 2024

## Slide 2
Outline
Introduction
MODIS RSB lunar calibration
VIIRS RSB lunar calibration
Additional Lunar Observation Applications
Ongoing and Future Efforts
Summary

## Slide 3: MODIS and VIIRS Lunar Calibration
MODIS and VIIRS share the same calibration strategies
  No SRCA in VIIRS
  VIIRS SV and SD have the same AOI
Lunar observations are scheduled on a near-monthly basis for a fixed phase angle range.
  The Moon is observed through the space-view (SV) port via a spacecraft roll maneuver.
  A data section rotation is performed
The Moon as an inter-comparison target:
  Observable by many instruments
  No overpass time constraints
  No atmospheric correction
  View-geometry corrections (lunar model).

## Slide 4: Lunar Observation Geometry
Track
Scan
* VIIRS shows the opposite relationship in roll angle vs SV trace size as its SV is on the opposite side of the y-axis
*
*
Inst. | Launch Year | Phase Range+ | Roll Range | # Events^
Terra | 1999 | 55° to 56° | -20° to 0° | 233
Aqua | 2002 | -55° to -56° | -20° to 0° | 220
SNPP | 2011 | -50.5° to -51.5° | -14° to 0° | 103
N20 | 2017 | -50.5° to -51.5° | -14° to 0° | 52
N21 | 2022 | -50.5° to -51.5° | -14° to 0° | 9
*
+ Some events fall outside of this range
^ Number of scheduled Moon events as of March 1, 2024.
Terra MODIS Band 1 Lunar Images
For MODIS and VIIRS, the Moon is visible in the SV for many scans. Only scans with the full lunar disk visible are used for calibration (below, red).

## Slide 5: Applications of MODIS and VIIRS Lunar Observations
Reflective Solar Bands (RSB)
  Stability Monitoring (MODIS and VIIRS)
    RVS characterization (MODIS) and SD degradation adjustment (VIIRS)
  Calibration Inter-comparisons (MODIS, VIRS, SeaWiFS, VIIRS, Pleiades, SGLI)
  Spatial (MODIS and VIIRS)
    Band-to-band registration (BBR) and MTF
  Other Applications
    Thermal leak and electronic crosstalk characterization (MODIS SWIR bands)
    VIIRS Day-Night band (DNB) characterization using the Moon
Thermal Emissive Bands (TEB)
  Stability Monitoring (MODIS and VIIRS)
  Calibration Inter-comparisons (VIIRS)
  Other Applications
    Relative calibration for low gain (fire detection) bands (MODIS and VIIRS)
    Electronic crosstalk and optical leak characterization (MODIS)
References included in the Appendix

## Slide 6: Lunar Calibration Methodology
Lunar irradiance computed using integration of each scan image.
In the current MODIS and VIIRS calculations, only images with the full disk of the Moon on the FPA are used.
Previous MODIS calibrations also used partial images and compensated by applying an oversampling factor.
Variation in the irradiance is mostly caused by view geometry differences between events. This variation can be removed by normalizing to the ROLO model.

## Slide 7: MODIS Lunar Calibration
Moon and SD views at different AOI.
Difference in trending is inferred as a difference in the scan mirror response versus scan angle (RVS).

## Slide 8: VIIRS Lunar Calibration
Moon and SD views at the same AOI.
Moon can be used to apply correction to the SD trending data.

## Slide 9: NOAA-21 VIIRS Lunar Calibration
NOAA-21 VIIRS has almost 1 full year of lunar calibration data.
Large gain changes in the SWIR bands were observed and attributed to icing.
A mid-mission outgas (MMOG) has restored the SD gain to near the pre-launch levels.
The next lunar calibration will be in late March 2024.
MMOG
MMOG

## Slide 10: Applications: Calibration Intercomparison
Lunar observations can be used to compare bands across multiple instruments.
  The ROLO model is used to account for differences in observation geometry.
  Offsets between the measurements and ROLO are nearly constant.
Normalization to ROLO shows some calibration differences between the bands of different instruments as a function of wavelength.
Xiong et al. Remote Sens. 2022, 14, 4754.

## Slide 11: Applications: Calibration Intercomparison
Additional corrections, such as a solar spectrum reference correction are needed for proper comparison.
  Example: SNPP uses Kurucz while N20 uses Thuillier. A more consistent calibration intercomparison can be performed by deriving all the calibration data using TSIS-1 HSRS data.
  Alternatively, a correction factor can be applied to the ratio with the following equations:
Xiong et al. Remote Sens. 2022, 14, 4754.

## Slide 12: Applications: MODIS and VIIRS Spatial Characterization
VIIRS* Focal Plane Layout
*MODIS has similar spatial offsets
VIIRS unscheduled Moon images showing spatial offsets
Centroids or image X-correlation are used to compute the Band-to-Band Registration (BBR) from the reference band†.
Aqua MODIS Band 8
N20 VIIRS
Band M9
† Band 1 for MODIS, and I1 for VIIRS
Wilson et al. IEEE TGRS 60, 4702312, 2022.

## Slide 13
13
Terra
Aqua
Orbit simulations provided by Earth Science Mission Operations (ESMO) Flight Dynamics System (FDS) at NASA/GSFC
Ongoing and Future Efforts: MODIS Lunar Phase Drift

## Slide 14
14
Terra Band 8
Aqua Band 19
Where we’ve been
Where we’re going
Where we’re going
Where we’ve been
History
2023
2024
2025
2026
History
2023
2024
2025
2026
Unscheduled Moon data combined with special Moon data used to determine the expected phase change.
The “special” data collects will continue whenever the opportunity is available.
Wilson et al. Proc. SPIE 1272917, 2023.
Details also presented at the GSICS Lunar Workshop, Dec. 2023.
Ongoing and Future Efforts: MODIS Lunar Phase Drift

## Slide 15: Future Efforts: TEB Lunar Calibration/Intercomparisons
MODIS/VIIRS Thermal Emissive Bands (TEB) also observe the Moon.
High signal levels cause saturation for nearly all TEB.
Pixel-wise comparison can be performed with surface-resolved thermal model of the Moon.
*Model data courtesy of Thomas Müller of MPE
See: Müller et al. A&A 650, A38, 2021.
  Corrections associated with Sun-Moon and Moon-Instrument distance are not applied below.

## Slide 16: Conclusions
MODIS and VIIRS lunar observations have been implemented successfully into the on-orbit calibration of each instrument.
  The MODIS lunar calibration is used to track the scan mirror RVS
  The VIIRS lunar calibration is used to adjust the SD F-factor.
  NOAA-21 lunar calibrations have begun and have almost 1 full year of lunar calibrations.
Moon observations can also be used for many alternative applications, including instrument intercomparison, spatial calibration, and electronic crosstalk correction.
Future Work:
  MODIS orbital drift monitoring and phase dependence correction.
  TEB calibration and intercomparison with spatial-resolved thermal models.

## Slide 17: Key References
Sun, J.-Q., et.al, “MODIS Reflective Solar Bands On-Orbit Lunar Calibration”, IEEE TGRS, vol. 45(7), 2383-2393, 2007.
Xiong, X, et.al, "Intercomparison of On-Orbit Calibration Consistency Between Terra and Aqua MODIS Reflective Solar Bands Using the Moon," IEEE GRSL, vol. 5( 4), pp. 778-782, 2008.
Xiong, X. and H. Chen, “Using lunar observations to assess Terra MODIS thermal emissive bands calibration,” Proc. SPIE 7807, Earth Observing Systems XV, 78070I, 2010.
Sun, J., et.al, “Evaluation of Radiometric Improvements With Electronic Crosstalk Correction for Terra MODIS Band 27”, IEEE TGRS, vol 52(10), 6497-6507, 2014.
Choi, T., et.al, “On-Orbit Lunar Modulation Transfer Function Measurements for the Moderate Resolution Imaging Spectroradiometer”, IEEE TGRS, vol 53(1), 270-277, 2014.
Wang, Z., et.al, “On-Orbit Characterization of MODIS Modulation Transfer Function Using the Moon”, IEEE TGRS, vol 52(7), 4112-4121, 2014.
Xiong, X., et.al, “Lunar Calibration and Performance for S-NPP VIIRS Reflective Solar Bands”, IEEE TGRS, vol. 54, issue 2, pp. 1052-1061, 2016.
Wilson, T., et.al, "Development and Implementation of an Electronic Crosstalk Correction for Bands 27–30 in Terra MODIS Collection 6", Remote Sensing, vol. 9(6), 569, 2017.
Wang, Z., X. Xiong, J. Fulbright, and N. Lei, "VIIRS day/night band radiometric calibration stability monitoring using the Moon", J. Geophysical Research, vol. 122(11), pp. 5616-5624, 2017.
Wilson, T., and X. Xiong, "Surface Corrected Lunar MTF Measurements in MODIS and VIIRS Using the SP Model," IEEE TGRS, vol. 60, pp. 1-12, Art no. 5110112, 2022
Xiong, X., J. Sun, A. Angal, T. Wilson, "Calibration Inter-Comparison of MODIS and VIIRS Reflective Solar Bands Using Lunar Observations", Remote Sensing Journal, 14 (21), 4754, 2022

## Slide 18
MODIS and VIIRS use similar but slightly different equations to compute the lunar irradiance
MODIS
VIIRS
N: Number of scans m1: Calibration coefficient
S,D: Scan, Detector
dn: Background-subtracted signal
RVS: Response versus scan angle
ω: Detector solid angle
Esun: Solar spectral irradiance
N: Number of scans F: F-factor derived from SD data
S,D: Scan, Detector
dn: Background-subtracted signal
RVS: Response Versus Scan Angle
ω: Detector Solid Angle
ci: Calibration Coefficients
The principles of each calculation are the same. Integrate dn times the calibration coefficients, and average over the total number of scans used.
Appendix: Lunar Calibration Methodology

## Slide 19
SP Model provided by Toru Kouyama of AIST (Japan) in January 2021.
Measured Image
Model Projection
Measured/Modeled Ratio
Model data is projected onto image coordinates using the observation geometry parameters.
Appendix: MTF Surface Correction with SP Model
Wilson et al. IEEE TGRS 60, 5110112, 2022.

## Slide 20
Terra MODIS Band 1
N20 VIIRS Band M7
Surface correction creates a smooth profile.
MTF derived from FFT of the line spread function.
Appendix: MTF Surface Correction with SP Model
Wilson et al. IEEE TGRS 60, 4702312, 2022.

## Slide 21
Electronic Crosstalk characterized using known spatial offsets beween lunar images.
Derived correction coefficients are used to correct the Level-1B imagery
Sending Bands
Band 27
Band 28
Band 29
Band 30
Appendix: MODIS Electronic Crosstalk Characterization
Aqua MODIS
Band 27
Chang et al. Proc. SPIE 126851E, 2023.