## Slide 1
Update on the MICMICS implementation of the GSICS DCC algorithm
S. Wagner, R. Shanbhag*, A. Mousivand, V. Debaecker*
* Telespazio
GSICS annual meeting 2024

## Slide 2: GSICS DCC and MICMICS
#9ba9ea
DCC Calibration
DCC Inter-Calibration
Desert Calibration
Desert Inter-Calibration
Lunar Calibration
Imager-Hyperspectral
Inter-Calibration
Lunar Inter-Calibration
Rayleigh Calibration
Rayleigh Inter-Calibration
Imager-Imager
Inter-Calibration
NWP Calibration
NWP Inter-Calibration
DCC Extraction Module
Lunar Extraction Module
Subsetter Tool
Data-Fusion Tool
Pre-Colocation Tool
Colocation Tool
Inter-Calibration Blender
Sun Glint Inter-Calibration
Radiative Transfer Module
Snow and Ice Inter-Calibration
SEVIRI
FCI
LI
SLSTR
OLCI
METimage
AVHRR
3MI
CLIM
MAP
SEVIRI
FCI
SLSTR
METimage
Ray-Matching
Inter-Calibration
UVN
UVNS

## Slide 3: GSICS DCC and MICMICS
#9ba9ea
DCC Calibration
DCC Inter-Calibration
Desert Calibration
Desert Inter-Calibration
Lunar Calibration
Imager-Hyperspectral
Inter-Calibration
Lunar Inter-Calibration
Rayleigh Calibration
Rayleigh Inter-Calibration
Imager-Imager
Inter-Calibration
NWP Calibration
NWP Inter-Calibration
DCC Extraction Module
Lunar Extraction Module
Subsetter Tool
Data-Fusion Tool
Pre-Colocation Tool
Colocation Tool
Inter-Calibration Blender
Sun Glint Inter-Calibration
Radiative Transfer Module
Snow and Ice Inter-Calibration
SEVIRI
FCI
LI
SLSTR
OLCI
METimage
AVHRR
3MI
CLIM
MAP
SEVIRI
FCI
SLSTR
METimage
Ray-Matching
Inter-Calibration
UVN
UVNS

## Slide 4: MICMICS DCCICS workflow
Data subsetter
Subsets of L1C products over ROI
Level 1C products
Calibration Output Database
DCCXTRM
(DCC extraction)
11m band available ?
Yes
DCCICS
GSICS DCC products
Inter-Calibration Blender
GEO imagers such as SEVIRI, FCI
Polar radiometers such as AVHRR, SLSTR, METimage

## Slide 5: MICMICS DCCICS workflow
Data subsetter
Subsets of L1C products over ROI
Level 1C products
Calibration Output Database
DCCXTRM
(DCC extraction)
Data fusion
(Remapping of IR sensor to monitored instrument grid)
11m band available ?
No
Data-fused products over ROI
DCCICS
GSICS DCC products
Inter-Calibration Blender
OLCI
SLSTR
SLSTR
GEO imagers such as LI
Polar radiometers such as OLCI, 3MI

## Slide 6: Set-up for MSG/SEVIRI
Reference channels
Reference radiance: as per the GSICS ATBD (for Lon 45.5E, same as for Lon 41.5E)
For SWIR, no reference value from VIIRS  based on typical radiance for SEVIRI
Homogeneity test done on all channels (not only on VIS0.6)
SEVIRI channel | VIIRS reference band
VIS0.6 | M5
VIS0.8 | M7
NIR1.6 | M10 (only for SBAF – no ref value)
HRV | M5

## Slide 7: SEVIRI – timeseries – calibration gains

## Slide 8: MSG/SEVIRI warm stability radiometric stability

## Slide 9: Set-up for OLCI
Reference channels for OLCI
Reference radiance: as per the GSICS ATBD (at Lon 0.0)
Homogeneity test done on all channels (including SLSTR)
Issue of the DCC very cold temperature (SLSTR cold end)
Data filtered using saturation flags
OLCI channel | VIIRS reference band
Oa01 | M1
Oa02 | M1
Oa04 | M3
Oa05 | M4
Oa06 | M4
Oa07 | I1
Oa08 | M5
Oa09 | M5
Oa10 | M5
OLCI channel | VIIRS reference band
Oa11 | M6
Oa12 | M6
Oa13 | M6
Oa14 | M6
Oa15 | M6
Oa16 | I6
Oa18 | M7
Oa19 | M7
Oa21 | M7
Difference in the overpassing time between S3 and NOAA-20
Purpose is to monitor the radiometric stability
Brute force: we extract everything and see what comes out!

## Slide 10
OLCI channels

## Slide 11: OLCI-A – Timeseries / PDF mode

## Slide 12: OLCI-A – Timeseries / Correction

## Slide 13: Set-up for SLSTR
Reference channels
Reference radiance: as per the GSICS ATBD
Homogeneity test done on all channels (including OLCI)
Remember that SLSTR is for SST, not meant to measure very cold temperatures such as for DCC…
SLSTR channel | VIIRS reference band
S1 | M4
S2 | M5
S3 | M7

## Slide 14
SLSTR channels

## Slide 15: SLSTR-A – Timeseries / PDF mode

## Slide 16: SLSTR-A – Timeseries / Correction

## Slide 17: Summary for OLCI-A and SLSTR-A
Drift in % per year | OLCI-A | 
 | MICMICS | 
 | DESCS (Obs/Simu) | DCC (Corr)
Oa01 | 0.02 ± 0.01 | -0.13 ± 0.01
Oa02 | 0.02 ± 0.01 | -0.06 ± 0.01
Oa03 | -0.01 ± 0.01 | 
Oa04 | -0.03 ± 0.01 | -0.12 ± 0.01
Oa05 | -0.03 ± 0.01 | 0.0 ± 0.01
Oa06 | -0.05 ± 0.01 | -0.09 ± 0.01
Oa07 | -0.01 ± 0.01 | -0.09 ± 0.01
Oa08 | -0.01 ± 0.01 | -0.25 ± 0.01
Oa09 | 0.01 ± 0.01 | -0.04 ± 0.01
Oa10 | 0.01 ± 0.01 | -0.1 ± 0.01
Drift in % per year | OLCI-A | 
 | MICMICS | 
 | DESCS (Obs/Simu) | DCC (Corr)
Oa11 | 0.01 ± 0.01 | -0.04 ± 0.01
Oa12 | 0.01 ± 0.01 | -0.08 ± 0.0
Oa13 |  | 0.03 ± 0.02
Oa14 |  | 0.19 ± 0.01
Oa15 |  | 0.25 ± 0.01
Oa16 | 0.02 ± 0.01 | 0.21 ± 0.01
Oa17 | 0.02 ± 0.01 | 
Oa18 | 0.02 ± 0.01 | -0.08 ± 0.01
Oa19 |  | 0.01 ± 0.01
Oa21 | 0.02 ± 0.01 | -0.02 ± 0.01
Drift in % per year | SLSTR-A |  |  |  | 
 | S3MPC | MICMICS | MICMICS |  | 
 |  | Inter-Band | DESCS | DESICS | DCC
S1 | 0.3 ± 0.2 | 0.36 ± 0.03 | 0.37± 0.01 | 0.4± 0.02 | -0.36 ± 0.01
S2 | 0.2 ± 0.1 | 0.2 ± 0.02 | 0.2± 0.01 | 0.21± 0.01 | 0.01 ± 0.0
S3 | 0.3 ± 0.2 | 0.38 ± 0.02 | 0.36± 0.01 | 0.38± 0.01 | -0.22± 0.01
OLCI:
  For OLCI, further work needed on channel selection + reference signal
  Complete time series processing is on-going
  Further data filtering need to improve DCC extraction
  Results are not final…
  SLSTR:
  Some drift observed for S1, S2 and S3

## Slide 18: Conclusion and future work
MICMICS set to extract and process DCC data over specific areas for both LEO and GEOs
Agile system, easy to implement new missions such as MTG/FCI or MTG/LI
NOAA-20 VIIRS set as a new reference
Need to further iterate on selection of bands + reference VIIRS radiance
MICMICS products will replace MODIS products in the demo phase for GEOs  GPPA?
For LEOs, more work needed to derive proper corrections. But promising results for radiometric stability monitoring.

## Slide 19
Thank you!
Questions are welcome.