## Slide 1: DCC BRDF netCDF formats and pixel resolution
David Doelling, Conor Haney, Prathana Khakurel, Rajendra Bhatt, Arun Gopalan
GSICS annual meeting, VIS/NIR session,
EUMETSAT, Darmstadt, Germany, March 14, 2024

## Slide 2: Pixel resolution impact on DCC identification
The DCC methodology relies on identifying DCC pixels based on the following criteria:
  BT11µm < 205 K
  Hom0.65µm < 0.03
  Hom11µm < 1.0 K
  where Hom = spatial homogeneity of 3x3 pixels
Aggregate the VIIRS M band 750-m and Landsat-8 30-m native resolution imagery to lower pixel resolutions
  How does the pixel resolution impact the standard DCC identification thresholds?
  Is the DCC reflectance PDF shape dependent on pixel resolution?
Can the reference DCC reflectance be transferred to other sensors with differing pixel resolution?

## Slide 3: SNPP VIIRS M05 DCC 750-m TSP granule East of Solomon Islands
Himawari-8 0.65µm image

## Slide 4
SNPP-VIIRS, 750m
M05 0.67µm
M15 11µm BT
205K contour
0.8 ref contour
SNPP VIIRS M05 DCC 750-m granule, East of Solomon Islands

## Slide 5
M05 pixel reflectances
M05 pixel reflectances (w/ Hs thresholds)
BTM15 < 205 K
BTM15 < 205 K
HM05 < 0.03
SDVM15 < 1.0 K
Many overshooting tops are removed

## Slide 6: Landsat-8 OLI/TIRS B4 30-m TWP granule Banda Arc, Indonesia

## Slide 7: Landsat-8 OLI/TIRS B4 30-m TWP granule Banda Arc, Indonesia
Landsat-8, 30m
OLI B04 0.66µm
TIRS B1 10.8µm BT
205K contour
0.8 ref contour

## Slide 8: BT Threshold Sensitivity Analysis
SNPP-VIIRS M05, 750m
Landsat 8 OLI/TIRS B4, 30m
BT < 190 K
BT < 195 K
BT < 200 K
BT < 205 K
BT < 210 K
• Decreasing the BT threshold decreases the skewness or darker tail of the PDF
• Increasing the BT threshold increases the frequency of DCC identified pixels

## Slide 9
0.65µm reflectance images by pixel resolution

## Slide 10
0.65µm reflectance 3x3 homogeneity images by pixel resolution

## Slide 11: PDF statistics using homogeneity thresholds
0.75-km
1.5-km
3.0-km
0.75-km
1.5-km
3.0-km
0.03-km
0.06-km
0.12-km
0.24-km
0.48-km
0.96-km
0.03-km
0.06-km
0.12-km
0.24-km
0.48-km
0.96-km
VIIRS M05 0.65µm
BT11µm<205K
OLI B04 0.65µm
BT11µm<205K, Hom on
OLI B04 0.65µm
BT11µm<205K
VIIRS M05 0.65µm
BT11µm<205K, Hom on
BT11µm<205K, Hom on | MEAN | MODE | NUM
x1 (0.75km) | 0.892 | 1.005 | 220937
x2 (1.5km) | 0.890 | 1.015 | 40778
x4 (3.0km) | 0.889 | 1.015 | 5754
BT11µm<205K, Hom on | MEAN | MODE | NUM
x1 (0.03km) | 0.875 | 0.915 | 11979587
x2 (0.06km) | 0.875 | 0.915 | 2967211
x4 (0.12km) | 0.873 | 0.915 | 707787
x8 (0.24km) | 0.867 | 0.915 | 152943
x16 (0.48km) | 0.858 | 0.915 | 27817
x32 (0.96km) | 0.850 | 0.915 | 3854
• For these images the homogeneity thresholds or pixel resolution do not significantly change the shape of the PDF

## Slide 12: DCC BRDF netCDF files
For visible wavelengths the DCC reflectance is well behaved
  Use the Hu DCC BRDF model
  For SWIR bands the DCC reflectance is wavelength dependent
  Need wavelength specific DCC BRDFs
Empirical DCC reflectance BRDFs are based on angular binned pixel-level DCC identified reflectances
Standardization of DCC BRDFs amongst agencies allows the DCC BRDFs to be shared
  Make sure the DCC BRDF netCDF file is self describing for traceability and universal implementation

## Slide 13: Terra-MODIS DCC BRDFs for 35°<SZA<40°
1.64 µm
# of pixels
Mean Reflectance
Sigma Reflectance
1.24 µm
0.65 µm

## Slide 14: DCC BRDF netCDF parameters
netcdf file:/Users/ddoellin/Desktop/DCC_BRDF_2023/DCC_TERRA_MODIS_ADM_All_Months_TWP.nc { dimensions:
n_channel = 4;
n_sza = 18;
n_month = 13;
n_raa = 18;
n_vza = 11;
group: geometry { variables: float nbin_sza_bound(n_sza=18); :long_name = "solar zenith angle bin boundaries"; :units = "degrees"; :lo_bound = 0.0, 5.0, 10.0, 15.0, 20.0, 25.0, 30.0, 35.0, 40.0, 45.0, 50.0, 55.0, 60.0, 65.0, 70.0, 75.0, 80.0, 85.0; // double :high_bound = 5.0, 10.0, 15.0, 20.0, 25.0, 30.0, 35.0, 40.0, 45.0, 50.0, 55.0, 60.0, 65.0, 70.0, 75.0, 80.0, 85.0, 90.0; //
double float nbin_raa_bound(n_raa=18); :long_name = "relative azimuth angle bin boundaries"; :units = "degrees"; :lo_bound = 0.0, 10.0, 20.0, 30.0, 40.0, 50.0, 60.0, 70.0, 80.0, 90.0, 100.0, 110.0, 120.0, 130.0, 140.0, 150.0, 160.0, 170.0; // double :high_bound = 10.0, 20.0, 30.0, 40.0, 50.0, 60.0, 70.0, 80.0, 90.0, 100.0, 110.0, 120.0, 130.0, 140.0, 150.0, 160.0, 170.0, 180.0; //
double float nbin_vza_bound(n_vza=11); :long_name = "view zenith angle bin boundaries"; :units = "degrees"; :lo_bound = 0.0, 5.0, 10.0, 15.0, 20.0, 25.0, 30.0, 35.0, 40.0, 45.0, 50.0, 55.0, 60.0, 65.0, 70.0, 75.0, 80.0, 85.0; // double :high_bound = 5.0, 10.0, 15.0, 20.0, 25.0, 30.0, 35.0, 40.0, 45.0, 50.0, 55.0, 60.0, 65.0, 70.0, 75.0, 80.0, 85.0, 90.0; //
double float raa_bin_centers(n_raa=18); :centers = 5.0, 15.0, 25.0, 35.0, 45.0, 55.0, 65.0, 75.0, 85.0, 95.0, 105.0, 115.0, 125.0, 135.0, 145.0, 155.0, 165.0, 175.0; // double :long_name = "relative azimuth angle bin centers"; :units = "degrees"; :valid_range = 0.0f, 180.0f; // float :bounds = "raa_bound"; float
vza_bin_centers(n_vza=11); :centers = 2.5, 7.5, 12.5, 17.5, 22.5, 27.5, 32.5, 37.5, 42.5, 47.5, 52.5; //
double :long_name = "view zenith angle bin centers"; :units = "degrees"; :valid_range = 0.0f, 90.0f; // float :bounds = "vza_bound";
float sza_bin_centers(n_sza=18); :long_name = "solar zenith angle bin centers"; :units = "degrees"; :valid_range = 0.0f, 90.0f; //
float :bounds = "sza_bound"; :centers = 2.5, 7.5, 12.5, 17.5, 22.5, 27.5, 32.5, 37.5, 42.5, 47.5, 52.5, 57.5, 62.5, 67.5, 72.5, 77.5, 82.5, 87.5; // double

## Slide 15: DCC BRDF netCDF parameters
group: channel_data { variables: String channel_id(n_channel=4);
:channel_names = "B1", "B4", "B6", "B2";
:wavelengths = "1.24um", "1.64um", "2.12um", "1.37um";
String month_id(n_month=13); :months = "January", "February", "March", "April", "May", "June", "July", "August", "September", "October", "November", "December", "Annual";
float channel_brdf_coeff(n_sza=18, n_vza=11, n_raa=18, n_channel=4, n_month=13);
float number_of_pixels(n_sza=18, n_vza=11, n_raa=18, n_channel=4, n_month=13);
float standard_deviation(n_sza=18, n_vza=11, n_raa=18, n_channel=4, n_month=13); :unit = "%"; } //
global attributes:
:title = "DCC BRDF coefficients (TWP)";
:satellite = "TERRA";
:instrument = "MODIS"; :collection = "NASA C7 product";
:DCC_latitude_domain = "±30°";
:DCC_longitude_domain = "95° to 175°"; :DCC_time_range = "Jan 2002 to Dec 2010";
:DCC_temperature_threshold = "<210 K";
:DCC_BT_channel = "B31(11μm)";
:VZA_threshold = "<60°";
:SZA_threshold = "<82°";
:IR_threshold = "<1%";
:VIS_std_threshold = "<3%";
:RAA_threshold = "0° to 180° (0° to 90° as forward scatter)";
:fill_value = -9999.0; // double :created = "2024-01-10 16:15:37";
:author = "Prathana Khakurel";

## Slide 16: Conclusions
DCC identification thresholds
  Colder BT thresholds reduce the tail of the PDF at the expense of sampling
  The spatial homogeneity thresholds remove the overshooting tops and corresponding shadows and partially reduce the PDF tail
Preliminary pixel resolution results
  Pixel resolution impacts the homogeneity factor to identify DCC pixels
  Pixel resolution seems to have only a slight impact on DCC PDF shape allowing for the potential of DCC inter-calibration across pixel resolutions
DCC BRDF netCDF formats
  Make sure all netCDF files are self describing
  Allows DCC BRDF to be shared amongst agencies