## Slide 1
Inter-calibration using desert sites
Ali Mousivand, Sebastien Wagner, Rakshith Shanbhag, Mounir Lekouara and Bertrand Fougnie
GSICS annual meeting 2024
14th March 2024, Darmstadt

## Slide 2: MICMICS (Mission Integrated Calibration Monitoring and Inter-Calibration System)
Main assets:
  Easy integration of new missions;
  Easy integration of new calibration methods;
  Inter-operability of the processing modules;
  Rationalisation of resources + efforts (including maintenance);
  Support the operational generation of GSICS products (and intermediate products such as collocations);
  Support generation of Fundamental Climate Data Records;
Status:
  The prototype has been extensively tested and validated;
  Already supporting the EUMETSAT diagnostics on SEVIRI, AVHRR, OLCI & SLSTR;
  Currently used for the FCI and LI commissioning;
  Developments are on-going for EPS-SG and CO2M.
  Will become the EUM GSICS engine and replace MPSTAR in 2024;
MICMICS = agile system dedicated to the near-real time monitoring of radiometric performances and inter-calibration

## Slide 3: MICMICS workflows
#9ba9ea
DCC Calibration
DCC Inter-Calibration
Desert Calibration
Desert Inter-Calibration
Lunar Calibration
Imager-Hyperspectral
Inter-Calibration
Lunar Inter-Calibration
Rayleigh Calibration
Rayleigh Inter-Calibration
Imager-Imager
Inter-Calibration
NWP Calibration
NWP Inter-Calibration
DCC Extraction Module
Lunar Extraction Module
Subsetter Tool
Data-Fusion Tool
Pre-Colocation Tool
Colocation Tool
Inter-Calibration Blender
Sun Glint Inter-Calibration
Radiative Transfer Module
Snow and Ice Inter-Calibration
SEVIRI
FCI
LI
SLSTR
OLCI
METimage
AVHRR
3MI
CLIM
MAP
SEVIRI
FCI
SLSTR
METimage
Ray-Matching
Inter-Calibration
UVN
UVNS
#9ba9ea
DCC Calibration
DCC Inter-Calibration
Desert Calibration
Desert Inter-Calibration
Lunar Calibration
Imager-Hyperspectral
Inter-Calibration
Lunar Inter-Calibration
Rayleigh Calibration
Rayleigh Inter-Calibration
Imager-Imager
Inter-Calibration
NWP Calibration
NWP Inter-Calibration
DCC Extraction Module
Lunar Extraction Module
Subsetter Tool
Data-Fusion Tool
Pre-Colocation Tool
Colocation Tool
Inter-Calibration Blender
Sun Glint Inter-Calibration
Radiative Transfer Module
Snow and Ice Inter-Calibration
SEVIRI
FCI
LI
SLSTR
OLCI
METimage
AVHRR
3MI
CLIM
MAP
SEVIRI
FCI
SLSTR
METimage
Ray-Matching
Inter-Calibration
UVN
UVNS

## Slide 4: DESert Inter-Calibration System (DESICS)
Uses desert Pseudo Invariant Calibration Sites (PICS) to transfer the calibration from a reference instrument to the monitored instrument.
BOA reflectance retrieval
  Atmospheric correction: Customised version of the polarized 6SV2.1,
  Atmosphere:
    Customized Desert Aerosol model over the Sahara and Arabian Peninsula;
    US standard atmosphere, scaled with H2O and O3 column;
    O3, WV, surface pressure from ECMWF, and AOT550 from CAMS;
TOA reflectance simulation
  RTM: customised version of the polarized 6SV2.1
  Surface: simulated spectral surface reflectance for monitored instrument
  Atmosphere: same as those of BOA reflectance retrieval
Filtering
  Apply geometry criteria
  | | < 2 deg
  | | < 2 deg
  | | < 5 deg
  SZA<60
Evaluate & Monitor bias:
  Estimate the relative calibrations by comparing TOA simulated reflectance against actual measurements
Monitored instrument
Reference instrument
Forward RT simulation
Update Meteo data
Reference BOA reflectance
Atmospheric correction
Outlier removal
Update Meteo data
Simulated BOA reflectance for monitored instrument
Spectrally interpolate BOA reflectance
Calibration coefficients
High resolution spectrum
Filtering observations by geometry criteria
(∆SZA, ∆VZA, ∆RAA)
Simulated TOA reflectance for monitored instrument
Measured TOA reflectance

## Slide 5: Atmospheric correction
To extract the BOA reflectance for the reference instrument
The customized polarized 6SV2.1 integrated atmospheric correction module is used
SMAC is the frequently used approach by other desert-inter-cal systems
Expected accuracy of SMAC is understood to be 2-3% (similar on 6SV)
6SV is expected to offer similar accuracy if not better
All atmospheric parameters are spatially and temporally interpolated over each target

## Slide 6: Spectral interpolation
To transfer the reference BOA reflectance to monitored one
Currently, the ρ0 (mean reflectance) parameter of the RPV model BRDF is used
Critical step when there's a disparity in SRF between the reference and monitored instruments
Notes: ρ0 (mean reflectance), Θ(Asymmetry parameter), k (Minnart parameter), h (hot spot parameter)
Effort is on-going to create a database of Hyperspectral over desert targets using data from DESIS, EnMap

## Slide 7: Pseudo Invariant Calibration Sites (PICS)
Six priority one targets: Libya4, Egypt1, Algeria5, Niger2, Sudan1 and Arabia2 (skipped for this analysis)
Total observations:
S3A SLSTR: 6,548
S3B SLSTR: 4,597
MSG4: 256,971
Algeria5
S3A SLSTR: 1028
S3B SLSTR: 775
MSG4: 40,890
Libya4
S3A SLSTR: 1321
S3B SLSTR: 937
MSG4: 60,235
Egypt1
S3A SLSTR: 1458
S3B SLSTR: 1013
MSG4: 58,140
Niger2
S3A SLSTR: 1316
S3B SLSTR: 903
MSG4: 45,577
Sudan1
S3A SLSTR: 1425
S3B SLSTR: 969
MSG4: 52,129
S3A and S3B SLSTR and MSG4-SEVIRI observations until March 2024
Algeria-5
Libya-4

## Slide 8: SLSTR-A Desert Inter-calibration (Ref: OLCI-A & OLCI-B)
DESICS

## Slide 9: SLSTR-B Desert Inter-calibration (Ref: OLCI-A & OLCI-B)
DESICS

## Slide 10: MSG4 SEVIRI Desert Inter-calibration (Ref: OLCI-A)
Algeria-5
Libya-4

## Slide 11: MSG4 SEVIRI Desert Inter-calibration (Ref: OLCI-B)
Algeria-5
Libya-4
    Only Libya-4 for OLCI-B

## Slide 12: MSG4-SEVIRI inter-calibration with OLCI-A and OLCI-B
    A bias between the two?
    OLCI channels cover 400nm -1020nm, using OLCI for NIR1.6???

## Slide 13: Inter-calibration MSG4-SEVIRI comparison with Lunar and desert
    Preliminary results, still promising!

## Slide 14: Discussions and conclusions
Why Desert Inter-calibration?
  The method offers great potential inter-calibration
  Relevant for all spectral bands from VIS to SWIR
  Variety of reference instruments can serve as references
  All desert targets can be used (no concern regarding BRDF)
  Temporal calibration accuracy remains independent of the reference sensor used
Limitation and challenges
  Constraints for use as an absolute calibration method
  Accuracy is contingent upon factors such as atmospheric correction, calibration of reference instruments, and differences in SRF

## Slide 15: Discussions and conclusions
  Atmospheric correction
    Improving the atmospheric correction model?
  Spectral interpolation
    Finding the best spectral interpolation method?
      Machine learning approach?
      Using SBAF?
      Use of a continuous spectral database (e.g. from hyperspectral instruments such as EnMap, DESIS) instead of a single reference spectra?
    Seeking to develop a methodology with less reliance on user input
  Filtering
    Time filtering?
    Fixed criteria or dynamic?

## Slide 16
Thank you!
Questions are welcome.