## Slide 1
Evaluation of Hyperspectral Infrared Sounder Data with PCA
Shin Koyamatsu & Pierre Dussarrat
Remote Sensing Scientists
GSICS Meeting – 13/03/2024

## Slide 2: Agenda
Principal Component Analysis
Instrument: FY-3E / HIRAS-2
Noise Estimation
Anomaly Detection
Harmonisation Experiments
Conclusion

## Slide 3: Principal Component Analysis (PCA)
PCA is a popular dimension reduction methodology.
The methodology is data driven; a set of “signals axes” called the Principal Components (PC) is chosen as the eigenvectors of the signal covariance:
PCA splits the measurements (the light power spectra ) into independent pieces called the Principal Component Scores (PCS).
Eigenvalues represent variability of PCSs, corresponding to the Signal-to-Noise Ratio if signals are noise-normalized.
https://en.wikipedia.org/wiki/Principal_component_analysis

## Slide 4: PCA at EUMETSAT
Dissemination of the PCS
  Available to users for METOP-IASI data
  Dissemination baseline for MTG-S IRS; The users will use the PCS to reconstruct the radiances on their side
EUMETSAT is studying the interest of PCA for many years.
This presentation provides examples of application of PCA:
  Computation of instrumental noise without prior-knowledge of the instrument
  Detection of instrumental anomalies
  Experiment of data harmonisation
Hultberg, T. et al. "Local or global? How to choose the training set for principal component compression of hyperspectral satellite measurements: a hybrid approach." Sensors, Systems, and Next-Generation Satellites XXI. Vol. 10423. SPIE, 2017.

## Slide 5: Agenda
Principal Component Analysis
Instrument: FY-3E / HIRAS-2
Noise Estimation
Anomaly Detection
Harmonisation Experiments
Conclusion

## Slide 6: FY-3E / HIRAS-2
Launch: 04 Jul 2021
Orbit: Sun synchronous (ECT 05:40)
Configuration:
  28 Fields of Regard (FoR)
  3 x 3 pixel arrays (FoV)
  3 bands covering 648.75-2551.25 cm-1
GSICS 03/2022: PowerPoint 演示文稿 (umd.edu)

## Slide 7: Agenda
Principal Component Analysis
Instrument: FY-3E / HIRAS-2
Noise Estimation
Anomaly Detection
Harmonisation Experiments
Conclusion

## Slide 8: Noise Estimation: Methodology
Eigenvalues of covariance matrix represent the variability of PC scores at the corresponding PC.
  Leading PCs contain most of the signal information, and lower PCs contain mostly random noise.
Noise can be estimated by truncating eigenvalues above a certain value at some threshold as:
Noise covariance is retrieved as:
Lee, Lu, et al. "HIRAS noise performance improvement based on principal component analysis." Applied Optics 58.20 (2019): 5506-5515.
Zavyalov, Vladimir, et al. "Noise performance of the CrIS instrument." Journal of Geophysical Research: Atmospheres 118.23 (2013): 13-108.

## Slide 9: Noise Estimates
Noise was estimated for various thresholds
  Little sensitivity to across a wide range
  Large lead to noise saturation
  is used for the following analysis.
The estimated noise is in good agreement with the stored values.

## Slide 10: Agenda
Principal Component Analysis
Instrument: FY-3E / HIRAS-2
Noise Estimation
Anomaly Detection
Harmonisation Experiments
Conclusion

## Slide 11: Anomaly Detection
By looking at PC scores, it may be possible to find small anomalies that cannot be noticed from the radiance.
If we look at lower PC scores…

## Slide 12: Anomaly Detection
By looking at PC scores, it may be possible to find small anomalies that cannot be noticed from the radiance.
If we look at lower PC scores…

## Slide 13: Anomaly Detection
By looking at PC scores, it may be possible to find small anomalies that cannot be noticed from the radiance.
If we look at lower PC scores…

## Slide 14: PC Scores per Pixel
Spatial distribution per pixel shows …
FoV 1
FoV 2
FoV 3
FoV 4
FoV 5
FoV 6
FoV 7
FoV 8
FoV 9

## Slide 15: PC Scores per Pixel
Spatial distribution per pixel shows anomalies like
  discontinuous distribution
  bias between pixels, etc..
FoV 1
FoV 2
FoV 3
FoV 4
FoV 5
FoV 6
FoV 7
FoV 8
FoV 9

## Slide 16: PC Scores per Pixel
Spatial distribution per pixel shows anomalies like
  discontinuous distribution
  bias between pixels, etc..
FoV 1
FoV 2
FoV 3
FoV 4
FoV 5
FoV 6
FoV 7
FoV 8
FoV 9

## Slide 17: Anomaly Detection
Pixel discrepancies are visible in the PCS averages per pixel.
* PCS averages are normalized by

## Slide 18: Agenda
Principal Component Analysis
Instrument: FY-3E / HIRAS-2
Noise Estimation
Anomaly Detection
Harmonisation Experiments
Conclusion

## Slide 19: Harmonisation Experiments
We would like to define a new set of PC that favours the directions common to all pixels to remove pixel-dependent instrumental defects.
PCA is performed on each pixel, and PCs obtained for each pixel are used to evaluate their commonality.
By adding the term of “pixel-commonality” to the covariance matrix, both SNR and commonality are maximised simultaneously.
In this study, samples are divided into 18 “pixels” according to 9 FoVs and 2 directions of the interferometer scanning.
Hultberg, T. et al. "Removal of instrument artefacts by harmonisation of hyperspectral sensor data from multiple detectors." Sensors, Systems, and Next-Generation Satellites XXI. Vol. 10423. SPIE, 2017.

## Slide 20: Alignment with Pixel PCs
Some of the standard PCs are poorly aligned with some pixel PCs.
The harmonised PCs are more aligned with pixel PCs.
Angle between k-th PC and PC per pixel
Standard PC
Harmonised PC

## Slide 21: Mitigation of Pixel-Dependent Defects
Bias between pixels as seen at #21 are mitigated in the Harmonised PC.
Noisy distribution at #15 is not removed but appears at lower PC of #20 in the Harmonised PC.
Standard PC
Harmonised PC

## Slide 22: Agenda
Principal Component Analysis
Instrument: FY-3E / HIRAS-2
Noise Estimation
Anomaly Detection
Harmonisation Experiments
Conclusion

## Slide 23: Conclusions
The noise of HIRAS-2 instrument was estimated by using PCA, a data driven method.
We confirmed that the distribution and statistics of PC scores can be used to detect instrument anomalies.
EUMETSAT will use such technics during the commissioning of Metop-SG IASI-NG and MTG-S IRS
The anomalies could be mitigated by harmonization method, which evaluates the SNR and pixel-commonality simultaneously.

## Slide 24
Thank you!
Questions are welcome.