## Slide 1
FY-4B GIIRS-2 / Metop-IASI
Inter-comparison
Pierre Dussarrat & Guillaume Deschamps
Remote Sensing Scientists
GSICS meeting – 13/03/2024

## Slide 2: Agenda
Introduction to GIIRS
Colocations with IASI
Radiometric calibration
Spectral calibration
Limbs

## Slide 3: FY-4B / GIIRS-2
https://space.oscar.wmo.int/instruments/view/giirs_2

## Slide 4: FY-4B / GIIRS-2
FY-4A / GIIRS-1
  Launch: 10/12/2016
  Geostationary at 104.7°E
FY-4B / GIIRS-2
  Launch: 02/06/2021
  Geostationary at 133.0°E
  Relocation to 105.0°E in 02/2024

## Slide 5: GIIRS Detector Matrix
Pixel matrix change:
  FY-4A: 32x4 pixels (16km)
  FY-4B: 16x8 pixels (12km)
FY4A
FY4B

## Slide 6: Agenda
Introduction to GIIRS
Colocations with IASI
Radiometric calibration
Spectral calibration
Limbs

## Slide 7: Colocation IASI - GIIRS
Colocations definitions with IASI flybys:
Colocation criteria | 
Distance | < 10 km
Time | < 10 min
Secant | < 0.01
Period | 01/10/2023  01/02/2024
Apodisation | Hamming
Temperature | < 2K < 3K
17142 spectra | 
Colocation criteria | 
 | < 10 km
 | < 10 min
 | < 0.01
Period | 01/10/2023  01/02/2024
Apodisation | Hamming
17142 spectra | 

## Slide 8: Agenda
Introduction to GIIRS
Colocations with IASI
Radiometric calibration
Spectral calibration
Limbs

## Slide 9: Radiometric calibration
GIIRS radiometric calibration assessment taking IASI and RT-model as references:
Long-wave IR:
  Cold bias for low wavenumbers, introduced by the processing update from June 2023, the scan mirror thermal radiation is now accounted improving the calibration stability but producing a bias !
  The bias remains function of the scanning angle mirrors and reversed after yaw flips at equinoxes. Believed to be related to a wrong angle dependency of the scanning mirror reflectivity in the calibration equation.
  Consistent with CMA results presented to EUM on 08/2023
Giirs 2 @680– Background [K]
(Chris Burrows / ECMWF)
01/2023
07/2023
Calibration is reversed after yaw flip (03/2023) !

## Slide 10: Radiometric calibration
GIIRS radiometric calibration assessment taking IASI and RT-model as references:
Mid-wave IR:
  Overall good calibration
  Large spikes up to 500mK, the spectral responses functions of the GIIRS channels seem highly distorted
  Believed to be related to a strong straylight contamination

## Slide 11: Radiometric calibration
Assessment of the radiometric gain by linear regression between GIIRS-2 and IASI radiances
Long-wave IR:
  Gain < 1
Mid-wave IR:
  Gain > 1
Believed to be related to some under and over-evaluation of the instrument transmissions in the calibration equation

## Slide 12: Agenda
Introduction to GIIRS
Colocations with IASI
Radiometric calibration
Spectral calibration
Limbs

## Slide 13: Spectral Calibration
GIIRS spectral calibration assessment taking IASI as reference:
Long-wave IR:
  Mostly inside the 10ppm requirement
  Strong checkerboard pattern
  Related to parasite and pixels-dependent clutter signals at interferogram level (CMA results presented on 08/2023)
Mid-wave IR:
  Mostly inside the 10ppm requirement
  Strong diamond shape
  Believed to be related to strong straylight contamination
  Consistent with CMA results presented to EUM on 08/2023
Spectral calibration per pixel [ppm]

## Slide 14: Principal Components Analysis
PCA allows decomposing the signal into independent components ordered by variability amplitude and detecting subtle defects:
PC#12 (LWIR) and #8 (MWIR) can be clearly associated to spectral calibration
These can be monitored outside of the colocation times with IASI to assess the temporal variability of the spectral calibration
See Shin Koyamatsu’ s talk
https://en.wikipedia.org/wiki/Principal_component_analysis
Hultberg, T. et al. "Local or global? How to choose the training set for principal component compression of hyperspectral satellite measurements: a hybrid approach." Sensors, Systems, and Next-Generation Satellites XXI. Vol. 10423. SPIE, 2017.

## Slide 15: Agenda
Introduction to GIIRS
Colocations with IASI
Radiometric calibration
Spectral calibration
Limbs

## Slide 16: Limbs (01/2023)
Use the limb views to assess:
  The background calibration (spectra in space should equal 0)
  Potential straylight effects
Great improvements with respect to FY-4A but patterns still visible in both bands.
Believed to be a hint of “flaring” in LWIR band: symmetrical ghosts produces by lens internal reflections.

## Slide 17: Conclusions
FY-4B GIIRS-2 data quality is certainly better than FY-4A GIIRS-1
  Nonetheless many anomalies remain:
    Electronic parasites (spectral calibration LWIR),
    Straylight (spectral and radiometric calibration MWIR),
    Calibration equation (LWIR and MWIR)
Analysing GIIRS data is a great rehearsal for the EUMETSAT teams
Most of EUMETSAT monitoring modules are ready for MTG-S IRS commissioning

## Slide 18
Thank you!
Questions are welcome.