## Slide 1: Revisit to AHI GEO-LEO-IR Regression
TAKAHASHI Masaya
Meteorological Satellite Center of Japan Meteorological Agency

## Slide 2: Contents
Motivation
Regression Methods
  Ordinary least squares (OLS) and reduced major axis (RMA)
  Comparison of OLS and RMA for AHI GEO-LEO-IR
Regression Targets
  GEO radiance/digital counts vs. LEO radiance
Discussion

## Slide 3: Motivation
Current GEO-LEO IR algorithm uses ordinary least squares (OLS) regression for LEO-radiance (X, reference instrument) and GEO-radiance (Y, monitored instrument).
  GEO radiance stdv within averaging LEO pixel size is used as weight in the regression.
  Reference is assumed to be perfectly calibrated.
  JMA’s VNIR vicarious calibration uses Reduced Major Axis (RMA) which considers uncertainties in both X and Y.
  Tested for AHI GEO-LEO-IR in 2018, but large difference between OLS and RMA was found particularly in 3.9 μm cold scenes.
Feedback from ISCCP in 2019 (by K. Knapp) and ISCCP-NG in 2023 (by A. Heidinger)
  Users have to convert BT to radiance, apply GSICS coefficients, and convert the radiance to BT.
  GSICS-corrected BT LUT in MTSAT-2 GEO-LEO-IR is easy to use.
We revisited the regression method and targets (and contents of GEO-LEO-IR) for discussing GEO-LEO-IR v2 algorithm.

## Slide 4
Radiance vs radiance regression
Himawari-8/AHI (3.9um, Tb < 230K) and Metop-A/IASI
LEO Radiance [mW/m2/sr/cm-1]
GEO - LEO
N = 578
January 2016
Kilmer and Rodriguez (2016)
a) Ordinary least squares (OLS)
  No error in X is assumed, minimizing distance is vertical
b) Reduced Major Axis (RMA)
  Errors in X and Y are assumed, minimizing distance is diagonal
Regression Methods
GEO Radiance [mW/m2/sr/cm-1]
OLS
RMA

## Slide 5
Old comparison prepared for 2018 GSICS Annual Meeting
Himawari-8/AHI B07 (3.9 μm) vs. Metop-A/IASI for Jan 2018
Upper figures: old comparison in 2018
  RMA result was not consistent with collocation data plots
Lower figures: new comparison using the latest algorithm (correction of negative radiance handling)
  RMA shows consistent result with OLS, and it has slightly smaller bias at cold scenes
  The reason is unclear, but the correction of data handling may reduce inconsistency of collocated radiance difference at cold and warm scenes
Comparison of OLS and RMA
LEO TB [K] LEO TB [K]
AHI TB - LEO TB [K
OLS
RMA
LEO TB [K] LEO TB [K]
AHI TB - LEO TB [K
OLS
RMA
New comparison using the latest GEO-LEO-IR algorithm
Himawari-9/AHI B07 (3.9 μm) vs. Metop-B/IASI for Feb 2023

## Slide 6
Himawari-9/AHI B10 (7.3 μm) TB Biases for Feb 2023
OLS
RMA
vs. Metop-B/IASI vs. Metop-C/IASI vs. Aqua/AIRS vs. NOAA-20/CrIS
 | @220 K | @250 K | @ 290 K
OLS | -0.77 to -0.62 K | -0.17 to -0.11 K | 0.13 to 0.16 K
RMA | -0.36 to -0.13 K | -0.10 to -0.03 K | 0.02 to 0.04 K
RMA result seems consistent with scatterplots especially at cold scenes
Regression method which accounts for uncertainties of X and Y could be a candidate for v2 algorithm

## Slide 7
JMA’s GEO-LEO IR inter-cal info
  MTSAT-2 Imager used JMA own implementation
    Coefficients from GEO digital counts (DC) to LEO radiance in wavenumber [mW m-2 sr-1(cm-1)-1]
    LUT from GEO digital counts to LEO TB [K] (optional)
  Himawari-8/-9 AHI adopts GSICS standard
    Coefficients from GEO radiance to LEO radiance in wnum
How to get inter-calibrated AHI rad/TB from GSICS standard info
  JMA GEO radiance is based on wavelength [W m-2 sr-1 μm-1], not wnum
  Users have to take the following long process…
    Read GEO digital count from AHI L1b (Himawari Standard Data)
    Convert DC to radiance in wlen using coefficients in the L1b
    Convert radiance in wlen => TB => radiance in wnum
    Apply GSICS inter-calibration info to derive LEO radiance in wnum
    Convert LEO radiance in wnum => TB => radiance in wlen
GEO DC
GEO TB [K]
GEO rad
[WN]
LEO rad
[WN]
LEO TB [K]
LEO rad
[WL]
GSICS Inter-cal
(standard info)
GEO rad
[WL]
Regression Targets
In the case of MTSAT-2, LEO rad [WN] is directly derived from GEO DC.

## Slide 8
GEO DC
GEO TB [K]
GEO rad
[WN]
LEO rad
[WN]
LEO TB [K]
LEO rad
[WL]
GSICS Inter-cal
(standard info)
GEO rad
[WL]
The Way Forward
Feedback from ISCCP (2019) and ISCCP-NG (2023)
  Calibration table for GSICS inter-calibration is easy to use
  However, it is not practically possible for RAC due to its file size
  Having GEO DC vs. LEO rad [wnum or wlen] could be a solution for reducing process for users to derive inter-calibrated radiance/TB
(Knapp, 2019)

## Slide 9
Discussion
Regression method
  What is an appropriate regression method for IR inter-calibration?
    Current GEO-LEO-IR approach: ordinary least squares (OLS) with weighting?
    Reduced major axis (RMA)?
    Other methods (incl. linear/polynomial regression equation)?
  Regression target
  Current GEO-LEO-IR (GEO rad vs. LEO rad in wavenumber) requires users to take lots of steps for getting inter-calibrated GEO radiance.
    In particular for GEO radiance in wavelength unit
  Does anyone really needs alternative regression target (e.g., GEO DC vs. LEO rad)?
    Alternatively, some APIs could cover the messy conversion role :)

## Slide 10
Thanks for your attention!