## Slide 1
Kyunghwa Lee, Jaehoon Jeong, Jeonghyeon Seo, Mijeong Kim, Dongwon Lee
Current Status of Geostationary Environment Monitoring Spectrometer (GEMS)
2024 Global Space-based Inter-Calibration System (GSICS) Annual Meeting
Environmental Satellite Center (ESC)
National Institute of Environmental Research (NIER)
Myoung-Hwan Ahn, Mina Kang, Mijin Eo, Yeeun Lee
Climate and Energy Systems Engineering/Social Economy
Ewha Womans University

## Slide 2
Introduction of GEMS
Launch of the first UV-visible geostationary hyperspectral imager : 18 FEB 2020

## Slide 3
Data processing (L0-L4) & analyzing
Validation
Data back-up & archiving
Receiving
Distribution
Monitoring
Universities
Institutes
Public service
(http://nesc.nier.go.kr)
Air Quality Forecasting Center
Roles of National Institute of Environmental Research (NIER) for the GEMS operation
Oct. 2020
IN-Orbit Test (IOT)
Distribution of image files
8 Mar. 2020
LEOP
Now
19 Feb. 2020
Launch
L2 production / Validation
Mar. 2021
Jun., Nov., 2022
Distribution of NC files
ESC
Introduction of ESC

## Slide 4
Month | 07:45 | 08:45 | 09:45 | 10:45 | 11:45 | 12:45 | 13:45 | 14:45 | 15:45 | 16:45 | #
1 | - | - | HE | HK | FC | FW | FW | FW | - | - | 6
2 | - | - | HE | HK | FC | FW | FW | FW | FW | - | 7
3 | - | HE | HK | FC | FC | FW | FW | FW | FW | - | 8
4 | HE | HK | FC | FC | FC | FW | FW | FW | FW | FW | 10
5 | HE | HK | FC | FC | FW | FW | FW | FW | FW | FW | 10
6 | HE | HK | FC | FC | FW | FW | FW | FW | FW | FW | 10
7 | HE | HK | FC | FC | FW | FW | FW | FW | FW | FW | 10
8 | HE | HK | FC | FC | FW | FW | FW | FW | FW | FW | 10
9 | HE | HK | FC | FC | FW | FW | FW | FW | FW | FW | 10
10 | - | HE | HK | FC | FC | FW | FW | FW | FW | - | 8
11 | - | - | HE | HK | FC | FW | FW | FW | - | - | 6
12 | - | - | HE | HK | FC | FW | FW | FW | - | - | 6
Half Korea
(HK)
Full West
(FW)
Half East
(HE)
Full Central
(FC)
Month | 07:45 | 08:45 | 09:45 | 10:45 | 11:45 | 12:45 | 13:45 | 14:45 | 15:45 | 16:45 | #
1 | - | - | FC | FC | FC | FC | FW | FW | FW | - | 7
2 | - | HE | FC | FC | FC | FC | FW | FW | FW | - | 8
3 | - | HE | FC | FC | FC | FC | FW | FW | FW | - | 8
4 | HE | HK | FC | FC | FC | FC | FW | FW | FW | FW | 10
5 | HE | HK | FC | FC | FC | FC | FW | FW | FW | FW | 10
6 | - | HK | FC | FC | FC | FC | FW | FW | FW | FW | 9
7 | - | HK | FC | FC | FC | FC | FW | FW | FW | FW | 9
8 | - | HK | FC | FC | FC | FC | FW | FW | FW | FW | 9
9 | - | HK | FC | FC | FC | FC | FW | FW | FW | FW | 9
10 | - | HE | FC | FC | FC | FC | FW | FW | FW | - | 8
11 | - | HE | FC | FC | FC | FC | FW | FW | FW | - | 8
12 | - | - | FC | FC | FC | FC | FW | FW | - | - | 6
Reschedule of GEMS observation since 1 FEB 2024
+
-
Change
Current status of GEMS

## Slide 5
Monitoring and maintaining calibration
Observation |  | Frequency | Time | Comments
Earth |  | Avg. 8/day | HH:45min~HH+1hr:15min (duration: 30min) | CMA position: Open Schedule considering SKM, WOL
Solar | WSD | 1/day | Perform before/after local midnight at a sun-diffuser normal angle of 30.5° | CMA position: WD or RD Reschedule after midnight (16-17 UTC) if SKM is overlapped on regular observation time (13-14UTC)
 | RSD | 2/year |  | 
Dark | Normal | 2/day (180 images) | Right before/after daytime Earth observation | CMA position: Close Normal: Additional observation after SKM, WOL
 | Solar | 1/day (2 images) | Right before solar observation | 
 | LED | 1/week (42 images) | Right after LED observation | 
LED |  | 1/week (17 UTC on Sunday) | After dark imaging and prior to solar calibration | CMA position: Close Observations at multiple integration times
Thermally-Controlled Composite Structure
Radiator Assembly
Aperture
Calibration Mechanism Assembly
Scene Selection Wheel
Image credit: Ball
Transmissive
Diffusers
Current status of GEMS
WSD: Working solar diffuser
RSD: Reference solar diffuser
CMA: Calibration mechanism assembly
LED: Light emitting diode
CCD: Charge-coupled device (a light-sensitive integrated circuit)

## Slide 6
L1 production processes
< Solar Scene >
< Earth Scene>
L0 Input
Co-addition Correction
Pixel Flagging
Crosstalk Correction
Nyquist phase Correction
Electronic Offset Correction
Smear Correction
Linearity Correction
Gain Correction
PRNU Correction
Integration time Correction
Dark Correction
Geometric Calibration
Radiance Calibration
Stray Light Correction
Spectral Shift Correction
Diffuser BTDF Correction
Spectral Shift Correction
Done
Irradiance Calibration
L1A Output
L1A Output
Proceeding
2-Pixel Binning
Spatial Registration
L1B Output
2-Pixel Binning
Spatial Registration
L1B Output
Current status of GEMS

## Slide 7
Monitoring long-term GEMS data
Courtesy: BATC
Common
☯ Dark current
Current status of GEMS
The pixel-averaged dark current has increased approximately 7.63% for 3.5 years (or 0.005 % per a day)
The half width has increased by about 9.4 %

## Slide 8
Current status of GEMS
Monitoring long-term GEMS data
☯ Bad pixel
☯ Non-linearity
Hot pixel threshold
Hot pixels are continuously increasing with an e-folding time of about 21 years
Cold pixels are consistently maintained
Signal drift is about 0.04 %, caused by the instability of the LED lamp
Time series variance is less than 0.2 % (@CCD full well capacity, 5-95 %)

## Slide 9
Current status of GEMS
Monitoring long-term GEMS data
☯ Working solar diffuser (WSD) and reference solar diffuser (RSD)
WSD
RSD
1,201 times of exposure
10 times of exposure
Degradation of the diffuser and throughput occurs as observation time increases

## Slide 10
Monitoring long-term GEMS data
☯ WSD (APR 2020 – JAN 2024)
N, 300nm
S, 500nm
Current status of GEMS

## Slide 11
Current status of GEMS
Monitoring long-term GEMS data
☯ Integrated signals over whole CCD for solar irradiance
WSD
RSD
WSD
RSD

## Slide 12
Current status of GEMS
Monitoring long-term GEMS data
☯ Telemetry
Seasonal & stable variability meets requirements
Variability of CCD temperature is < 0.3 °C
Focal plane electronics (FPE) temperature meets the criteria of -35°C to 50°C, but it has gradually increased

## Slide 13
Current status of GEMS
Inter-comparison between GEMS and the Advanced Meteorological Imager (AMI)
☯ Spatiotemporal collocation
Temporal collocation: Using AMI data -10, 0, + 10 min from GEMS observation time
Spatial collocation: AMI 1 km by 1 km → 3.5 km by 8 km (to GEMS domain)

## Slide 14
Current status of GEMS
☯ Spectral collocation
Collocation of GEMS data using AMI SRF to compare with AMI VIR004 band (central wavelength at 470 nm)
Inter-comparison between GEMS and AMI

## Slide 15
Current status of GEMS
☯ Cloud effect removal
Comparison by considering clear pixels using cloud mask
Inter-comparison between GEMS and AMI
Collocated AMI cloud
Collocated radiance diff. w/ cloud
Collocated radiance diff. w/o cloud
2023.01.01 02:45
2023.01.01 02:45 GEMS - AMI
2023.01.01 02:45 GEMS - AMI

## Slide 16
Current status of GEMS
☯ Geometric difference
Almost 1-2 pixels difference in RMSE analysis
Sometimes, reversal trend after rebooting GEMS
Inter-comparison between GEMS and AMI
w/o cloud mask
2023.01.04
2023.01.04
w/o cloud mask
w/ cloud mask
w/ cloud mask
2023.07.17
2023.07.17
N-S
N-S
E-W
E-W
N-S
N-S
E-W
E-W

## Slide 17
2023-12-10
2023-12-10
2023.09.24
2023.09.24
Current status of GEMS
☯ Geometric difference
Almost 1-2 pixels difference in RMSE analysis
Sometimes, reversal trend after rebooting GEMS
Inter-comparison between GEMS and AMI
N-S
N-S
E-W
E-W
N-S
N-S
E-W
E-W
w/o cloud mask
w/o cloud mask
w/ cloud mask
w/ cloud mask

## Slide 18
Current status of GEMS
☯ Radiometric difference
Dramatic change in correlation coefficient and bias after rebooting GEMS
Inter-comparison between GEMS and AMI
2023.01.04
2023.07.17
2023.09.24
2023.12.10
w/ cloud mask

## Slide 19
Current status of GEMS
On-going/future work
☯ Bidirectional transmission distribution function (BTDF) update for mitigating diffuser degradation
GEMS irradiance trend ratio before updating BTDF
500 nm
300 nm
North
Nadir
South
*Relative FGEMS : normalized to FGEMS_Apr. 23 2020
Spatial index: 50
Spatial index: 1,050
Spatial index: 1,950

## Slide 20
Current status of GEMS
On-going/future work
☯ BTDF update for mitigating diffuser degradation
GEMS irradiance trend ratio after updating BTDF
500 nm
300 nm
North
Nadir
South
*Relative FGEMS : normalized to FGEMS_Apr. 23 2020
Spatial index: 50
Spatial index: 1,050
Spatial index: 1,950

## Slide 21
Current status of GEMS
On-going/future work
☯ Stray light correction
Considering ghost signals → bout a 10% reduction in the leftover stray light
Update the stray light distribution matrix using a point spread function (PSF) factor of 1.2
Ghost update
PSF factor (1.2) + Ghost update
☯ Developing an operational system for the inter-comparison between GEMS and other satellites to enhance the precision and reliability of GEMS data.

## Slide 22
Thank you for your attention.
2024 Global Space-based Inter-Calibration System (GSICS)