## Slide 1: Validation of TSIS-1 HSRS in the range 300 nm to 1700 nm using ground-based SI-traceable spectral solar irradiance measurements
Julian Gröbner1, Gregor Hülsen1, Saulius Nevas2, and Peter Sperfeld2.
1Physikalisch-Meteorologisches Observatorium Davos und World Radiation Center (PMOD/WRC), Davos Dorf, Switzerland
2Physikalisch-technische Bundesanstalt (PTB), Braunschweig, Germany.
This work has been supported by the European Metrology Program for Innovation and Research (EMPIR) within the joint research project EMPIR 19ENV04 MAPP “Metrology for aerosol optical properties”. The EMPIR is jointly funded by the EMPIR participating countries within EURAMET and the European Union.

## Slide 2: How to get the Top of Atmosphere solar spectrum from ground-based direct solar irradiance measurements?
The Beer-Lambert law
The langley-plot
The optical depth τ is assumed constant during this period (half-day)
logI0
Spectral solar irradiance, 13 September 2022
The retrieved I0(l) represent the solar spectrum at the top of the atmosphere and can be compared to space-based measurements from satellites (in certain spectral bands).
The QASUMEFTS solar spectrum (300 nm to 500 nm):
Gröbner et al., AMT, 2017.

## Slide 3: The QASUMEFTS solar spectrum
Derived from ground-based spectral solar measurements at Izana in September 2016.
Using a high resolution FTS and a double-monochromator spectroradiometer.
Spectral range 300 nm to 500 nm.
Expanded relative uncertainties of 2%.
Published Gröbner et al., AMT, 2017.
Thuillier et al., 2003
Harder et al., 2010
Hilbig et al., 2017
Meftah et al., 2016
SOLAR_ISS
Comparison to ToA solar spectra:

## Slide 4: TSIS-1 Hybrid Solar Reference Spectrum (HSRS)
Coddington et al., 2021 (V1.0), 2023 (V2.0)
TSIS-1 on the ISS
QASUMEFTS was used to produce TSIS-1 HSRS:

## Slide 5: Spectral solar irradiance measurements at the pristine high altitude station Izaña, Tenerife, Canary Islands, Spain
QASUME (direct)
7-22 September 2022
~14 clear sky half days
Campaign objectives:
Retrieve Top-of-Atmosphere solar spectra from SI-traceable solar irradiance measurements in the range 300 nm to 1700 nm.
Validate the space-based solar spectrum TSIS-1 HSRS.

## Slide 6: Spectral irradiance measurements are traceable to the primary spectral irradiance standard of PTB
Tuneable Laser facility TULIP
High temperature blackbody
BB3200pg
QASUME transfer standards
QASUME
Portable calibrator with low power lamps

## Slide 7: Spectral irradiance measurements are traceable to the primary spectral irradiance standard of PTB
BB3200pg
TULIP
QASUME transfer uncertainty U95=1.3%
Tuneable Laser facility TULIP
High temperature blackbody
BB3200pg

## Slide 8: Spectral irradiance measurements are traceable to the primary spectral irradiance standard of PTB
Spectral irradiance comparison between TULIP and BB3200pg
Shown are expanded relative measurement uncertainties (k=2).
Gray shaded area: QASUME (< 550 nm)/ QASUME-IR at BB3200pg.
Error bars : QASUME (< 550 nm)/ QASUME-IR at TULIP.
The ambient water vapour variability increased the measurement uncertainty of QASUME-IR between 1360 nm and 1650 nm (estimated).

## Slide 9: Top of the Atmosphere solar spectra from QASUME & QASUME-IR using Langley-plots
QASUME (direct)
±1%
14 half days
QASUME
QASUME-IR
Water vapour absorption

## Slide 10: Top of Atmosphere solar spectra using Langley plots
Water vapour absorption
Relative standard error of the retrieved ToA solar spectrum ~0.1%

## Slide 11: Validation of TSIS-1 HSRS with ground based solar irradiance measurements
Agreement with TSIS-HSRS: 1% outside of strong atmospheric absorption bands
U95QASUME=1.6%

## Slide 12: Uncertainties of Top of Atmosphere solar spectra QASUME & TSIS-1 HSRS
At wavelengths shorter than 400 nm, the relative uncertainty of QASUME is 0.8% and therefore lower than the one of TSIS-1 HSRS.

## Slide 13: Conclusions
The Top of Atmosphere solar spectrum TSIS-1 HSRS was validated with ground based measurements within 0.8% standard relative uncertainties.
In the range 310 nm to 400 nm the uncertainty of the TSIS-1 HSRS solar spectrum could be reduced from 1.3% to 0.8%, based on the QASUME measurements.
Published Gröbner et al., AMT, 2023.