## Slide 1
Vis/NIR breakout session — lunar part
Typically this part includes presentations on lunar calibration results for GSICS instruments
Dave Smith from RAL reported on Moon observations with Sentinel 3A and 3B SLSTR and comparisons to the GIRO
  Dave’s Moon image processing technique prompted a discussion of size-of-source effects and the impact on using an irradiance source (the Moon) for calibration
Tom Stone initiated an open discussion on issues related to lunar irradiance measurements from instruments and comparisons to lunar models
motivated by Hugh Kieffer’s lunar modeling work, which shows large differences between instruments that are not seen with vicarious techniques using ground targets
the cause must be related to processing Moon images into irradiance measurements, or evaluating the out-of-field spatial response of each pixel, i.e. size-of-source effects
  Hugh suggested a pixel spatial evaluation method that gives lunar irradiance values
Tom stressed the need for high-accuracy lunar measurements to set the absolute scale for lunar references (models)
  current active projects include air-LUSI (deployment this week), MLO-LUSI (to start operating later this year) and ARCSTONE (CubeSat, to launch in ~2 years), others?

## Slide 2
Vis/NIR breakout session — lunar part
Sebastien Wagner presented on GSICS lunar calibration activities at EUMETSAT
main topic: planning for the next (4th) GSICS lunar calibration workshop
  list of workshop topics includes:
    evaluating the lunar irradiance from Moon images
    the dispersion of instruments’ measurements when compared against the same lunar reference/model
    the GSICS lunar model inter-comparison exercise
    use of the Moon in the IR and microwave regions
    alternative uses of Moon imagery, e.g. MTF, stray light, band co-registration
  EUMETSAT has planned to host in Darmstadt
  timeframe discussed, agreed November or December 2023
Potential actions:
revive lunar model inter-comparison exercise and report results at 2023 annual meeting
Vis/NIR webmeeting lunar talks:
Hugh Kieffer to present his pixel spatial evaluation concept
Seb Wagner to present Sentinel 3 OLCI and SLSTR lunar calibrations