## Slide 1
Paul Poli, Timo Hanschmann, Viju John, Joerg Schulz (EUMETSAT)

## Slide 2: SSM/T-2 instrument
Mounted on
3 block 5D-2 satellites (F11, F12, F14) and
the 1st block 5D-3 satellite (F15)
First instrument to routinely observe the 183 GHz band (3 channels: 183.31 GHz ± 1, ± 3, ± 7 GHz)
“Reference article” for this instrument: I. Galin, D.H. Brest, and G.R. Martner, 1993: DMSP SSM/T-2 microwave water vapor profiler, Proc. SPIE 1935, Microwave Instrumentation for Remote Sensing of the Earth. doi: 10.1117/12.152603.

## Slide 3: SSM/T-2 FDR Release 2
Heritage
SSM/T-2 from FIDUCEO project
Difference with respect to previous release
Collocation with CM-SAF HOAPS 4.0 SSM/I retrievals over ice-free oceans, and aggregation of matching retrievals
Flagging of scenes believed to be affected by rain/cloud contamination, where HOAPS rain rate or total water path exceed thresholds
Flagging of scan positions affected by glare obstruction bracket (GLOB)
Output product: FDR Release 2
  Includes all the information above
doi:10.15770/EUM_SEC_CLM_0050
doi:10.15770/EUM_SEC_CLM_0046
doi:10.5676/EUM_SAF_CM/HOAPS/V002

## Slide 4: SSM/T-2 Uncertainties
FIDUCEO total uncertainty (K)
ERA-Interim
ERA5
DMSP F11
DMSP F12
DMSP F14
DMSP F15
SSM/T-2 channel 183 ± 7 GHz (lower tropospheric humidity)
Std. dev. of differences between FCDR and radiative transfer simulations (K)
3 components of uncertainty: independent, structured, common

## Slide 5: Mean differences with ERA5
183.31 ± 1.00 GHz ~Upper-Tropos. Hum.
183.31 ± 3.00 GHz ~Mid-Tropos. Hum.
183.31 ± 7.00 GHz ~Lower-Tropos. Hum.
P
E
Fig. 23 excerpt from Hersbach et al. (2020, doi:10.1002/qj.3803)
mm/day
SSM/T-2 F12
SSM/T-2 F14
SSM/T-2 F15
~ 0
AMSU-B NOAA-16
SSM/T-2 F11
AMSU-B NOAA-17
② ERA5 observation data assimilation feedback, for AMSU-B data actively assimilated in ERA5
① [SSM/T-2 FCDR] minus [clear-sky radiative transfer simulations (running NWP-SAF RADSIM & RTTOV, using ERA5 atmospheric profiles) for scenes believed to be clear of cloud/rain effects, after removing noisy events based on FIDUCEO total uncertainty]
①
②

## Slide 6
Thanks for your attention!

## Slide 7: Std. dev. differences with ERA5
183.31 ± 1.00 GHz ~Upper-Tropos. Hum.
183.31 ± 3.00 GHz ~Mid-Tropos. Hum.
183.31 ± 7.00 GHz ~Lower-Tropos. Hum.
SSM/T-2 F12
SSM/T-2 F14
SSM/T-2 F15
AMSU-B NOAA-16
SSM/T-2 F11
AMSU-B NOAA-17
①
②
② ERA5 observation data assimilation feedback, for AMSU-B data actively assimilated in ERA5
① [SSM/T-2 FCDR] minus [clear-sky radiative transfer simulations (running NWP-SAF RADSIM & RTTOV, using ERA5 atmospheric profiles) for scenes believed to be clear of cloud/rain effects, after removing noisy events based on FIDUCEO total uncertainty]