## Slide 1: Validation using Ray-matching and DCC with VIIRSs through parallel observation of Himawari-8,9
KODERA Kazuki and OKUYAMA Arata
Meteorological Satellite Center of
Japan Meteorological Agency

## Slide 2: Introduction
Himawari-9/AHI started to observe as operational satellite on 13th December 2022.
Although AHI onboard Himawari-9 has the same observation function as that onboard Himawari-8, there are slight differences due to sensors individual variability.
  E.g.) Center wavelength and shape of SRFs
Before the switchover, parallel observation of Himawari-8,9/AHI was performed. (27th Sep. to 13th Dec. 2022)
  Validations for the difference between AHI8 and AHI9 by Ray-matching and DCC methods.
VNIR

## Slide 3: Outline
Ray-matching method
  Outline of implementation in JMA
  Validation results for AHI8 and AHI9
DCC method
  Outline of test implementation in JMA
  Validation results for AHI8 and AHI9
Comparing Ray-matching and DCC methods on AHI9 biases validation
  Comparison with the direct comparison(GEO-GEO approach) : AHI9 vs. AHI8
The validation of AHI sensor sensitivity trends

## Slide 4: Outline of Ray-matching method in JMA
Input data
SNPP or N20
VIIRS SDR
Himawari-8/9 AHI data
(2 km resolution)
Collocations
data filtering
Pass
Himawari-8/9 AHI | Band01 (0.47 μm) | Band02 (0.51 μm) | Band03 (0.64 μm) | Band04 (0.86 μm) | Band05 (1.6 μm) | Band06 (2.3 μm)
SNPP or N20 VIIRS | M3 (0.49 μm) |  | I1 (0.64 μm) | M7 (0.87 μm) | M10 (1.6 μm) | M11 (2.3 μm)
Observation time difference | < 5 min.
Satellite zenith angle difference | < 10 deg.
Satellite azimuth angle difference | < 10 deg.
Sun glint angle (AHI only) | > 25 deg.
Brightness temperature @ 10.4 μm (AHI only) | < 273.15 K
STDV of reflectance/Mean of reflectance | < 5%
SBAFs
Using NASA SBAF Tool (B01-05) and calculating radiative transfer model (B06)
Collocating
Apply SBAFs
Himawari-8/9 data is not corrected by solar diffuser on real-time basis
VIIRS data is downloaded from NOAA CLASS server.
Outcomes
Details of our implementation is shown on back-up slides.

## Slide 5: Validation results by Ray-matching method
Scatter plot variation and number of collocations of AHI9 are similar to those of AHI8.
The differences between AHI9 and AHI8 are in ~5%. (except B05)
In both AHIs, the differences against N20 and SNPP are in ~2%.
Moyer et al. (2021) indicates that ~2% bias exists between SNPP and N20 in all reflective solar bands.
  These ray-matching results are good agreement with this reference.
AHI biases against references in Oct.2022 | AHI9 |  | AHI8 | 
 | Vs. N20 | Vs. SNPP | Vs. N20 | Vs. SNPP
B01 (0.47 μm) | 2.9% | 1.0% | -1.5% | -3.5%
B02 (0.51 μm) | 1.5% | 0.0% | 1.1% | -0.6%
B03 (0.64 μm) | -1.1% | -3.4% | 1.0% | -1.3%
B04 (0.86 μm) | 0.5% | -2.8% | 0.9% | -2.5%
B05 (1.6 μm) | 2.5% | -0.8% | 8.9% | 5.5%
B06 (2.3 μm) | -5.1% | -7.2% | -3.5% | -5.7%
AHI9 vs.N20
AHI9 vs.SNPP
AHI8 vs.SNPP
AHI8 vs.N20
B03 (0.64um) of AHIs

## Slide 6: Outline
Ray-matching method
  Outline of implementation in JMA
  Validation results for AHI8 and AHI9
DCC method
  Outline of test implementation in JMA
  Validation results for AHI8 and AHI9
Comparing Ray-matching and DCC methods on AHI9 biases validation
  Comparison with the direct comparison(GEO-GEO approach) : AHI9 vs. AHI8
The validation of AHI sensor sensitivity trends

## Slide 7: Test implementation outline of DCC method in JMA
Input data
SNPP or N20
VIIRS SDR
Himawari-8/9 AHI data
(2 km resolution)
Input data is the same as Ray-matching method.
data filtering to get DCC pixels
Select DCC
Region of selecting DCC | 20S.~20N. and 120E.~160E.
BT | < 206.8 K
Satellite zenith angle | < 40 deg.
Sun zenith angle | < 40 deg.
Relative azimuth angle | 10 < RAA < 170 deg.
STDV of IR(VNIR) /Mean of IR(VNIR) | < 3%
Apply Hu model
Calculation
Comparison with
each mode (in B01-B04) or mean (in B05-B06)
* Deseasonalization is NOT applied yet in this test implementation.
N20 reference value *1
AHI
mode/mean value
VIIRS
Mode/mean value
Hu model
SBAFs
Bin sizes for AHI bands |  | Bin sizes for VIIRS bands | 
B01 | 1.70 | M3 | 1.06
B02 | 2.60 |  | 
B03 | 1.79 | I1 | 2.04
B04 | 1.37 | M7 | 0.50
B05 | 0.086 | M10 | 0.050
B06 | 0.030 | M11 | 0.041
VIIRS radiance value for 140E *1 | 
M3 | 570.81 (mode)
I1 | 439.89 (mode)
M7 | 267.57 (mode)
M10 | 17.87(mean)
M11 | 8.67(mean)
Bin sizes are tentative and come from approximately 0.3% of the mean values.
*1: In here, N20 reference value means the reference DCC radiances of N20/VIIRS calculated for each GEO domain suggested by Raj at the past GSICS VNIR monthly meeting. These values (right bottom table) refer to Raj’s following presentation.
Reference http://gsics.atmos.umd.edu/pub/Development/20210610/DCC_ATBD_June_10_2021.pdf
http://gsics.atmos.umd.edu/pub/Development/20230112/Bhatt_VIIRS_DCC_reference4GEOsV1.pdf
AHI value vs. N20 reference value*1
  AHI / N20_ref. *SBAF
AHI value vs. N20 observation derived from SDR
  AHI / N20_sdr *SBAF
AHI value vs. SNPP observation derived from SDR
  AHI / SNPP_sdr *SBAF

## Slide 8: Validation results by DCC method
AHI9’s PDFs are smooth as similar to AHI8’s.
Time series are stable but AHI9’s plots seem to have slight larger variation than AHI8’s.
The differences between AHI9 and AHI8 are in ~5%. But in B01, it seems that AHI9 has slight large bias against N20.
B03 (0.64um) of AHI9
AHI biases against references in Oct.2022 | AHI9 |  |  | AHI8 |  | 
 | Vs. N20_ref. | Vs. N20_sdr | Vs. SNPP_sdr | Vs. N20_ref. | Vs. N20_sdr | Vs. SNPP_sdr
B01(0.47 μm) | 6.2% | 7.1% | 2.0% | 1.0% | 1.8% | -2.9%
B02(0.51 μm) | -0.9% | -0.1% | -4.7% | -1.8% | -1.0% | -5.6%
B03(0.64 μm) | 3.1% | 4.6% | -2.5% | 4.8% | 6.2% | -1.0%
B04(0.86 μm) | 4.2% | 5.3% | -0.9% | 4.2% | 5.3% | -0.9%
B05 (1.6 μm) | -6.2% | -1.6% | -4.3% | -1.0% | 3.8% | 1.2%
B06 (2.3 μm) | -12.7% | -8.0% | -8.5% | -11.2% | -6.4% | -6.9%
Mode radiance (W/m^2/sr/um)
Mode radiance (W/m^2/sr/um)
Re-analysis period(+/- 14days)
Daily period (1day)
Re-analysis period(+/- 14days)
Daily period (1day)
Tuning period
Jul. Aug. Sep. Oct. Nov. Dec.
2022
B03 (0.64um) of AHI8
Jul. Aug. Sep. Oct. Nov. Dec.
2022

## Slide 9: Outline
Ray-matching method
  Outline of implementation in JMA
  Validation results for AHI8 and AHI9
DCC method
  Outline of test implementation in JMA
  Validation results for AHI8 and AHI9
Comparing Ray-matching and DCC methods on AHI9 biases validation
  Comparison with the direct comparison(GEO-GEO approach) : AHI9 vs. AHI8
The validation of AHI sensor sensitivity trends

## Slide 10: Comparison by Ray-matching and DCC methods
Chart: 
 | 0.028856 | 0.014922 | -0.011335 | 0.0048185 | 0.024815 | -0.050998
 | 0.062154 | -0.0088639 | 0.031338 | 0.042088 | -0.075056 | -0.12693
 | 0.070983 | -0.00062443 | 0.045755 | 0.053438 | -0.01648 | -0.080228
Chart: 
 | 0.045051 | 0.0043254 | -0.020888 | -0.0038469 | -0.058691 | -0.016781
 | 0.046271 | 0.0062245 | -0.021249 | -0.0026447 | -0.059287 | -0.016089
 | 0.051799 | 0.0096386 | -0.015595 | 0 | -0.052616 | -0.017202
 | 0.051799 | 0.0096386 | -0.015595 | 0 | -0.052616 | -0.017202
 | 0.05077 | 0.0096386 | -0.015595 | 0 | -0.053598 | -0.017188
AHI9 is darker
Differences between Ray-matching and DCC methods are within about 5% except NIR bands(B05 and B06).
In the point of differences between AHI9 and AHI8, Ray-matching and DCC methods are good agreement. (<1%)
However, the AHI9 biases validated by DCC method are larger than those by Ray-matching method.
  These may indicate there is room of improvement in our DCC test implementation.
In VIS bands, DCC with N20_ref. results are better agreement with ray-matching results than DCC with N20_sdr. On the other hand, in NIR bands, DCC with N20_sdr seems to be better.
AHI9 biases against N20
AHI9 biases against AHI8
In Oct,2022
AHI9 is Brighter
AHI9 is darker
AHI9 is Brighter

## Slide 11: GEO-GEO approach : AHI9 vs. AHI8
GEO-GEO approach
  AHI9 minas AHI8 reflectance for each pixel under the conditions: same time and position
  Not considering the difference of SRFs. But in VNIR band, AHI9 SRFs are almost same as AHI8 SRFs (SBAFs~1) except B05.
  These results are able to be regarded as the differences of AHI9 and AHI8 except B05.
B01 (0.47um)
B02 (0.51um)
B03 (0.64um)
B04 (0.86um)
Large daily variation is not seen.
In B01, AHI9 is 3~5% brighter than AHI8 in particularly around bright clouds like DCC.
In B03, AHI9 is 2~3% darker than AHI8. B02, B04 and B06 have small differences(within ~1%)
These results are good agreement with the Ray-matching and DCC validations.
B05 (1.6um)
B06(2.3um)
Chart: 
 | 0.045051 | 0.0043254 | -0.020888 | -0.0038469 | -0.058691 | -0.016781
 | 0.046271 | 0.0062245 | -0.021249 | -0.0026447 | -0.059287 | -0.016089
 | 0.051799 | 0.0096386 | -0.015595 | 0 | -0.052616 | -0.017202
 | 0.051799 | 0.0096386 | -0.015595 | 0 | -0.052616 | -0.017202
 | 0.05077 | 0.0096386 | -0.015595 | 0 | -0.053598 | -0.017188
Double difference AHI9-AHI8 by GSICS methods
(1day loop on Oct. 1st,2022)
( in Oct.,2022)
AHI9 bias against AHI8

## Slide 12: Outline
Ray-matching method
  Outline of implementation in JMA
  Validation results for AHI8 and AHI9
DCC method
  Outline of test implementation in JMA
  Validation results for AHI8 and AHI9
Comparing Ray-matching and DCC methods on AHI9 biases validation
  Comparison with the direct comparison(GEO-GEO approach) : AHI9 vs. AHI8
The validation of AHI sensor sensitivity trends

## Slide 13: AHI sensor sensitivity trends
Health Check
Parallel Obs.
AHI9 DCC: -0.61%/yr (±0.09%)
AHI9 Ray-matching: -0.65%/yr (±0.07%)
AHI8 DCC: -0.52%/yr (±0.05%)
AHI8 Ray-matching: -0.62%/yr (±0.02%)
B03 (0.64um) against SNPP
DCC method has larger variations than Ray-matching method.
The trends of AHI9 are good agreement with these of AHI8. (<0.1%/yr)
  Although AHI9 had been in standby operation and AHI9 hadn't observed (except health check) until Dec. 2022, it seems that the sensor sensitivity of AHI9 has changed as well as that of operational AHI8.
  AHI9 data is limited yet (only a few months since operational start). After getting enough data, more investigation are needed.
AHI9 DCC: -0.61%/yr (±0.17%)
AHI9 Ray-matching: NA
AHI8 DCC: -0.50%/yr (±0.06%)
AHI8 Ray-matching: -0.59%/yr (±0.03%)
Jan May Sep Jan May Sep Jan May Sep Jan May Sep Jan May Sep Jan May Sep
2017 2018 2019 2020 2021 2022
* No collocations for AHI9 Ray-matching with N20 during past HC periods
Jan May Sep Jan May Sep Jan May Sep Jan May Sep Jan May Sep Jan May Sep
2017 2018 2019 2020 2021 2022
B03 (0.64um) against N20

## Slide 14: Summary and future works
Summary
JMA’s operational satellite was switched over to Himawari-9 from Himawari-8 on 13th Dec. 2022.
For operational start of Himawari-9, we validated AHI9 data quality and compared with AHI8 by using parallel observation data.
  The differences between AHI9 and AHI8 validated by Ray-matching and DCC methods are within ~5%.
    These result also are good agreement with GEO-GEO comparison.
  Himawari-9 had NOT observed since launch in Dec. 2016. (except health check.) However, the sensor sensitivity of AHI9 might have changed as well as AHI on-board the operational satellite Himawari-8.
Future works
Himawari-9 has solar diffuser as on-board calibration target same as Himawari-8.
  We will work on the SD data analysis after we can get enough data like 1year.
Some improvements might be needed in our DCC test implementation.
  e.g., applying deseasonalization.

## Slide 15: END
That all, thank you for your attention.
Any questions or comments?
Contact: k_kodera@met.kishou.go.jp

## Slide 16
Backup slides

## Slide 17: SRF differences (AHI8,AHI9 and NPP/VIIRS)
I1
M5
M7 I2
M3
M2
M4
M3
M10 I3
M11
B01
(0.47μm)
B02
(0.51μm)
B03
(0.64μm)
B04
(0.86μm)
B05
(1.6μm)
B06
(2.3μm)

## Slide 18: AHI9 biases Comparison by Ray-matching and DCC methods
Chart: 
 | 0.028856 | 0.014922 | -0.011335 | 0.0048185 | 0.024815 | -0.050998
 | 0.062154 | -0.0088639 | 0.031338 | 0.042088 | -0.075056 | -0.12693
 | 0.070983 | -0.00062443 | 0.045755 | 0.053438 | -0.01648 | -0.080228
Chart: 
 | 0.0095091 | 0.00015562 | -0.033929 | -0.027944 | -0.0075818 | -0.071917
 | 0.020481 | -0.046698 | -0.025151 | -0.0092687 | -0.042644 | -0.085018
Chart: 
 | 0.045051 | 0.0043254 | -0.020888 | -0.0038469 | -0.058691 | -0.016781
 | 0.046271 | 0.0062245 | -0.021249 | -0.0026447 | -0.059287 | -0.016089
 | 0.051799 | 0.0096386 | -0.015595 | 0 | -0.052616 | -0.017202
 | 0.051799 | 0.0096386 | -0.015595 | 0 | -0.052616 | -0.017202
 | 0.05077 | 0.0096386 | -0.015595 | 0 | -0.053598 | -0.017188
AHI9 is darker
Differences between Ray-matching and DCC methods are within approximately 5%.
In the point of differences between AHI9 and AHI8, Ray-matching and DCC methods are good agreement. (<1%)
However, the AHI9 biases validated by DCC method are larger than those by Ray-matching method.
  These may indicate there is room of improvement in our DCC test implementation.
Against N20
Against SNPP
Against AHI8
In Oct,2022
AHI9 is Brighter

## Slide 19: JMA Ray-matching criteria Table
Ray-Matching criteria | Ray-Matching threshold
Monitored sensor | Himawari8 and Himawari9 / AHI
Reference sensor and version | SNPP and NOAA20 / VIIRS NOAA
Radiance or reflectance pair regression | Reflectance
SBAF | SCIAMACHY 1st order fit ( for AHI B01~B05) Radiative transfer model ( for AHI B06 ) *Under condition of “All sky tropical ocean”
Latitude Domain | ± 20° latitude of sub-satellite location
Longitude Domain | ± 20° longitude of sub-satellite location
Underlying surface | Targets meeting TB < 273.15K
Spatial grid resolution | AHI 1 pixel vs. average of VIIRS 3x3 pixels (for M band) AHI 1 pixel vs. average of VIIRS 5x5 pixels (for I band) * See the backup slide of “Our implementation details –resolution difference-”
AHI/VIIRS pixel resolution | 2km / 0.75km(M) or 0.375km(I) * We use AHI data resampled to 2km resolution for All VNIR bands.
AHI/VIIRS sub-sampling | 2km / 0.75km(M) or 0.375km(I)
Spatial homogeneity ( STDV of reflectance/Mean of reflectance ) | < 5% * See the backup slide of “Our implementation details –spatial homogeneity-” slide.
Table A

## Slide 20: JMA Ray-matching criteria Table
Ray-Matching criteria | Ray-Matching threshold
Time matching difference | < 5 minutes
Solar zenith angle (SZA) difference | <10°
View zenith angle (VZA) difference | <10°
Relative azimuthal angle (RAA) difference | <10°
Scattering angle difference | -
Sun glint angle (Scattering angle) | >25°for AHI only
Linear regression, regression through space offset | Linear regression with offset and linear regression via the origin (force-fit regression)
θ： Sun glint angle
Table A
Table B
Ray-Matching ATBD 2011 (NASA)​ | Ray-Matching threshold​
Timeline temporal resolution​ | Monthly and daily​
Outlier Filter​ | -
Other criteria​ | -
Temporal regression​ | -​
Intercept
slope

## Slide 21: Our implementation details – resolution difference -
Reflectance of
AHI 1 pixel
Average reflectance
on 3x3 VIIRS M band pixels
To considering resolution difference of Input data, our implementation is following way.
Collocating
  Matching up AHI 1 pixel with VIIRS 1pixel
Comparison for AHI refl. with VIIRS refl.
  Comparing refl. of AHI 1 pixel with average refl. of VIIRS 3x3 pixels in M bands
Match up
AHI 1 pixel
VIIRS 1 pixel
Compare
Input Data we use in ray-matching
  AHI : 2km resolution
  VIIRS : 0.75km(M) 0.375km(I)

## Slide 22: Our implementation details – spatial homogeneity -
Pixels in green area are used for checking spatial homogeneity.
The condition of spatial homogeneity check is
AHI data
2km / 1pixel
VIIRS data M bands
0.75km / 1pixel
Spatial homogeneity area
STDV of reflectance
Mean of reflectance
< 5%

## Slide 23: Remove outliers in warm scenes
Some outliers
Fig.1. Ray-matching in All scenes (without TB condition)
Fig.2. Ray-matching in cold scenes (with TB condition of 273K )
Apply threshold of 273K

## Slide 24: Rough uncertainty estimation
Chart: AHI9 biases against AHI8 by Ray-matching method
| B01 | B02 | B03 | B04 | B05 | B06
 | 0.046065 | 0.0062245 | -0.021249 | -0.0026447 | -0.059545 | -0.016089
Bar plots show the biases by validation on 1 month statistic period in Oct.
Error bars mean the range of the biases by validation in 1day period in Oct.
  As rough estimation, Ray-matching method seems to have ~1% uncertainty at least.
AHI9 is darker
AHI9 is Brighter