## Slide 1
Further development of GSICS GEO-LEO IR v2 inter-calibration algorithm
Tim Hewison (EUMETSAT)
+ Many other GSICS contributors over >10 yrs!
GSICS Annual WG Meeting - IR Session 2023-03-01

## Slide 2: Agenda
Review:
Current GEO-LEO IR algorithm
Issues with current algorithm
Proposed changes
Issues to Investigate:
Standard Scene Radiances
Multiple References
Hot Land
Discuss:
The Next Steps
Agree a way forward – Cooperative Development
Volunteers to investigate further changes
Application to LEO-LEO, Ray-matching, …

## Slide 3: Review: Current GSICS GEO-LEO IR algorithm
Collocate in Space, Time, Angle
  Collect Simultaneous Nadir Overpasses (SNOs)
  Tie to contemporary reference instrument
  with very small uncertainty
Hyperspectral Reference (IASI)
  Convolve IASI spectrum with Spectral Response Function (SRF) of monitored instrument
  Can diagnose SRF errors
Compare
  Apply weighted regression to collocated radiances
  Evaluate uncertainties
Generate GSICS Correction
  Update daily
  Distribute via GSICS Servers
Evaluate & Monitor Bias
  Check long-term stability & Decontamination
[mW/m2/sr/cm-1]
[mW/m2/sr/cm-1]

## Slide 4: Review: Issues with current GSICS GEO-LEO IR algorithm
Formulation not user friendly
  Need to invert function to apply – complicates error propagation
Performance at the Cold End
  Large biases – especially in Brightness temperature
  Biases should tend to zero for zero radiance
  High IASI shortwave channels' noise and uncertain calibration
Hot Land Bias issue - unresolved – for now, focus only on night-time data
  First reported by KMA 
  Add CrIS as reference instrument to include collocations around 01:00/13:00 LST
  Restrict RAA? geographic domain? radiometric range?
  Meanwhile, mask out hot land in v2a
    focus first on cold end issue - primarily a meteorological imager
Impact of high viewing angles
  Inconsistent results from Full Disc and Rapid Scan Service
  e.g. due to cloud parallax issues
  repeating VZA dependence analyse for MSG3-IASIC
Diurnal variation
  Need to handle multiple references - including IASI, CrIS, HIRAS, …
  Prime GSICS Correction - merging multiple reference instruments through double-differences
Shown abnormal large biases at high temperature (>300K, Australian desert) scene in window channels during the daytime.

## Slide 5: Proposed metric for tuning algorithm
Proposed metric for tuning algorithm trade-offs
  Uncertainty on bias at range of radiances
  Expressed in Brightness Temperatures (channel independent)
  Standard Scene Radiance
    1976 US Standard Atmosphere in clear sky over calm sea at nadir
    Calculated by RTTOV
    For SEVIRI: Standard Scene Tbs = [284.0, 236.0, 255.0, 284.0, 261.0, 286.0, 285.0, 267.0] K
    On the dry side for GEO WV channels
  Cold - 220K adopted
    ~Cold Cloud Tops
    Same for all channels
    Would 205K be better (DCC threshold)?
  Hot – 305K proposed
    To optimise performance over hot land
    Only for window channels
    Not implemented yet
Plot 2D Histogram (log scale) of collocated radiance + Fit + Uncertainty*10:

## Slide 6: Proposed metrics – Bias uncertainty at 220K, Tb_std, 305K?
 Tb_std bit low for WV channels.  Could go lower than 220K for cold scenes

## Slide 7: Plot in Brightness Temperature instead of Radiance
Still perform all calculations in radiances
  Weighted Linear Regression: y = a.x + b
  x = Reference instrument‘s collocated radiances (LEO = IASI)
  y = Monitored instrument‘s collocated radiances (GEO = SEVIRI)
  sy = Std. Dev. of Monitored instrument‘s collocated radiances + Noise
Convert to Brightness Temperature at last step for plotting
Easier to read
  Especially for uncertainties
Emphasises non-linear response
  Especially in 3.9µm channel for cold scenes
  Regression function looks non-linear

## Slide 8: Weighted linear regression in radiances, Plotted in BT
Uncertainties scaled by x10 to make visible  Uncertainties ~0.5K at 220K, ~0.003K at Tb_std  Plotting in BT highlights non-linearity and large bias for cold scenes

## Slide 9: Change from Weighted Linear to Polynomial Regression
To address issue with large bias for cold scenes
Change from Weighted Linear to Polynomial Regression
Initially:
  Weighted Quadratic Regression: y = a.x^2 + b.x + c
  x = Reference instrument‘s collocated radiances (LEO = IASI)
  y = Monitored instrument‘s collocated radiances (GEO = SEVIRI)
  sy = Std. Dev. of Monitored instrument‘s collocated radiances + Noise
  Constraint to be zero at zero radiance: c = 0
Implemented in Python using numpy polyfit

## Slide 10: Weighted Quadratic Regression of Radiances, Plotted in BT
 More physical function – does tend to zero at Tb=2.7K  Uncertainty at 220K ~0.01K, ~0.003K at Tb_std  305K not reached in night-time data, except in window channels + large uncertainty

## Slide 11: Limit Collocations to near Nadir - VZA<30°
 Fitted Quadratic function is not significantly different  Implies quadratic function provides adequate predictor of bias, independent of VZA

## Slide 12: Invert relationship for GEO-LEO radiances
To make more user-friendly function for GSICS harmonisations:
Swap x and y compared to current GEO-LEO IR algorithm:
Use weights from GEO for LEO:
  Weighted Quadratic Regression: y = a.x^2 + b.x + c
  x = Monitored instrument‘s collocated radiances (GEO = SEVIRI)
  y = Reference instrument‘s collocated radiances (LEO = IASI)
  sy = Std. Dev. of Monitored instrument‘s collocated radiances + Noise
  Constraint to be zero at zero radiance: c = 0
Swap sign in plots for consistency with previous results:
  plot(x, x-y)
Implemented in Python using numpy curve_fit
  to fit to same function
    def fit_func(x, a, b):
      return a * x**2 + b * x # quadratic with offset=0

## Slide 13: Invert relationship for GEO-LEO radiances
 Very similar biases  Small increase in uncertainties  Uncertainty at 220K ~0.02K, ~0.005K at Tb_std

## Slide 14: Invert relationship for GEO-LEO radiances + Errors on x
But this is not mathematically correct
Uncertainties derived for x (MON) applied to y (REF)
Need to use different function to allow uncertainties on x and y:
  Orthogonal Distance Regression (ODR)
Use weights from GEO for LEO:
  Weighted Quadratic Regression: y = a.x^2 + b.x + c
  x = Monitored instrument‘s collocated radiances (GEO = SEVIRI)
  y = Reference instrument‘s collocated radiances (LEO = IASI)
  sx = Std. Dev. of Monitored instrument‘s collocated radiances + Noise
  Constraint to be zero at zero radiance: c = 0
Swap sign in plots for consistency with previous results:
  plot(x, x-y)
Implemented in Python using scipy odr and numpy curve_fit
  to fit to same function def fit_func(x, a, b)

## Slide 15: Invert relationship for GEO-LEO radiances: ODR with sx
 Very similar biases  Small increase in uncertainties  Uncertainty at 220K ~0.02K, ~0.007K at Tb_std

## Slide 16: Investigate Radiance Slicing method
Is Quadratic enough?
  Could there be real radiance ranges with different bias patterns?
  e.g. hot land scenes
Weighted regressions are dominated by clear collocations
Investigate alternative method – Radiance Slicing:
  Divide the collocations into radiance intervals
    Implemented in brightness temperature bins 190, 200, 210, … 310 K
  Calculate mean and its standard error in each bin
  Plot as error bars
  Compare to weighted regression method

## Slide 17: Add Radiance Slicing
 Biases and their standard errors in Tb slices generally similar to quadratic fit (except IR3.9) + overlap with uncertainties  Most channels show a small excess (~0.5K) around 215-235K

## Slide 18: Radiance Slicing over a larger dataset
Repeat radiance slicing over a larger dataset

## Slide 19: Review: Proposed GEO-LEO IR v2 Algorithm
From Tim Hewison (EUMETSAT): Developing an Algorithm for GSICS GEO-LEO IR v2 inter-calibration (2022):
Fitting Quadratic function with offset=0 - Following suggestion from Fred Wu (2020)
  Good consistency with current linear regression near Tb_std
  Still allows small biases at cold cloud tops (Tb~220K)
  More physical bias model (in absence of stray light)
Inverting relationship used in current GEO-LEO IR algorithm
  Simplifies user’s application and uncertainty propagation
  ~Consistent results with current GSICS Correction
  Requires Orthogonal Distance Regression to handle uncertainties on MON – Proposed by Arata Okuyama (c. 2008)
  Already used in Meteosat First Generation FCDR recalibration with HIRS
Radiance slicing method
  Complements regression method – provides check on applicability
  e.g. Confirming no outlier BT ranges (useful for SLSTR, …)
  Allows definition of filters in algorithm development – e.g. to reject hot land pixels
Define 3 scene Tb’s as a metric to optimise algorithm + reporting
  205K, Tb_std, 305K
Orthogonal Distance Regression (ODR)
Use weights from GEO for LEO:
  Weighted Quadratic Regression: y = a.x^2 + b.x + c
  x = Monitored instrument‘s collocated radiances (GEO)
  y = Reference instrument‘s collocated radiances (LEO)
  sx = Std. Dev. of GEO radiances within collocation + Noise
  sy = Noise of Reference Instrument – assumed to be zero
  Constraint to be zero at zero radiance: c = 0

## Slide 20: Review: ODR algorithm proposed 2022-10-06 + Radiance Slicing
 Small excess biases in most channels around 215-235K now reduced (~<0.5K)  IR13.4 channel bias changed due to different ice contamination

## Slide 21: Extend to include daytime collocations
Extend to include daytime collocations

## Slide 22: Include daytime collocations
 Introduces Hot Land Collocations with Excess Bias  Quadratic Function no longer provides good fit – needs further study

## Slide 23: Way Forward + Discussion
Ideas for further development:
  Parallax mask – reject high VZA + low BT combinations
  Filter daytime data better
  Define Standard Scene Tbs: 205K, Tb_std, 305K?
  Check sensitivity of bias to collocation thresholds
    Plot bias v dVZA, RAS, dt, time, …
    Check VZA dependence during daytime
  Check collocations bias Gaussian
  Analysis of time series to define smoothing period for RAC/NRTC
    Standard error or variable moving window
Way-forward
  Do we wait to solve hot land issues?
  Implement for other GEO imagers?
    Other LEO imagers?
    Other reference instruments?
  Application to VIS/NIR Channels?
    Investigate Ray-matching?

## Slide 24: Definition of additional Standard Scene Radiances
Current Standard Scene Radiances – used by EUM, JMA,
  1976 US Standard Atmosphere in clear sky over calm sea at nadir
  Calculated by RTTOV
  On the dry side for GEO WV channels
Cold - 220K adopted – used by JMA, NOAA
  ~Cold Cloud Tops
  Same for all channels
  Would 205K be better (DCC threshold)?
Hot – 305K proposed
  To optimise performance over hot land
  Only for window channels
Other?
Considerations for alternative approaches:
Standard Scene radiances should be channel dependent
  and maybe also geographically dependent
  but ideally should be comparable for all GSICS products for a given instrument class
Could be defined based on percentile of observation space
  but ideally should be comparable for all GSICS products for a given instrument class
Can also be used as metric for tuning algorithm trade-offs
  Uncertainty on bias at range of radiances
  Expressed in Brightness Temperatures (channel independent)
Currently:
  EUMETSATuse Tstd
  JMA use Tstd + 220K, 250K, 290K – for all IR channels
  KMA use ?
  ISRO use ?
  CMA use Tstd
  NOAA use 220K, 250K, 290K

## Slide 25: Multiple reference instruments
Apply same inter-calibration algorithm with different references
Calculate delta (double-differences)
  (used in Prime GSICS Correction concept)
  Check diurnal variations – following Fangfang’s approach
If delta is less than some threshold:
  E.g. ±0.1K
  (based on uncertainty of references’ relative calibration)
  Combine results
Sometimes, diurnal cycle and instrument calibration differences are mixed
Side-issue:
  Use of CrIS as reference
  (gap-filling to account for truncated BUFR data)
IASI-A, IASI-B, AIRS, NOAA20-CrIS, SNPP-CrIS (gap-filling): Jul. 2019.~Jan. 2020.
Latitude > -10 ° (To avoid Australian Desert region)
Minju Gu (KMA) - KMA GEO-LEO IR product status - March 2020

## Slide 26: Hot Land
EUMETSAT analysis
  GEO-GEO shows diurnal variations ~1K
  Meteosat-11 -10 (0°- 9.5°E)
  Low inclination
Azimuth Angle filtering = Ray-matching
  Fails to reject bias over hot land pixels
Similar impact on 8.7µm as window channels
   Probably not an emissivity issue
Diurnal variation of AMI-AHI Tb[K]
- Red, Blue, Green and Gray lines represent AMI Tb, AHI Tb, Bias(AMI-AHI Tb) and solar zenith angle, respectively
Minju Gu - KMA GEO-LEO IR product status - March 2020

## Slide 27: Reminder: Implications for GSICS Plotting Tool
Changes to the GEO-LEO IR algorithm
Will not work with current GSICS Plotting Tool
Need to revise
See agenda items from Monday

## Slide 28: Proposed Cooperative Further Development Work
GPRCs operating GEO imagers to implement proposed algorithm for GEO-LEO IR:
  With any further improvements agreed here (e.g. repeating based on BT)
  CMA, EUMETSAT, ISRO/IMD, JMA, KMA, NOAA?
  Check sensitivity of bias to collocation thresholds (and that they are Gaussian)
    Plot bias v Relative Zenith Angle, Relative Azimuth Angle, time of day, time difference, atmospheric parameters, …
  Analysis of time series to define smoothing period for RAC/NRTC (instrument-specific)
    Standard error or variable moving window
Volunteers to investigate further improvements:
  Parallax mask – reject high VZA + low BT combinations
  Using multiple GEO imagers per LEO overpass
  Detect and Filter collocations affected by Hot Land issue
  Multiple References/Diurnal Variations
  Define Standard Scene Tbs: e.g. 205K, Tb_std, 305K?
  Uncertainty Analysis!
  Application of algorithm for Ray-matching of VIS/NIR channels?
GPRCs operating multiple GEO imagers to implement proposed GEO-GEO algorithm:
  CMA, EUMETSAT, ISRO/IMD, JMA, KMA, NOAA?
  next agenda item…

## Slide 29: Development Timeline
Agree baseline v2 algorithm for GEO-LEO IR
  by 2023-09?
GPRCs to implement baseline algorithm for their GEOs
  by 2023-12?
GPRCs to report performance of algorithm + sensitivity studies
  By 2024-03?
Report on application to VIS/NIR channels
  ?
Report on application to LEO-LEO IR
  ?
Report on application to GEO-GEO – previous agenda item
  ?

## Slide 30
Thank you!
Questions are welcome.