## Slide 1: Scoping New GSICS Product Class - A Strawman Proposal
Tim Hewison, Sebastien Wagner, Vincent Debaecker
EUMETSAT

## Slide 2: Aims for revised GSICS Product
Aim to develop strawman proposal to address needs for:
GSICS Corrections/Calibration Coefficients for VIS/NIR + TIR channels
  Combined in single product
  would allow one product per mission
  to include more sophisticated validity date/times - to allow diurnal variations
  additional validity conditions - e.g. exclude parts of diurnal cycle/dynamic range
to complement the current product content with additional metadata / variable as required
  improved product traceability and usage
to accommodate updated GEO-LEO v2 algorithm:
  more user-friendly algorithm formulation (not inverted!)
  better performance at the cold end
  address Hot land bias issues
  impact of high view angles
  diurnal variation
  Correction in form of a generic regression algorithm (change weighted linear to polynomial regression)
to interface to future version of GSICS Plotting Tool

## Slide 3: Assumptions
Continue to generate GSICS Products
  GSICS Correction/Harmonization/Calibration
To be distributed by GSICS Data and Products Servers
Continue to use netCDF
  Using groups in netCDF4
  following CF-convention
  see NetCDF Climate and Forecast Metadata Convention
  + NetCDF Attribute Convention for Dataset Discovery
Updating GSICS netCDF convention
  and GSICS filenaming convention
  GSICS file naming conventions need to be revised to remove indication of the spectral domain

## Slide 4: Previous Discussions
Discussed at GDWG Web Meeting 27 October 2022:
  http://gsics.atmos.umd.edu/bin/view/Development/Gdwgweb
Based on that, Manik developed this dummy product:
  https://drive.google.com/drive/folders/1-7IBvZexns2Mq-aY10yisCQmTiYyY0fP
using the Collab notebook code here:
  https://colab.research.google.com/drive/1qq-ogt47PtGaSobm11oRJbjp7iruKrhZ

## Slide 5: Strawman Proposal
Provide single GSICS product for each mission (RAC/NRTC)
  for all channels - combining different methods/references
to provide users only best estimate of calibration/correction
  for each channel
  with uncertainty
  + traceability to methods/references used to generate it (and their weights/uncertainties)
  (weights change with time)
  Simpler than current prototype for VIS/NIR – single blend of methods
  Replaces Prime GSICS Correction – and single reference corrections for IR channels

## Slide 6: Full Hierarchy Product Structure
Best Blend
Method 1
Method 2
Method 3
Reference 1
Reference 2
Reference 3

## Slide 7: Simple Product Structure
Best Blend
X
X
X
X
X
X

## Slide 8: Open Issues for Discussion
Assumes we include different maturity for different bands in the same product
  Risk: How to deal with incomplete processing?
Alternatives:
  To include multiple reference instruments?
  To include multiple methods?
  for all channels? (lots of NaNs)
    or group channels by spectral band
  All more complex to define, implement and use
  Of little interest to external users
  (Assumes deep-dive possible through querying internal databases)

## Slide 9: Implications for GSICS Plotting Tool
Define standard reflectance scenes for VIS/NIR
  Follow similar concept for IR channels
  allows users to evaluate impact of non-linear GSICS correction for different scenes
  Default = 100% = equivalent slope change for linear correction (Lmin/Lref/Lmax)
  Need to include formula and coefficients to convert to/from radiance
Simplifies future plotting tool
  But include recent NRTC results overplotted by default in future
Assumes deep-dive possible through querying internal databases

## Slide 10: Example Current GSICS Plotting Tool RAC + NRTC

## Slide 11: GSICS Plotting Tool Combining RAC + NRTC
Default configuration:
  Read RAC
  Plot as time series
  Read all NRTC since end of RAC
  Plot as points on same time axes

## Slide 12: Product Structure
Group variables:
  Time
  GSICS Correction/Calibration Formula + Coefficients (+uncertainties) + validity range (radiance, time_of_day, dates)
    per channel
    by maturity (by channel)
    Reference Instrument(s) - (by channel) + weights (by channel, time)
    Methods (by channel) + weights (by channel, time)
  Monitored Instrument
    Channels
      Names
      Central wavelengths
      Radiance-BT conversion formula + coefficients (alpha, beta, wnc)
      Radiance-Reflectance conversion formula + coefficients
      Standard Scene Radiance/BT/Reflectance

## Slide 13: Next Steps
Share your thoughts on this proposal
Agree consensus on way forward
  By GSICS Exec Panel?
Task GDWG to update GSICS conventions for new products:
  GSICS netCDF convention
  and GSICS filenaming convention
GPRCs to generate sample products
  Who?
  Which missions?
  When? E.g. By 2024 Annual Meetings
  EUMETSAT may be able to distribute via gsics.eumetsat.int - TBC