## Slide 1
Mission Integrated Calibration Monitoring & Inter-Calibration System (MICMICS)
Ali Mousivand, Sebastien Wagner, Tim Hewison, Mounir Lekouara
GSICS annual meeting 2023

## Slide 2: Agenda
Some historical context
  MSG SEVIRI Cal/Val
Cal/Val activities at EUMESAT
  Challenges
  An integrated approach
MICMICS
  MICMICS prototyping
  MICMICS workflows
  MICMICS timeline
Few examples
  GEO-LEO IR
  LEO-LEO IR
  Desert

## Slide 3: Some historical context – MPSTAR monitoring tools for MSG
  SEVIRI Solar Channel Calibration system (SSCC)  Ref = RTM
      Applied to VIS0.6 / VIS0.8 / NIR1.6 / HRV
  Deep Convective Clouds Calibration System (DCCCS)
      Applied to VIS0.6
      Ref = MODIS Aqua
  Lunar Calibration System
      Applied to VIS0.6 / VIS0.8 / NIR1.6 / HRV
      Ref = GIRO model
    GSISCS GEO-LEO engine for IR
Notes: MPSTAR = Offline Operational Infra-structure hosting monitoring facilities
  Under Configuration management  OPS procedures to implement + deploy

## Slide 4: Cal/Val challenges
Cal/Val Challenges
  Increasing number of missions and channels to monitor
  Increasing number of calibration/inter-calibration products
  Need to allow more complex a posteriori data analysis + monitoring (across channels + missions)
  More complex processors + number of processors (methods) to be maintained + operated to support OPS
  More stringent mission requirements on instrument performances
  Need for rationalizing developments + tools
Individual mission specific/calibration system specific tools are no longer efficient!

## Slide 5: Paradigm shift
An integrated approach:
Reduced maintenance efforts
Straightforward propagation of algorithm enhancements
Easier cross-calibration and comparison of results

## Slide 6: Mission Integrated Calibration Monitoring & Inter-Calibration System (MICMICS)
An integrated tool to independently monitor and analyze multiple instruments’ calibration and their on-board calibration system, by integrating various vicarious calibration systems.
MICMICS addresses the L1 radiometric calibration needs for all channels of EUMETSAT imaging instruments and selected EUMETSAT and third party reference instruments (inter-calibration).
MICMICS performs systematic comparisons with reference instruments to generate GSICS inter-calibration products – both directly via Simultaneous Nadir Overpasses, and indirectly, via double-differencing vicarious calibration results.
Operational MICMICS will be integrated with Multi Mission Element(MME) to serve the CAL/VAL role

## Slide 7: MICMICS team
INRC manager
Mounir Lekouara
Project lead
Ali Mousivand
VIS-NIR
Sébastien Wagner
IR support
Tim Hewison
implementation
Vincent Debaecker
implementation
Rakshith Shanbhag
Support
IR implementation
Alessandro Burini

## Slide 8: MICMICS Prototyping
L1 data (e.g. FBF, DSNNAS)
External Databases (e.g. GSICS server)
Data Acceptance Module
CPMs/Workflows
Orchestrator
Databases
IID
COD
IDS
SCD
Data Analysis and Reporting
Reports
Alerts
GSICS corrections
(when operational)
Ground segment

## Slide 9: MICMICS Workflows
Instruments
Instruments
Lunar Calibration
Desert Calibration
DCC Calibration
Lunar Inter-Calibration
Inter-Calibration Blender
DCC Inter- Calibration
Rayleigh Calibration System
Rayleigh Inter-Calibration System
Imager-Hyperspectral Inter-Calibration
NWP Calibration
Imager-Imager Inter-Calibration
ICBS
IHICS
IIICS
NWPC
Ray-Matching Inter-Calibration System
NWP Inter-Calibration
NWPIC
DCC Extraction Module
Lunar Extraction Module
DECS
DCCICS
DCCCS
LCS
LICS
RAYMICS
RAYCS
RAYICS
DCCXTRM
LXTRM
MICMICS
CPMs
VIS/NIR channels
MSG SEVIRI VIS/NIR
S3
SLSTR & OLCI VIS/NIR
MTG LI VIS
EPS AVHRR VIS/NIR
EPS-SG 3MI VIS/NIR
MTG FCI VIS/NIR
Thermal channels
MSG SEVIRI IR
MTG FCI IR
S3 SLSTR IR
EPS AVHRR IR
EPS-SG VII IR
EPS-SG MWI/ICI MW
CO2M
CLIM & MAP
EPS-SG VII VIS/NIR
Pre-Colocation Tool
Colocation Tool
Subsetter Tool
Data-Fusion Tool
SUBTL
DFTL
PCOLT
COLT

## Slide 10: MICMICS Timeline
 | CPMs for Reflected Solar Band | MSG | S-3 | S-3 | MTG | MTG | EPS-SG | EPS-SG | EPS
 |  | SEVIRI VIS/NIR | OLCI VIS/NIR | SLSTR VIS/NIR | FCI VIS/NIR | LI VIS | VII VIS/NIR | 3MI VIS/NIR | AVHRR
 | Lunar Cal (LCS) |  |  |  |  |  |  |  | 
 | Lunar Inter-Cal (LICS) |  |  |  |  |  |  |  | 
 | Desert Calibration (DESC) |  |  |  |  |  |  |  | 
 | Desert Inter-Calibration (DESIC) |  |  |  |  |  |  |  | 
 | DCC Inter-Cal (DCCICS) |  |  |  |  |  |  |  | 
 | DCC Cal (DCCS) |  |  |  |  |  |  |  | 
 | Inter-Calibration Blender (ICBS) |  |  |  |  |  |  |  | 
 | Rayleigh Calibration System (RAYCS) |  |  |  |  |  |  |  | 
 | Rayleigh Inter-Cal System (RAYICS) |  |  |  |  |  |  |  | 
 | Ray-matching Inter-Cal System (RAYMICS) |  |  |  |  |  |  |  | 
 | CPM for Thermal Band | MSG | S-3 | S-3 | MTG | MTG | EPS-SG | EPS-SG | EPS
 |  | SEVIRI IR | OLCI | SLSTR IR | FCI IR | LI | VII IR | 3MI | AVHRR
 | Imager-Hyperspectral Inter-Cal |  |  |  |  |  |  |  | 
 | Imager-Imager Inter-Cal |  |  |  |  |  |  |  | 
 | NWP Cal |  |  |  |  |  |  |  | 
2021-2022
2023-2024
No firm plan yet
Not applicable

## Slide 11: Few Example CPMs
Few Example CPMs

## Slide 12: IR Channels calibration monitoring GEO-LEO IR
Collocate in Space, Time, Angle
    Collect Simultaneous Nadir Overpasses (SNOs)
    Tie to contemporary reference instrument
    with very small uncertainty
Hyperspectral Reference (IASI)
    Convolve IASI spectrum with Spectral Response Function (SRF) of monitored instrument
    Can diagnose SRF errors
Compare
    Apply weighted regression to collocated radiances
    Evaluate uncertainties
Generate GSICS Correction
    Update daily
    Distribute via GSICS Servers
Evaluate & Monitor Bias
    Check long-term stability & Decontamination
[mW/m2/sr/cm-1]
[mW/m2/sr/cm-1]

## Slide 13: GEO-LEO IR Workflow
Instruments
Instruments
Lunar Calibration
Desert Calibration
DCC Calibration
Lunar Inter-Calibration
Inter-Calibration Blender
DCC Inter- Calibration
Rayleigh Calibration System
Rayleigh Inter-Calibration System
Imager-Hyperspectral Inter-Calibration
NWP Calibration
Imager-Imager Inter-Calibration
ICBS
IHICS
IIICS
NWPC
Ray-Matching Inter-Calibration System
NWP Inter-Calibration
NWPIC
DCC Extraction Module
Lunar Extraction Module
DECS
DCCICS
DCCCS
LCS
LICS
RAYMICS
RAYCS
RAYICS
DCCXTRM
LXTRM
MICMICS
CPMs
VIS/NIR channels
MSG SEVIRI VIS/NIR
S3
SLSTR & OLCI VIS/NIR
MTG LI VIS
EPS AVHRR VIS/NIR
EPS-SG 3MI VIS/NIR
MTG FCI VIS/NIR
Thermal channels
MSG SEVIRI IR
MTG FCI IR
S3 SLSTR IR
EPS AVHRR IR
EPS-SG VII IR
EPS-SG MWI/ICI MW
CO2M
CLIM & MAP
EPS-SG VII VIS/NIR
Pre-Colocation Tool
Colocation Tool
Subsetter Tool
Data-Fusion Tool
SUBTL
DFTL
PCOLT
COLT

## Slide 14: SLSTR-IASI inter-calibration
Developed as general CPM in MICMICS
Routine monitoring of SLSTR IR channels (nadir and oblique) vs IASI
Collection of collocations since August 2019
  Since Jan 2021 Oblique view enabled
  and S7 with spectral gap filling enabled

## Slide 15: Desert Calibration
RTM
  A customised version of the polarized 6SV2.1 RTM, DISORT, Monte-Carlo and a few more RTMs (from libRadTran)
Surface
  4-parameter BRDF RPV model
Atmosphere
  US standard 1962, scaled with H2O and O3 column
  Customized Desert Aerosol model
  O3, WV, surface pressure and AOT550 from ECMWF
Instruments (so far)
  Sentinel-3 OLCI & SLSTR
  MSG SEVIRI
  MTG-FCI and MTG-LI
  EPS-AVHRR
  Straightforward to add new instruments

## Slide 16: Conclusion
MICMICS = agile system dedicated to the near-real time monitoring of radiometric performances and inter-calibration
Main assets:
  Easy integration of new missions
  Easy integration of new calibration methods
  Inter-operability of the processing modules
  Rationalisation of resources + efforts (including maintenance)
  Support the operational generation of GSICS products (and intermediate products such as collocations)
  Support generation of Fundamental Climate Data Records
Status
  The prototype has been extensively tested and validated
  Already supporting the EUMETSAT diagnostics on SEVIRI, AVHRR, OLCI and SLSTR
  Will become the EUM GSICS engine and replace MPSTAR in 2023
  Fully ready for the FCI and LI commissioning
  Developments are on-going for EPS-SG and CO2M

## Slide 17
Thank you!
Questions are welcome.

## Slide 18: MICMICS Prototyping
Data Acceptance Module
MICMICS Catalogue
Data Discovery Layer
Level 1 + Aux Repository
MICMICS CPM-1
MICMICS CPM-2
MICMICS CPM-3
MICMICS CPM-4
JobOrder1
JobOrder2
JobOrder3
Data Processing Layer
MICMICS Results DB
MICMICS Data Analysis and Reports
Results
Data Analysis Layer
MICMICS Orchestrator
MICMICS JobOrders
JobOrder1
JobOrder2
JobOrder3
Job Preparation Layer
IID SCD
CFG

## Slide 19: Deep Connective Cloud Inter-Calibration System (DCCICS)
Inter-calibration system using DCC as calibration transfer targets and the GSICS reference instrument(NOAA-VIIRS) as a calibration reference (red ellipse in the figure).
General Triggering and Scheduling:
  Triggered by the availability of DCCXTRM products in the MICMICS product catalogue over the defined window period (e.g: for Re-analysis Correction (RAC) it is P+15D-15D).
Input
  The DCCICS accepts a job order as input.
  A typical use case is the following:
    Step-1: The DCCXTRM product catalogued is queried using the temporal mode to fetch the data over the defined time period.
    Step-2: The DCCICS module processes the list of DCCXTRM files over the time frame, to generate a GSICS VISNIR DCCICS product.
Output
  A NetCDF file containing the inter-calibration observables/statistics calculated over land and sea
  An optional quick look file in PNG format
  NOTE: the module also produces temporary files such as a report file, quick looks (JPEG/PNG), and CSV files, kept in the working directory for potential investigations
Platforms | Instruments | Channels
Meteosat-8 to 11 | SEVIRI | VISNIR
MTG-I1 to I4 | FCI | VISNIR
 | LI | VIS0.7
Sentinel-3A to 3B | OLCI | All
 | SLSTR | (S1 to S6) and S8
DCCICS workflow with all dependencies, descriptions are only for the red ellipse

## Slide 20: Workflow description for the DCCICS FCI
Processing Step 1 | 
Triggering Mechanism | Time Driven by Schedule: Daily Run
Execution Coverage | Depends of the mode: Last 30 days
Requisites | 
Inputs | 
Input 1 | Mandatory: YES Origin: MICMICS DCCXTRM Retrieval Mode: N/A (the product that triggers the workflow) File Type: MICMICS PRODUCT File Name Type: Physical Product ID: SATCAL+DCCXTRM
Input 2 | Mandatory: YES Origin: These files are part of the CPM delivery Retrieval Mode: N/A File Type: JSON files (static files) File Name Type: Physical Product ID: dccics_{SensorID}_{SatelliteID}.json e.g. dccics_fci_mti1.json
Auxiliary File: IID | Mandatory: YES Origin: MICMICS IID Retrieval Mode: LatestValidityClosest File Type: Auxiliary Product File Name Type: Physical Product ID: iid_dump_{Satellite_id}_{Sensor_id}.json
Auxiliary File: HU Model data | Mandatory: YES Origin: These files are part of the CPM delivery Retrieval Mode: N/A File Type: Auxiliary Product File Name Type: Physical Product ID: Hu_data.nc
Auxiliary File Seasonality files | Mandatory: YES Origin: These files are part of the CPM delivery Retrieval Mode: N/A File Type: Auxiliary Product File Name Type: Physical Product ID: SeasonalIndices_{SensorID}_{SatelliteID}_RAC30Days.nc
Configuration File | Mandatory: YES Origin: These files are part of the CPM delivery. Retrieval Mode: N.A. File Type: xml configuration file File Name Type: Physical Product ID: SATCAL+ DCCICS +CFG_{dataset_A} e.g. SATCAL+DCCICS+CFG_FCI-MTI1.xml
Outputs | 
Output 1 | Mandatory: YES Destination: Calibration Output Database (COD) Number of Output Products: 1 File Type: MICMICS generated file File Name Type: Physical Product ID: SATCAL+RAC+{scenario_type}IR+DCCICS e.g: SATCAL+RAC+GEOLEOIR+DCCICS
Output 2 | Mandatory: NO Destination: Calibration Output Database (COD) Number of Output Products: 1 file per channel File Type: MICMICS generated file File Name Type: Physical Product ID: SATCAL+RAC+{scenario_type}IR+QLK (Quicklook) e.g: SATCAL+RAC+GEOLEOIR+QLK
Output 3 | Mandatory: Yes Destination: Number of Output Products: 1 File Type: Output Report File Name Type: Physical Product ID: N/A

## Slide 21: Deep Connective Cloud Extraction Module (DCCXTRM) necessary to run DCCICS
Role
  Extract the dcc pixel from subset data
  Generate the dcc data to be further processed by the dcc inter-calibration and calibration workflows
  Ingest the required information into catalogues to trigger further processing and relocate the products of the workflow in their final destination within the MICMICS infrastructure
Input
  The DCCICS accepts a job order as input.
  A typical use case is the following:
    Step-1: The subset data catalogue is navigated to detect if new Level 1 subset input is available.
    Step-2: In case a new input is available, the DCCXTRM is triggered.
    Step-3: If a dcc pixel is detected, the DCCXTRM module generates a DCCXTRM product, which will be itself catalogued for further processing.
Output
  If DCC pixels are detected and extracted, DCCTRM produces outputs to be catalogued:
  A NetCDF file containing the DCC pixel observables to be processed further in the DCC Inter-Calibration Workflow.
  An optional quick look file in PNG format.
  Note: the module also produces temporary files such as a report file, quick looks (JPEG/PNG), and CSV files, kept in the working directory for potential investigations.
Platforms | Instruments | Channels
Meteosat-8 to 11 | SEVIRI | VISNIR
MTG-I1 to I4 | FCI | VISNIR
 | LI | VIS0.7
Sentinel-3A to 3B | OLCI | All
 | SLSTR | (S1 to S6) and S8
DCCXTRM workflow with all dependencies, descriptions are only for the red ellipse

## Slide 22: Workflow description for the DCCXTRM FCI
Processing Step 1 | 
Triggering Mechanism | Data Driven by FCI L1c Subset products (trigger when the subset product is available)
Execution Coverage | 
Requisites | 
Inputs | 
Input 1 | Mandatory: YES Origin: MICMICS SUBSETTER Retrieval Mode: N/A (the product that triggers the workflow) File Type: MICMICS PRODUCT File Name Type: Physical Product ID: SATCAL+ROI
Auxiliary File: IID | Mandatory: YES Origin: MICMICS IID Retrieval Mode: LatestValidityClosest File Type: Auxiliary Product File Name Type: Physical Product ID: iid_dump_{Satellite_id}_{Sensor_id}.json
Auxiliary File: LAND SEA MASK | Mandatory: YES Origin: These files are part of the CPM delivery Retrieval Mode: N/A File Type: Auxiliary Product File Name Type: Physical Product ID: {Sensor_id}_LAND_SEA_MASK_{SSP}.nc Eg: FCI_LAND_SEA_MASK_00.nc
Configuration File | Mandatory: YES Origin: These files are part of the CPM delivery. Retrieval Mode: N.A. File Type: xml configuration file File Name Type: Physical Product ID: SATCAL+DCCXTRM+CFG_{dataset_A} e.g. SATCAL+DCCTRM+CFG_FCI-MTI1.xml
Outputs | 
Output 1 | Mandatory: YES Destination: Calibration Output Database (COD) Number of Output Products: 1 file per subset File Type: MICMICS generated file File Name Type: Physical Product ID: SATCAL+DCCXTRM (dcc pixel file)
Output 2 | Mandatory: NO Destination: Calibration Output Database (COD) Number of Output Products: 2 files ( 1 with all vis channels, 1 with NIR channel) File Type: MICMICS generated file File Name Type: Physical Product ID: SATCAL+DCCXTRM+QLK (Quick-look)
Output 3 | Mandatory: Yes Destination: Number of Output Products: 1 File Type: Output Report File Name Type: Physical Product ID: N/A