## Slide 1
Lunar Calibration Activities at AIST
- An update on SP Lunar Model
Toru Kouyama, Masataka Imai, Ryosuke Nakamura (AIST/AIRC, Operando OIL)
Yasuhiro Yokota (ISAS/JAXA)
2020 Lunar calibration workshop
Lunar model development
SP = Spectral Profiler, a spectrometer onboard Kaguya

## Slide 2
KAGUYA | SELENE: A Japanese Lunar orbiter
・Size: 2 x 2 x 5m, 14 science instruments
・Orbit: Polar orbit (non sun-synchronous)
Altitude: 100 km
Ground track repeat cycle: ~ 30 days
・Mission period: 2007 – 2009 (finished)
・14 instruments, including SP
Observing lunar surface
with various solar incident and phase angle conditions.

## Slide 3
(Spectral Profiler)
Spectral
: Spectrometer
Point sensor
http://www.kaguya.jaxa.jp/en/equipment/tc_e.htm
Multi-band Imager
Terrain Camera
SELENE(KAGUYA) and SP
Spatial
Wavelength
Multiband Imager
SP

## Slide 4
SP Lunar Reflectance model (Yokota et al., 2011, Kouyama et al., 2016)
Reflectance spectrum
at a reference condition
i = 30°, e=0°, α=30°
Reflectance map (cube) - example: 758nm
Lunar surface
Photometric property is also modeled as a function of (i, e, α)
Radiance map (cube)
(Sub solar lon, lat) = (+10, 3), (Sub observer lon, lat) = (0, 3)
Hyperspectral reflectance map (516 – 1600 nm)

## Slide 5
April 13, 2003
April 15
April 18
Simulating Moon observations
(2D image projection)
SP model is a disk-resolved, radiance-based model.
Also it can be used as a irradiance model by integrating whole brightness of the lunar disk.

## Slide 6
Applying SP model to lunar calibration
Observation
2017
Observation
/ Simulation
Simulation
2003
Band 1
Band 1
Degradation
We can assume no-degradation
Compare
compare
compare
[cf. Kouyama et al., 2019]

## Slide 7
SP model performance
Measuring sensitivity degradation
2016
2017
[Kouyama et al., 2017]
50-kg small satellite
“Hodoyoshi-1”

## Slide 8
Comparing with ROLO
SP model performance
Sensitivity degradation in ASTER (2003 → 2017)
Onboard lamp
Vicarious
(Green)
(Red)
(IR)
(IR, Backward)
Phase angle = -27° (2003), -20° (2017)
The results from SP model were well consistent with the ROLO results (within 1 %).
The results helped to update ASTER’s radiometric calibration coefficient.
[Tsuchida et al., 2020]
[Kouyama et al., 2019]
ASTER’s lunar observations
2003-04-14
2017-08-05

## Slide 9
SP reflectance shows a “redding” trend
darker in shorter wavelength
brighter in longer wavelength.
(cf. Ohtake et al., 2010 & 2013)
SP’s reflectance
Not good absolute accuracy.
Less consistency among different wavelengths.
[Ohtake et al., 2013]
Evaluation and correction of SP model tendency:
comparing with ROLO model
Notes: This plot shows a comparison of observation results among many sensors at a same place
SP reflectance shows a steeper profile than those
As a result… In shorter wavelength region, SP tends to describe Moon reflectance darker.
感度偏差: sensitivity deviation

## Slide 10
Correction curve for SP model
based on ROLO-SP comparison
ROLO irradiance is based on ver.311g (Kieffer and Stone, 2005).
Ratio (ASTER/SP)
[Kouyama et al., 2016]
Lunar irradiance ratio (ROLO/SP)
Evaluation and correction of SP model tendency:
comparing with ROLO model
We confirmed the redding trend of SP from comparison with ROLO,
and proposed the correction curve

## Slide 11
Chart: Lunar irradiance comparison (Normalized by 550 nm ref.)
| 390 | 480 | 550 | 590 | 700 | 860 | 950
 | 0.39035 | 0.88935 | 1 | 1.0169 | 1.0052 | 0.77129 | 0.70993
Observed
Hayabusa-2
Better spectral consistency with observations
SP: Not corrected
SP: Corrected with ROLO
[after Suzuki et al., 2017, Icarus]
Evaluation and correction of SP model tendency:
comparison with lunar observation

## Slide 12
Update: SP model availability
The SP model cube will be released via JAXA’s site.
Dr. Yokota, now in JAXA’s data analysis/archive section, is working hard for the release.
Maybe near future…
Hyperspectral map of lunar surface reflectance
https://jlpeda.jaxa.jp/product/archive/detail_10/

## Slide 13
Update: SP model availability 2
The SP model cube is also available from me.
Dr. Matsunaga (PI of SP) allows me to share the model to researchers personally.
A sample IDL code:
Quick look for
SP reflectance map
Map of Albedo groups
Geometry maps
for a given observation condition
Incident
Emission
Phase
Radiance map (cube)
Shared with NOAA, JMA, etc…

## Slide 14
Update: SP model availability 2
The SP model cube is also available from me.
Dr. Matsunaga (PI of SP) allows me to share the model to the researchers personally.
Developing an application (lead by Masataka Imai):
Observation date
Inputs
Satellite position
(or TLE)
Spectral response function
Spatial resolution
Radiance map (band)
SP model
Outputs
2D image projection
Disk-integrated Irradiance (band)
ROLO/GIRO

## Slide 15
Summary & Future plan
SP model (disk-resolved hyperspectral model) was proposed, and it shows a good performance to evaluate sensitivity degradation.
Bias (redding trend) in the SP observation, thus in SP model, was confirmed. It can be corrected through the comparison with ROLO. => Model comparison (fusion) is essential for SP model
The SP model can be shared, please contact me. Also JAXA has a plan to release the SP model to the public.
Investigation for further update of SP model and inter-model comparison is continuing: e.g. expanding wavelength range, phase angle dependence, libration dependence, etc…

## Slide 16
Thank you!
References
Yokota et al., 2011. Lunar photometric properties at wavelengths 0.5–1.6 μm acquired by SELENE Spectral Profiler and their dependency on local albedo and latitudinal zones. Icarus215,639–660.
Kouyama et al., 2016. Development of an application scheme for the SELENE/SP lunar reflectance model for radiometric calibration of hyperspectral and multi spectral sensors, Planetary and Space Science.

## Slide 17
Backup slides…

## Slide 18
(Future) Update: Wavelength range
Dr. Yokota has prepared updated version of SP model (510 – 2100 nm), but not validated yet

## Slide 19
Phase angle dependence of SP model and ROLO
@ 745.3 nm
ROLO
SP model
Disk reflectance
(Normalized by 30°)

## Slide 20
Phase angle dependence between ROLO and SP
@ 745.3 nm
*This structure is different in different wavelengths

## Slide 21
Stability of SP sensitivity during mission
The degradation of SP was not significant over the mission period (up to 1 %).
= Good performance for measuring relative degradation.
Comparison of four observations of
Apollo 16 landing site [Yamamoto et al., 2011]
Nov. 19, 2007
Mar. 12, 2009
SP model accuracy
Notes: Sensor stability during the mission

## Slide 22
Other issues
Not good model accuracy in high emission angle and high latitude regions
Yokota’s recommendation: emission angle < 45 degrees.
Model
ASTER
SP model is a radiance model. Accuracy of image registration may affect uncertainty.