## Slide 1: Lunar calibration and Himawari-8 AHI monitoring
Meteorological satellite center, JMA
OKUYAMA Arata

## Slide 2: Mission Overview
Himawari-8
  Advanced Himawari Imager (AHI): GEO imager w/ 3 VIS, 3 NIR, 10 IR bands
  Solar diffuser is equipped for VNIR calibration (but w/o SDSM)
  Full-disk observation every 10 min. + 5 regional observations every 2.5/0.5 min.
  Has been operational since July 2015, located at ~140.7 E
Himawari-9
  Launched on 2 Nov. 2016, Located at ~140.7 E, ~0.1 degrees apart from Himawari-8
  10 Mar. 2017: the satellite was put into in-orbit standby as back up for Himawari-8
  The switchover from H8 to H9 is planned in 2022

## Slide 3: Observation in 10 min. cycle
Region 4, 5: mainly used for landmark observation, but region 5 is also used for lunar observation
Full Disk Observation
every 10 min. (23 swaths)
Region 1
2000 x 1000km
(NE Japan)
Every 2.5 min.
Region 2
2000 x 1000km
(SW Japan)
Every 2.5 min.
Region 3
1000 x 1000 km
(Target Area)
Every 2.5 min.
Region 4
1000 x 500 km
(Landmark Area)
Every 30 sec.
Region 5
1000 x 500 km
(Landmark Area)
Every 30 sec.
Pre-defined area
Flexible observation area
AHI FoR
Earth edge
Lunar observations
Band5 (1.6μm)

## Slide 4: AHI Lunar Observation
Lunar observation: based on the prediction of its position within AHI’s Field of Regard
Regional observation mode (1000 x 500 km for the earth scene) is used
1 observation / 30 seconds
one scan to observe the Moon
All 6 VNIR bands (0.47, 0.51, 0.64, 0.86, 1.6, 2.3 µm) are used for GIRO

## Slide 5: Trend monitoring approaches
Lunar
  Reference: GIRO (GSICS implementation of the ROLO) simulated irradiance
  A rough and empirical phase angle dependency correction is applied for NIR bands.
Solar diffuser
  Reference: computed radiance reflected by the SD
  The SD is covered to prevent sunlight exposure.
Vicarious calibration by RTM
  Reference: Simulated radiance over cloud-free ocean surface (for B03-B06) and uniform water cloud top using radiative transfer code, RSTAR.
Ray-matching w/ VIIRS
  Reference: SNPP/VIIRS observed reflectance
  SRF difference is considered by the NASA SBAF* tool.
Deep Convective Cloud (DCC)
  Reference: Mode or mean of MODIS DCC histogram
  SRF difference is considered by the NASA SBAF* tool.
  Application to NIR bands looks challenging.
* https://satcorps.larc.nasa.gov/cgi-bin/site/showdoc?mnemonic=SBAF
Obs / GIRO (B05: 1.6um)
Phase angle

## Slide 6: Trend monitoring
B01 (0.47um)
B04 (0.86um)
B03 (0.64um)
B02 (0.51um)
B06 (2.3um)
B05 (1.6um)
Lunar
SD
RTM
Ray-match
DCC
* All the trends are normalized for the intercept of the regression line to be 1.0.

## Slide 7: Trend monitoring
Sensitivity trend based on the GIRO tool is consistent with the results by other approaches.
Lunar calibration approach is applicable to trend monitoring for all AHI VNIR bands.
Annual trend of AHI/Reference [%/year] (Slopes of the regression lines)
Chart: 
| B01 | B02 | B03 | B04 | B05 | B06
Lunar | -0.38103 | -0.49764 | -0.76225 | -0.62125 | -0.096538 | -0.16108
SD | -0.41538 | -0.36446 | -0.53779 | -0.55454 | -0.057597 | -0.02309
RTM | -0.46825 | -0.57771 | -0.816 | -0.70483 | -0.19246 | -0.24036
Ray-match | -0.39849 | -0.52306 | -0.74993 | -0.62241 | -0.26392 | -0.23079
DCC | -0.2184 | -0.37972 | -0.6875 | -0.56976
0.47um
0.51um
0.64um
0.86um
1.6um
2.3um

## Slide 8: Application to RVS monitoring
Can we evaluate the response versus scan-angle (RVS) characteristics by using the “Moon chasing” events? Especially for EW direction.
The ratio of AHI obs and GIRO simulation has sometime (not always) unexpected variation.
Yu (2020) pointed that:
  Non-uniformity of the space count can affect a constant term of the calibration equation.
  Straylight can be also overwrapped the moon radiance.
AHI FoR
Earth edge
Lunar observations
Band5 (1.6μm)
  Reference: Yu, F., X. Wu, X. Shao, and H. Qian, “The East-West Response versus Scan-angle Performance of GOES-16/17 ABI Solar Reflective Bands”, CALCON, 2020
?
?
time
time
0450-0600 18 Sep. 2019
03:50-04:50 02 Feb. 2018
B01 AHI/GIRO
1.176
1.175
1.174
1.173
1.172
1.160
1.158
1.156
1.154
1.152
04:00
04:10
04:30
04:20
04:40
05:00
05:12
05:36
05:24
05:48

## Slide 9: Non-uniformity of the spacelook count?
Some of the irradiance ratio (AHI/GIRO) shows a periodic variation with 10 min cycle.
AHI computes offset term of the calibration equation based on a deep-space obs at the beginning (or end) of the full disk swath.
What if the observed the spacelook counts depend on North-South scan position?
AHI / GIRO
AHI irradiance
GIRO irradiance
time
Earth
Deep space 1
Deep space 2
…
Moon
C1
C2
C3
Deep space 3
C1
C2
C3
…
This is not corrected yet for AHI lunar cal work.
1.176
1.172
Calibration offset is updated in every FD swath.

## Slide 10: Typical observation “timeline”
Space obs(SP)
Lunar obs (R5)
[sec]
[sec]

## Slide 11: Straylight?
B01
AHI / GIRO
The ratio (AHI/GIRO) shows up-and-down pattern in some moon chasing events.
The averaged space counts (radiances) in each image show similar pattern to the ratio.
To remove the undesired radiance on the scans close to the Earth, the averaged contribution of the space radiance is subtracted from the moon irradiances.
The ratio based on the corrected irradiance shows more stable variation.
Average of deep space radiance
w/o correction
w/ correction
time
time
1.160
1.148

## Slide 12: Straylight?
The subtraction process looks effective, except for B03.
This approach can be promising to check the response-versus-scan characteristics.
The coherent noise reduction process is not applied to AHI/B03. It might be a potential reason of the fluctuation.
1.160
1.150
1.125
1.115
1.165
1.155
w/o correction
w/ correction
1.190
1.180
1.270
1.260
1.290
1.280
B01 (0.47um)
B04 (0.86um)
B03 (0.64um)
B02 (0.51um)
B06 (2.3um)
B05 (1.6um)
0450-0600 18 Sep. 2019
AHI / GIRO
AHI / GIRO

## Slide 13: Summary
Sensitivity trend based on the GIRO tool is consistent with other results.
“Moon chasing” event will be a good opportunity to evaluate RVS characteristics, if the straylight and the non-uniformity of the spacelook count (if exists) are corrected adequately.
Future issues:
  non-uniformity of the space count
  OFAR（B01-B03）
13
Acknowledgement
  The presentation by Dr. Yu in CALCON 2020 gave me good suggestions.

## Slide 14: Back up

## Slide 15: VIS/NIR on-board Calibration using Solar Diffuser (SD)
Quadratic calibration equation in “L1A (L1.0) equivalent data” processing
Robsn: Observed radiance
CAn: Raw digital count
Cspn: Deep space raw digital count
qn, mn: Coefficients
n: Detector ID
r : Scan mirror reflection coef.
q, f : Incidence angle to SM
qn: pre-launch test value
mn:
Pre-launch test value (until 7 June 2015)
Values based on solar diffuser (SD) observations (since 8 June 2015). SD observation is performed every 2 weeks
Csp: updated by deep space observation at each Full-disk swath
aa

## Slide 16: Advanced Himawari Imager (AHI)
Band | Central Wavelength [μm] | Spatial Resolution [km] | # of detectors (*) | Levels of digital count [bit]
1 | 0.47 | 1 | 676 (3) | 11
2 | 0.51 | 1 | 676 (3) | 11
3 | 0.64 | 0.5 | 1460 (3) | 11
4 | 0.86 | 1 | 676 (6) | 11
5 | 1.6 | 2 | 372 (6) | 11
6 | 2.3 | 2 | 372 (6) | 11
7 | 3.9 | 2 | 332 (6) | 14
8 | 6.2 | 2 | 332 (6) | 11
9 | 6.9 | 2 | 332 (6) | 11
10 | 7.3 | 2 | 332 (6) | 12
11 | 8.6 | 2 | 332 (6) | 12
12 | 9.6 | 2 | 332 (6) | 12
13 | 10.4 | 2 | 408 (6) | 12
14 | 11.2 | 2 | 408 (6) | 12
15 | 12.4 | 2 | 408 (6) | 12
16 | 13.3 | 2 | 408 (6) | 11
AHI Field of View Center (VNIR)
ITT EXELIS(2013): AHI-8 EQUIPMENT MANUAL 2
CALIBRATION AND ALIGNMENT HANDBOOK Rev. J
*Number of redundant detector columns per side

## Slide 17: Obs/GIRO for the moon chasing - 63 events in 5 years
X: Azimuth angle of a scan direction; Y: obs/GIRO, normalized to a value at the azimuth angle ~ 0deg.
w/o correction; w/ correction
B02
B01
B03
B05
B06
B04
1.002
0.996
1.002
0.996
1.006
0.996
1.003
0.997
1.004
0.996
1.006
0.996