## Slide 1: The New SCIAMACHY Lunar Dataset
M. Krijger (ESS), A. Dehn (ESA), S. Wagner (EUMETSAT), G. Lichterberg (DLR), A Kumar (DLR), B. Aberle (DLR), K Bramstedt (IUP)
Study funded by
Notes: The SCIAMACHY (SCanning Imaging Absorption spectroMeter for Atmospheric CartograpHY) instrument, operational from 2002 to 2012 aboard the Envisat satellite mission, was designed as an imaging spectrometer equipped with scanning mirrors. These mirrors facilitated the projection of observed light onto a slit, effectively splitting the light across thousands of wavelengths ranging from 240 to 2400nm. The versatility of the scanning mirrors allowed for diverse observations, including Earth nadir, limb, Moon, and Sun, captured at various times and viewing angles throughout the mission. The resulting dataset provided by ESA boasts exceptional attributes, including high spectral resolution, an extensive wavelength range, a lengthy time series, diverse viewing geometries, and the incorporation of solar irradiances. Refer to M. Krijger's other presentation for an in-depth exploration of this dataset. In a study funded by EUMETSAT, the initial version of the lunar model, LESSSR v1.0, was established using a preliminary version of the SCIAMACHY dataset. Notably, this model benefitted from the combination of high spectral resolution data and laboratory measurements of the reflectance properties of various lunar dust constituents, collectively referred to as RELAB, resulting in promising model outcomes. Subsequently, ESA made the decision to embark on a comprehensive recalibration of the raw lunar observations. In a new collaborative endeavor between ESA and EUMETSAT, EUMETSAT provided funding for a study aimed at incorporating this new dataset into the LESSSR model (v1.1). This effort included a meticulous assessment of uncertainties and an exploration of potential enhancements to the lunar model, with the overarching goal of jointly intercalibrating GOME-2 lunar measurements and further improving the LESSSR model. This presentation provides a comprehensive outline of the steps involved in the derivation of the LESSSR lunar model from the SCIAMACHY dataset, and a thorough analysis of uncertainties. Furthermore, we offer a preliminary comparative assessment of the LESSSR model alongside existing lunar models and measurements. We conclude by shedding light on the future steps and exciting model prospects within this collaborative project. The LESSSR model based upon the SCIAMACHY dataset of unique and high-quality lunar observations is slated for public use by EUMETSAT.

## Slide 2: SCIAMACHY on ENVISAT

## Slide 3: The instrument
Imaging spectrometer
Spatial dimensions through scan mirror(s):
  IFoV: 0.045 degrees by 1.8 degrees
Spectral dimension through 8-channel spectrometer, 8192 wavelengths:
  214 nm to 1773 nm
  1934 nm to 2044 nm
  2259 nm to 2386 nm
Nadir, Limb, solar occultation
  and lunar views
Many in-flight monitoring modes
Data provided by ESA

## Slide 4: SCIAMACHY

## Slide 5: SCIAMACHY viewing modes

## Slide 6: SCIAMACHY viewing modes

## Slide 7: Lunar phase angle coverage
Dedicated moon campaigns

## Slide 8: Lunar libration angle coverage

## Slide 9: SCIAMACHY Lunar Mode
Moon
IFOV
Similar for solar irradiance

## Slide 12: FDR4ATMOS: Convert to Reflectance
Wavelength [nm]
Reflectance as measured by SCIAMACHY
Account for scanning speed, duration, distance, slit size, etc

## Slide 15: Issue V10

## Slide 20
Full ESA investigation started

## Slide 21: Warning?
Second Mirror Angle
Due Orbital mechanics

## Slide 22: The Uncertainties
FDR4ATMOS NPL study:
  Absolute Uncertainty
    (Lunar) Radiance 1.5%-2.2%
    Solar Irradiances 2%-2.7%
    Correlated (due calibration distance uncertainty)
    (Lunar) reflectance 1.3-2%
  Relative Uncertainty (preliminary)
    (Lunar) Radiance 0.2%-0.5%
    Solar Irradiances 1.4-1.8%
    (Lunar) reflectance 1.4%-1.9%

## Slide 23: Future
Make available to public
  Official ESA release once LSICS format decided
  SCIAMACHY Lunar V10 (with issue)
Investigate Issue
  Reprocessing Mid 2024
   SCIAMACHY Lunar V10.1
Derive lunar model
   LESSR v1.1, v2.0 (presentation later)
Include with other lunar dataset
  GOME2 lunar dataset
  LIME lunar dataset
  Others?
   LESSR v3.0

## Slide 24: Conclusion
New SCIAMACHY data v10
Official release soon (pending LSICS format)
The Good
  Over 1100 geometries/measurements
  Hyperspectral 218-2386nm
  High relative accuracy
  On board solar irradiance measurement
The Bad
  Coupling mirror angle (calibration) and phase
  Degradation correction issue (patchable, investigation)
The Uncertainties
  Absolute/Relative <2%