## Slide 1: Introduction to the LSICS Development Session
Tom Stone – USGS

## Slide 2: LSICS Development — Overview
Motivation: replace GIRO for community access to the lunar cal reference
A proposed framework was presented at the GSICS 2023 Annual meeting
  an operational system to generate reference irradiances for Moon measurements
    inputs: date/time & location of Moon observations, and sensor spectral response
    outputs: model-generated spectral irradiance at the sensor bands
  modular construction, to allow plug-in modules for different lunar disk models
    initially an implementation of H. Kieffer’s SLIM algorithm
    implementing other models is enabled by standard module interface specifications
NOAA expressed support for developing this at the GSICS 2023 meeting
  resources have been provided — talks by Fred and Bikash later in this session
The project was named by vote (and discussion), July 2023
  the winner: Lunar Spectral Irradiance Calibration System (LSICS)
Community access to LSICS is intended
  repository and procedures are TBD

## Slide 3: Issues Leading to Initiating LSICS Development
The need for access to the lunar calibration reference (lunar model outputs)
a major issue discussed at the 1st GSICS Lunar Calibration Workshop, 2014
  different groups had replicated the ROLO model independently
  identified a need for consistent lunar model outputs among the users
  provided the rationale for EUMETSAT to release the GIRO to the community
    licensing agreement issue
access also was a driver for developing the Miller-Turner model (MT2009)
  designed for use to generate Earth night-side illumination by the Moon
  has some limitations in geometry coverage — no librations, initially no wax/wane diff
Recent lunar model development efforts
  LIME toolbox — (almost) completed; monolithic construction with GUI (Stefan’s talk)
  SLIM — need to translate from its native program language (= cost) to public domain
  other models that contributed to the comparison exercise — access ???

## Slide 4: Community Benefits Derived from Developing the LSICS
In the time since ROLO and GIRO were built, limitations have been found in the model-generated lunar irradiances:
  new lunar measurements indicate a 5-8% low bias (air-LUSI; Natalia’s talk)
  long time-series of instrument comparisons show residual libration patterns (e.g. VIIRS)
New lunar models are expected to improve the accuracy of lunar irradiance predictions
  absolute radiometry; phase and libration variations; spectral content
The new GSICS lunar cal system is intended to capture these improvements
  lunar model development is happening in several places
  it is important to build-in the ability to interchange the core disk-reflectance module
Inter-calibration consistency is increasingly recognized as essential for remote sensing for climate
  the Moon can provide exceptional cross-calibration consistency — all sensors view the same ultra-stable source; differences in lunar brightness are predicted by lunar models

## Slide 5
Ingest and Geometry Calculation Module
Operation: compute Lunar Observation Angle Set (LOAS)
• Phase angle (signed)
• Sub-solar longitude and latitude
• Sub-observer longitude and latitude
Intermediate Data Files
• Geometry: LOAS
• Spectral: SRF, std units
Lunar Disk Reflectance Module
Operation: compute lunar disk reflectance spectra
• set up basis functions
• reconstruct disk reflectance model
• compute model on operating wave- length set using LOAS parameters
Spectral Irradiance Module
Operation: produce model irradiances in sensor bands
• Convolve disk reflectance, solar irradiance and SRF
• Apply distance corrections
Model Definitions
• Operating wavelength set
• Basis function coefficients
Reference Spectra
• Lunar reflectance
• Solar Irradiance
Intermediate Data Files
• Operating wavelengths
• Disk reflectance spectra
Input Files
• Observation times
• Observer locations
• Sensor SRFs
Final Outputs
• Lunar spectral irradiances for input observations in sensor spectral bands
Framework flowchart from GSICS 2023 Annual meeting