## Slide 1: JiLin-1 space-borne lunar irradiance measurement and applications
4th Joint GSICS/IVOS Lunar Calibration Workshop,
4-8 December 2023, Darmstadt, Germany
Zhenhua Jing1, Xiuqing Hu2, Yang Wang3
1Nanjing University of Aeronautics and Astronautics (NUAA)
2National Satellite Meteorological Centre (CMA/NSMC)
3Shanghai Institute of Technical Physics (SITP)

## Slide 2: Outline
JiLin1 GP02 PMS lunar observations
Lunar observation applications
Informed machine learning for lunar reflectance simulation
Summary

## Slide 3: JiLin1-GP02 PMS
JiLin1(JL-1) GP02 (2019.1.21—) is a commercial small satellite
  Launched on January 21, 2019 (GP01 & 02)
  Operated by the commercial corporation Chang Guang Satellite Technology Co. Ltd.
  Key payload for lunar observation: panchromatic multispectral sensor (PMS2)
  No on-board calibration device
Parameter | Specification
Launch time | 2019.01
Sensor | PMS、SWIR、MWIR、LWIR
Orbit type | sun-synchronous orbit
Mean altitude | 528 km
Orbital period | 95.2 minutes
Inclination | 97.51 degrees
Local time | 10:00 AM
Repetition period | 28 days

## Slide 4: JiLin1-GP02 PMS
Parameter | Specification |  | 
Central wavelength (nm) | B0: 624.08 B1: 415.21 B2: 444.69 B3: 483.36 B4: 559.61 B5: 656.75 B6: 836.14 | B7: 487.41 B8: 619.41 B9: 660.75 B10: 705.46 B11: 742.51 B12: 784.49 | B13: 863.44 B14: 664.46 B15: 681.94 B16: 754.51 B17: 758.87 B18: 941.43 B19: 1013.97
IPOV (μrad) | 9.23 | 18.46 | 36.92
Ground resolution (m) | 5 | 10 | 20
A/D conversion bits | 12 | 14 | 16
Spatial resolution on the Moon (km) | ~3.5 (~1000 pixel for moon) | ~7 | ~14
  Panchromatic and multispectral imager (PMS)
  Multi-band imager with 19 spectral bands (415 -1014 nm)
  Observing the target at three resolutions, and rational polynomial coefficients (RPCs) are used to describe the ground-to-image relationship

## Slide 5: PMS lunar observations
  Specially designed payload imaging parameters
  Regular lunar observations for PMS2 begin in November 2019 (over the Pacific Ocean in the ascending ground shadow region)
  JL1GP02 Moon-sweeping mission was customized to capture the lunar disk directly
  maneuver angular velocity
:

## Slide 6: PMS lunar observations
JILIN-1 GP02 PMS2/B4 lunar image (559.61nm) September 2020
STK simulation

## Slide 7: Lunar observation applications
  Geographic (selenographic) position determination
  For JiLin-1 GP02 PMS lunar observation
  Expandable to observations on other platforms
  Radiometric calibration
  Informed machine learning for lunar reflectance simulation

## Slide 8: Geolocation of lunar observations
Interior Orientation Model:
Rigorous Sensor Model:
Line-of-sight vector in camera coordinate system
Mean-Earth/mean-rotation system (most lunar cartographic products refer to the MER frame not principal axis (PA) frame )
References
Z.H. Jing, X.Q. Hu, S. Li, H.B. Pan. Geolocation of Lunar Observations with JiLin-1 High-resolution Optical Sensor. IEEE TGRS, 2023
PMS2 observation geometry
light transmission time and stellar aberration correction

## Slide 9: Geolocation of lunar observations
simulation with SP model cube
observation
Significant initial misalignment, and no clear trend

## Slide 10: Correction of Pointing
  Prior and posterior equivalent attitude compensation：
  Prior correction: direct calculation of the image space deviation without positional solving (for translation errors)
  Post-correction: geometric solving using linear array CCD (translation and rigid transformation errors)
linear array CCD model
area array CCD model
simulated images
observed images
Post-correction
collinearity equation
Moon vector measurement equation
Prior correction

## Slide 11: Geolocation of lunar observations
B4_20200407173023_200024104_img
B4_20200407173023_200024104_img_grid
After correction, geo-referenced images are acquired directly

## Slide 12: Error assessment scheme
angle +7.11°
observed image
simulated image
LROC/WAC
image matching
angle -29.69°
LROC/WAC
Orthographic projection centered at 0° N, 0° E
reference image
  Create a corresponding simulated image for each observed image and match it to the reference image

## Slide 13: Geometric Accuracy of PMS Bands
  The average geometric deviation for different resolutions is ~0.5 pixels
  Errors between lunations are fairly smooth, very small fluctuations

## Slide 14: Comparison with two lunar craters
Site | Diameter (km) | Longitude (deg) | Latitude (deg) | Depth (km)
Plato | 100.68 | -9.38 | 51.62 | 1.8
Tycho | 85.29 | -11.22 | -43.31 | 4.8
Two very prominent craters on the near side of the Moon as a reference
reference position by IAU
40 × 40 area
50 × 50 area
Local areas also provide good positional accuracy

## Slide 15: Geolocation for different views
observations from different platforms
  Rigorous sensor model relies on interior and exterior orientation elements, considering the following observed image features
  Images observed from different platforms differ due to differences in sampling mechanisms
  But all can be related to the nominal image
Ground-based view (to be tested):
libration + position angle
Spaced-based view (tested):
libration + position angle + scanning direction
nominal image
image with libration & position angle
scanning in different directions

## Slide 16: Radiance target
References
Pieters C. M., et al. Lunar international science coordination/calibration targets (L-ISCT). Advances in Space Research, 2008
Besse S., et al. A visible and near-infrared photometric correction for Moon Mineralogy Mapper (M3). Icarus, 2013.
  Lunar international science coordination/calibration targets
  Eight lunar areas, each ~200 km in diameter, for the Lunar Orbiter
  Spectra of different regions of the Moon can also serve as a reference for Earth observation satellites
  M3 imagery covers almost the full Moon, and extensive comparisons have been made
  The photometric correction data for M3 was obtained from OP2C1, mainly for highland material

## Slide 17: Radiance calibration
Example: B4-559.61 nm of PMS2 (preliminary)
reference from M3 OP2C1 data
Observations are automatically positioned and extracted
based on co-linear equation
References
Besse S., et al. A visible and near-infrared photometric correction for Moon Mineralogy Mapper (M3). Icarus, 2013.
Besse S., et al. One Moon, many measurements 2: Photometric corrections. Icarus, 2013.
OP2C1
AP16 site
reference spectrum (i, e, α=30, 0, 30°)
area 2 reflectance used
Comparison using radiance

## Slide 18: Observed irradiance
based on scanning signal features (dynamic)
Ellipse fitting rather than thresholds
  Two key points for PMS observed irradiance

## Slide 19: Results with GIRO irradiance
  Visible channel performance of PMS monitored using lunar data from November 2019 to March 2023
  Degradation in two bands, B3 and B4, was observed using GIRO simulations
    The irradiance comparison trend for band 4 is in good agreement with the radiance comparison

## Slide 20: Informed machine learning application
  Pure data-driven deep learning model
  Conventional machine learning starts with a specific problem with training data and can be expressed as a regression problem
  Lack of understanding of the patterns presented by the data, as well as knowledge
  Predictions may not be consistent with the above properties
  Status:
  Not enough new measurements with high-accuracy
  A lot of observations have been accumulated
  Smoothness properties of the lunar reflectance spectrum are known

## Slide 21: Informed machine learning application
  Two types of a priori knowledge
  GIRO simulation results
  Monotonicity of the lunar reflectance spectrum
  The last loss term quantifies the violation of a given prior knowledge
    given by the lunar spectral features, avoiding the irregular structure presented by the direct simulation of ROLO
  The knowledge loss term depends only on input features and learned function and can be evaluated on unlabeled datasets, i.e., no actual observations are required
Data + Prior knowledge

## Slide 22: Informed machine learning application
  Training using GLIS ground-based data and model simulations
  GLIS: 3265 irradiance observations (2017-2018, part of the data)
  Spectral range: 400-1000 nm (259 channels)
  Features: wavelength, photometric angles, GIRO simulations
  Unlabeled datasets for knowledge loss term
  Unlabeled: 400, 673 unlabeled data, 1813 dates (December 2015-April 2019)
  Wavelength grid: 300-2500 nm, 10 nm steps
labeled
unlabeled

## Slide 23: Informed machine learning application
  Training using GLIS ground-based data and model simulations
  Predicted reflectance is close to model-smoothed reflectance features
  Results at atmospheric absorption bands are not good
Lunar reflectance (obs, GIRO model and pediction)

## Slide 24: Informed machine learning application
Lunar reflectance (measurements vs GIRO-black line)
  Knowledge-based loss term does not constitute a strong constraint
  Embedding spectral features into neural network design (strong constraint)
    Black-box architecture does not change its nature, still produces outputs that violate certain features
  Adding higher precision data as a constraint (e.g., FY-3G HAOC, etc.), not added currently
Consistency is within 10% between the two observations, except for some significant deviations
Bias pattern varies with wavelength and moon phase
The HAOC data is still being processed and analyzed

## Slide 25: Summary
  Combined irradiance and radiance calibration
  Both methods show good agreement and need to be further processed and analyzed
  Radiance calibration or model contributes to photometric correction studies in lunar science
  Lunar calibration is very useful for commercial satellites, JiLin-1 is observing the Moon frequently
  Data- and prior knowledge-driven neural network design
  Using multiple calibration results and instrument maintenance activities to obtain consistent GLIS datasets (reprocessing)
  Training on clean dataset, FY-3G HAOC … data for constraint and validation

## Slide 26
Thank you for your attention!