## Slide 1
Status of the S3-OLCI missions using lunar calibration
S. Wagner, V. Debaecker*, M. De Bartolomei, O. Henriquez**, M. Neneman, OPS team
* Telespazio support
** CS support
4th Joint GSICS/IVOS Lunar Calibration Workshop

## Slide 2: Sentinel-3 OLCI
OLCI channels

## Slide 3: Sentinel-3 OLCI
Source : ESA web site
Source : ESA web site
Across track = 740 detectors per camera
Imaging CCD = Spatial x Spectral content
Digital processing  21 bands (+ 1 smear band) over the spatial dimension

## Slide 4: Sentinel-3 lunar manoeuvres - background
  First acquisition with Camera#4 on OLCI-B in 2018 during commissioning
  Purpose : assessment of the stray-light correction performances.

## Slide 5: Sentinel-3 lunar manoeuvres - background
Roll angle = changing parameter to adjust the Moon position across track ( camera + position in the camera)
Maximum negative roll rotation allowed = -165 degrees  star trackers not all pointing at the Earth.
Location of the Moon across track  centrered
Moon phase |g|  [5,8] deg
Cal window start + 20s < Moon < Cal window end – 20s for SL analysis

## Slide 6: Sentinel-3 lunar manoeuvres – background + constrains
Example of ground track showing the full arc. In blue: yaw; in yellow: additional time (~1 minute before and 18 minutes after) in which the spacecraft will be in Geodetic pointing mode without yaw-steering (the same mode as used during In-Plane manoeuvres).

## Slide 7: Sentinel-3 lunar manoeuvres
Extract from the original image
ACT
ALT

## Slide 8: Sentinel-3 lunar manoeuvres - background
Outcome of 2018 manoeuvre led to:
  One manoeuvre with S3A in 2020 (while in OPE) for Camera#4
  Successful execution of inter-leaved monthly manoeuvres in 2022 for each camera of OLCI-A and OLCI-B
  Continuation since Nov 2022 of those monthly manoeuvres with Camera#4
2022 acquisition campaign = anchor points (snapshots):
  Stray light correction performance assessment
  Inter-band / inter-camera radiometric performance assessment
Routine acquisitions with Camera#4 = regular assessment
  Radiometric stability assessment (including inter-band)
  Inter-calibration

## Slide 9: OLCI lunar observations
Dataset:
  Camera#4 OLCI-B in 2018 (commissioning)
  Camera#4 OLCI-A in 2020 (during operations)
  One acquisition per camera with OLCI-A + OLCI-B in 2022
  Routine monthly observations for Camera#4 with OLCI-A and B, since September 2022
  Phase is ~ 6.5 deg +/- 2 deg (but first observations with negative phase)
Data processing:
  From Level 0 to Level 1 breakpoints  IPF offline
  Lunar data extraction + radiometric assessment
   EUMETSAT MICMICS prototype
Lunar irradiance:
Two parameters to be estimated as accurately as possible:
  The oversampling factor OSF (which may vary in time)
  The pixel solid angle i (which can vary from pixel to pixel)
Offset correction  average value over deep space subtracted to the radiance image

## Slide 10: MICMICS Workflows
Instruments
Instruments
Lunar Calibration
Desert Calibration
DCC Calibration
Lunar Inter-Calibration
Inter-Calibration Blender
DCC Inter- Calibration
Rayleigh Calibration System
Rayleigh Inter-Calibration System
Imager-Hyperspectral Inter-Calibration
NWP Calibration
Imager-Imager Inter-Calibration
ICBS
IHICS
IIICS
NWPC
Ray-Matching Inter-Calibration System
NWP Inter-Calibration
NWPIC
DCC Extraction Module
Lunar Extraction Module
DECS
DCCICS
DCCCS
LCS
LICS
RAYMICS
RAYCS
RAYICS
DCCXTRM
LXTRM
MICMICS
CPMs
VIS/NIR channels
MSG SEVIRI VIS/NIR
S3
SLSTR & OLCI VIS/NIR
MTG LI VIS
EPS AVHRR VIS/NIR
EPS-SG 3MI VIS/NIR
MTG FCI VIS/NIR
Thermal channels
MSG SEVIRI IR
MTG FCI IR
S3 SLSTR IR
EPS AVHRR IR
EPS-SG VII IR
EPS-SG MWI/ICI MW
CO2M
CLIM & MAP
EPS-SG VII VIS/NIR
Pre-Colocation Tool
Colocation Tool
Subsetter Tool
Data-Fusion Tool
SUBTL
DFTL
PCOLT
COLT

## Slide 11: OLCI lunar observations - oversampling
Ellipse fitting
  Calculation of the pointing angular rate on the Moon
    ALT IFOV Moon = Pointing Angular Rate [deg/sec] * Sampling Time ([sec])
    Oversampling = ALT IFOV Moon / ALT IFOV Earth

## Slide 12: Relative biases with respect to GIRO + LIME
All observations are included (i.e. all cameras) positive and negative lunar phase angles
Models:
GIRO = GSICS Implementation of the ROLO model – EUMETSAT
LESSSR = Lunar Extended Satellite Simulation Solar Reflectance – EUMETSAT (with support from M. Krijger - ESS)
LIME = Lunar Irradiance Model ESA. Courtesy S. Adriaensen – OPT-MPC/VITO
Results:
Larger biases with respect to the GIRO than to the LIME.
OLCI-A and OLCI-B results consistent with each other
GIRO results more stable in time than LIME results
Larger variability + larger biases for the LESSSR

## Slide 13: Temporal stability
Only Camera#4 results with positive lunar phase are considered (routine monitoring)
 Reference measurement = first measurement with Camera#4 and positive phase (09/2022 for OLCI-A and 10/2022 for OLCI-B)
Results:
Between -0.5 and +0.5% variability in time for S3A
Even better for OLCI-B, except an out-of-family event with the observation from October 2023  Requires further investigation.

## Slide 14: Difference between OLCI-A and OLCI-B
Top panel:
Mean bias in irradiance between observations and models.
Error bars = standard deviation over the complete set of measurements
Bottom panel:
Difference between OLCI-A and OLCI-B varies spectrally between ~2% and ~1%
Sun glint results : courtesy OPT-MPC/VITO

## Slide 15: Issue with the LESSSR applicator – work in progress
S3A – Oa01
Seasonal effect in the LESSSR results
Introduces strong variability
Seen in all bands
Under investigation
Similar effect on SEVIRI time series
Seen in all bands
Rescaling with the distances?

## Slide 16: Conclusions and future work
Measurements to continue in 2024, on a monthly basis for monitoring purposes
  Radiometry  lunar results complement the other monitoring tools
  They confirm the temporal stability of the individual channels and of the inter-band
  Need to investigate the out-of-family results for October 2023
  We will also expand the analysis to the reflectance domain
  Further investigate the implementation of the LESSSR applicator  impact not only OLCI
  Development of an lunar data extraction module in our MICMICS system to process SLSTR lunar observations (nadir view) + monitoring of radiometric performances of S1 to S6 using GIRO + LESSSR
  Plan for changing the solar irradiance spectrum to TSIS in GIRO and LESSSR (currently Wehrli)
ESA + MPC:
  Regular technical meetings to discuss progress / status on lunar work (straylight + radiometry)

## Slide 17
Thank you!
Questions are welcome.

## Slide 18
Back-up slides