## Slide 1: Radiometric Performance of Himawari-8/-9 AHI VNIR Bands Using Lunar Calibration
TAKAHASHI Masaya
Meteorological Satellite Center of Japan Meteorological Agency

## Slide 2: Contents
Introduction
  JMA Activities Using Lunar Observation Data
  Himawari-8/-9 Mission Overview
  AHI Lunar Observation
AHI Radiometric Performance by Lunar Calibration
  Lunar Irradiance Measurements
  Lunar Calibration Results Using GIRO
Summary and Future Plans
  Himawari-10 Introduction

## Slide 3: Introduction – JMA Activities Using Lunar Observation
Over 40-y history of GEO satellites operation in Japan
Use of the Moon for evaluating radiometric performance of the GEO imagers
  Started in early 2010s for GMS-5 and MTSAT-2
  Expanded application area for Himawari-8/-9
Past activities presented at the Lunar Calibration Workshops
  1st LCWS (2014, M. Takahashi)
    GMS-5 and MTSAT-2 Lunar Calibration
  2nd LCWS (2017, M. Takahashi)
    Himawari-8/AHI Lunar Calibration, AHI Inter-calibration with Aqua/MODIS, and MTF evaluation
  3rd LCWS (2020, A. Okuyama)
    Himawari-8/AHI Lunar Calibration, including potential use for evaluating RVS, detector response uniformity, and straylight
  4th LCWS (2023)
    Himawari-8/9 /AHI Lunar Calibration (this talk)
Satellite | Operation Period
GMS | 1978 – 1981
GMS-2 | 1981 – 1984
GMS-3 | 1984 – 1989
GMS-4 | 1989 – 1995
GMS-5 | 1995 – 2003
GOES-9* | 2003 – 2005
MTSAT-1R | 2005 – 2010
MTSAT-2 | 2010 – 2015
Himawari-8 | 2015 – 2022
Himawari-9 | 2022 – 2029
* Back-up operation of GMS-5 w/ GOES-9 by NOAA/NESDIS

## Slide 4: Himawari-8/-9 Mission Overview
Himawari-8
  Advanced Himawari Imager (AHI): 16-band VIS/IR imager
    Identical specification to AHI on Himawari-9
  Operation: 2015-07-07 to 2022-12-13
    Currently in-orbit standby operation (backup of Himawari-9)
Himawari-9
  Switchover of operation from Himawari-8 on 2022-12-13, after ~2 months parallel observation with Himawari-8
    To be operated until JFY2029
Himawari-8/-9 geostationary positions: ~140.7E

## Slide 5: Himawari-8/-9 AHI
16 spectral bands (5 similar spectral range in VNIR among AHI/ABI/FCI)
Observation by 2 independent (EW and NS) scan mirrors
Onboard calibration
  Solar diffuser (SD) and blackbody for VNIR and IR bands
  SD obs: twice / month, but nominal calibration slope (gain) is not updated
    Himawari-8: calibration trend is estimated on annual basis and included in HSD (L1b equiv. data) as the trend correction info
 | B01 | B02 | B03 | B04 | B05 | B06 | B07 | B08 | B09 | B10 | B11 | B12 | B13 | B14 | B15 | B16
Central wavelength [μm] | 0.47 | 0.51 | 0.64 | 0.86 | 1.6 | 2.3 | 3.9 | 6.2 | 6.9 | 7.3 | 8.6 | 9.6 | 10.4 | 11.2 | 12.4 | 13.3
Spatial resolution at SSP [km] | 1 | 1 | 0.5 | 1 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2
# of detectors for N-S direction | 676 | 676 | 1460 | 676 | 372 | 372 | 332 | 332 | 332 | 332 | 332 | 332 | 408 | 408 | 408 | 408
Wavelength [μm]
Wavelength [μm]

## Slide 6: AHI Observation Repeat Cycle
Region 5 (1000 x 500 km every 30 sec) is used for lunar observation.
Full Disk Observation
every 10 min. (23 swaths)
Region 1
2000 x 1000km
(NE Japan)
Every 2.5 min.
Region 2
2000 x 1000km
(SW Japan)
Every 2.5 min.
Region 3
1000 x 1000 km
(Target Area)
Every 2.5 min.
Region 4
1000 x 500 km
(Landmark Area)
Every 30 sec.
Region 5
1000 x 500 km
(Landmark Area)
Every 30 sec.
Pre-defined area
Flexible observation area

## Slide 7: AHI Lunar Observation
ONE scan to observe the Moon
  1 obs. / 30 sec using Region 5 (1000 x 500 km over the Earth)
  All phase angle scenes [-180 to +180 deg] are collected as much as possible, based on the Moon position prediction
Earth disk
AHI FoR
Himawari-8/AHI
(Mar. 2015 – Nov. 2022)
~75000 Obs.
(~7.5 years)
Himawari-9/AHI
(Aug. 2022 – Oct. 2023)
~12000 Obs.
(~15 months)
B01 (0.47μm)
B02 (0.51μm)
B03 (0.64μm)
B04 (0.86μm)
B05 (1.6μm)
B06 (2.3μm)
2015-08-01T03:03:26Z (phase angle: 10.5 deg)
Earth disk
AHI FoR
Phase
Angle
[deg]

## Slide 8: Total Lunar Eclipse
Himawari-8/AHI observation on 2015-09-28
  B05 (1.6 μm): 0.0 – 0.3 in albedo
  B07 (3.9 μm): 300 – 400 K
B05 (1.6 μm)
B07 (3.9 μm)
AHI FoR
Earth edge
Lunar observations
B05 (1.6 μm)
B07 (3.9 μm)
1 day before the eclipse (2015-09-27)
The Moon locations on 2015-09-27
~355 K
~250 K

## Slide 9: AHI Radiometric Performance by Lunar Calibration (GIRO)
AHI lunar observation data used in this study
Himawari-8/AHI (H-8)
  Jul. 2015 – Dec. 2022 (~7.5 years)
  ~30000 Moon observations for GIRO
Himawari-9/AHI (H-9)
  Oct. 2022 – Oct. 2023 (13 months)
  ~4000 Moon observations for GIRO

## Slide 10: AHI Lunar Irradiance Measurement
Moon pixel selection
  Based on digital count (DC) threshold
  Calibrated DCs are used
Quadratic calibration equation for AHI VNIR bands
  Quadratic term (no update): pre-launch determined value
  Slope (no update)
    H-8: average of SD obs before operation start
    H-9: pre-launch determined value corrected by SD obs
  Offset (update every full-disk swath): from deep space obs
Oversampling factor and sample solid angle
  Constant, derived from angular sample distance and iFoV
Lunar irradiance ratio normalized by the first result is used in this study
  To cancel out the uncertainties of oversampling factor and sample solid angle
Ω: sample solid angle
Radiancei,j : calibrated radiance at (i,j) image coordinate

## Slide 11: Phase Angle vs. Normalized ΔIrr (VIS)
H-8
B01 (0.47 μm) B02 (0.51 μm) B03 (0.64 μm)
Phase Angle [deg] Phase Angle [deg] Phase Angle [deg]
Phase angle dependence is seen in all VIS bands
  Root cause is still under investigation (lunar image processing may need to be revisited)
Spread of ΔIrr at a certain phase angle in H-8 show instrument response degradation
GOES-16/ABI Ch02 (0.64 μm) (Basnet et al., 2023)
H-9
Normalized ΔIrr Normalized ΔIrr
B01 (0.47 μm) B02 (0.51 μm) B03 (0.64 μm)

## Slide 12: Phase Angle vs. Normalized ΔIrr (NIR)
B04 (0.86 μm) B05 (1.61 μm) B06 (2.25 μm)
Phase Angle [deg] Phase Angle [deg] Phase Angle [deg]
H-8
Normalized ΔIrr Normalized ΔIrr
H-9
B04 (0.86 μm) B05 (1.61 μm) B06 (2.25 μm)
GOES-16/ABI Ch03 (0.87 μm), Ch05 (1.61 μm), and Ch06 (2.25 μm) (Basnet et al., 2023)
Phase angle dependence of AHI VNIR bands is good agreement with GOES-16/ABI
~15%
~10%
15%
10%

## Slide 13: Calibration Trend Estimation
Phase Angle [deg]
Normalized ΔIrr
Normalized ΔIrr (%)
* First result is scaled to 0%
Phase angle vs. normalized ΔIrr for H-8 B01 (0.47 μm)
Phase Angle Range [deg] | Trend Estimation (95% Conf. Intvl) [%/yr]
[-92, 92] | -0.38 (±0.0027)
[70, 90] | -0.45 (±0.0049)
[50, 70] | -0.39 (±0.0038)
[30, 50] | -0.40 (±0.0039)
[10, 30] | -0.35 (±0.0039)
[-10, 10] | -0.38 (±0.0041)
[-30, -10] | -0.34 (±0.0031)
[-50, -30] | -0.38 (±0.0029)
[-70, -50] | -0.39 (±0.0038)
[-90, -70] | -0.42 (±0.0058)
AHI VNIR bands’ calibration trend is estimated using Normalized ΔIrr (H-8 B01 in this slide)
  Trends from limited phase angle data (20-deg range) show good agreement with that by all applicable data (-92 to 92 deg)
  In the following slides, all VNIR bands’ trend is derived from all applicable data
Time series of normalized ΔIrr for H-8 B01 (0.47 μm)

## Slide 14: H-8 Calibration Trends (~7.5 years)
Lunar : −0.38 ± 0.003 [%/yr]
Solar : −0.43 ± 0.008 [%/yr]
Raymatch: −0.35 ± 0.016 [%/yr]
RTM : −0.42 ± 0.025 [%/yr]
Lunar : −0.45 ± 0.004 [%/yr]
Solar : −0.32 ± 0.008 [%/yr]
Raymatch: −0.44 ± 0.016 [%/yr]
RTM : −0.49 ± 0.026 [%/yr]
Lunar : −0.70 ± 0.003 [%/yr]
Solar : −0.50 ± 0.007 [%/yr]
Raymatch: −0.64 ± 0.014 [%/yr]
RTM : −0.72 ± 0.027 [%/yr]
Lunar : −0.12 ± 0.009 [%/yr]
Solar : −0.03 ± 0.010 [%/yr]
Raymatch: 0.19 ± 0.017 [%/yr]
RTM : −0.25 ± 0.039 [%/yr]
Lunar : −0.10 ± 0.006 [%/yr]
Solar : −0.06 ± 0.011 [%/yr]
Raymatch: −0.21 ± 0.022 [%/yr]
RTM : −0.16 ± 0.030 [%/yr]
Lunar : −0.63 ± 0.002 [%/yr]
Solar : −0.57 ± 0.008 [%/yr]
Raymatch: −0.60 ±0.011 [%/yr]
RTM : −0.70 ± 0.025 [%/yr]
B01 (0.47 μm) B02 (0.51 μm) B03 (0.64 μm)
B04 (0.86 μm) B05 (1.61 μm) B06 (2.25 μm)
Similar trends among lunar cal by GIRO (plots in lightblue), solar cal using SD, ray-matching vs. S-NPP/VIIRS, and vicarious cal by RT simulation using Aqua/MODIS
  0.4–0.7% per year degradation in 0.47 to 0.86 μm bands, little change in 1.61 and 2.25 μm bands
  Lunar & solar cal: small uncertainties in trend estimation (± XX in legend shows 95% confidence interval)
Relative Calibration Bias (%)
Relative Calibration Bias (%)
Note: first results are scaled to 0%

## Slide 15: H-9 Calibration Trends (13 months)
Lunar calibration results are closer to ray-matching results
To derive more reliable results, further samples and/or improvement of the calibration method needed in all methods
  E.g., H-9 solar cal results show larger variations compared with H-8 (root cause has yet to be found)
Lunar : −0.83 ± 0.06 [%/yr]
Solar : −1.67 ± 0.80 [%/yr]
Raymatch: −1.14 ± 0.22 [%/yr]
Lunar : −0.68 ± 0.08 [%/yr]
Solar : −1.14 ± 0.72 [%/yr]
Raymatch: −0.71 ± 0.18 [%/yr]
Lunar : −0.86 ± 0.08 [%/yr]
Solar : −1.29 ± 0.60 [%/yr]
Raymatch: −1.07 ± 0.17 [%/yr]
Lunar : −0.91 ± 0.18 [%/yr]
Solar : −0.41 ± 0.37 [%/yr]
Raymatch: 0.75 ± 0.17 [%/yr]
Lunar : −0.54 ± 0.12 [%/yr]
Solar : −0.35 ± 0.33 [%/yr]
Raymatch: 0.55 ± 0.17 [%/yr]
Lunar : −1.36 ± 0.03 [%/yr]
Solar : −1.46 ± 0.50 [%/yr]
Raymatch: −1.05 ± 0.13 [%/yr]
B01 (0.47 μm) B02 (0.51 μm) B03 (0.64 μm)
B04 (0.86 μm) B05 (1.61 μm) B06 (2.25 μm)
Relative Calibration Bias (%)
Relative Calibration Bias (%)
Note: first results are scaled to 0%

## Slide 16: Summary and Future Plans
Radiometric performance of AHI VNIR bands were validated using GIRO
  Target bands: 6 VNIR bands (0.47, 0.51, 0.64, 0.86, 1.6, 2.3 μm)
  Validated period: ~7.5 years (Mar. 2015 to Dec. 2022) for Himawari-8 and 13 months (Oct. 2022 to Oct. 2023) for Himawari-9
Calibration trends estimated by GIRO are good agreement with other calibration methods (on-board solar cal, ray-matching, and vicarious cal) for Himawari-8
  Further samples and/or improvement of the calibration method needed in particular for Himawari-9
  AHI lunar image processing will be revisited
  New lunar irradiance model solving phase angle dependence is waited
Preparation for JMA’s future GEO mission: Himawari-10 (introduction in next slides)
  Update/improvement of AHI lunar calibration approach would be applicable to Himawari-10 VIS/IR
  Application of the Moon data for other purposes (e.g, MTF, straylight) would also be investigated.

## Slide 17: Future Mission: Himawari-10
Himawari-10 Perspective Image
© Mitsubishi Electric

## Slide 18: Himawari-10 Overview
JMA contracted manufacturing of Himawari-10 in March 2023, with initiation of operation scheduled for FY 2029.
Design lifetime
  10-y observation + 5-y on-orbit storage
Geostationary position
  At around 140.7 deg. E
Missions
  Geostationary HiMawari Imager (GHMI)
  Geostationary HiMawari Sounder (GHMS)
  Data Collection System
  Space Environment Suite
    Proton & electron flux observation, as a government furnished equipment by NICT
Satellite Design | 
Spacecraft | MELCO standard DS2000 bus
Mass (approx.) | 2.4 t (dry), 6.1 t (with propellant)
Size (approx.) | 4 m x 3 m x 6 m (folded), 11 m (deployed)
Design life | ≥ 15 years (mission period ≥ 10 years)
Communications | Ka-band: Mission data downlink Ku-band: TT/C uplink & downlink UHF-band: DCP uplink
Satellite Outline
GHMI
GHMS
Space Environment Suite

## Slide 19: Geostationary HiMawari Imager (GHMI)
L3Harris’s new 18-band VIS/IR imager based on the same concept with its GeoXO Imager (GXI) selected by NASA
Observing sequence & band configuration changed for Himawari-10
Values in the tables show JMA requirements
 | Center Wavelength [µm] | Bandwidth [µm] | Spatial Resolution at Nadir [km]
VIS | 0.46 - 0.48 | ≤ 0.07 | ≤ 1
 | 0.54 - 0.56 | ≤ 0.05 | ≤ 1
 | 0.63 - 0.65 | ≤ 0.12 | ≤ 0.5
NIR | 0.85 - 0.87 | ≤ 0.06 | ≤ 1
 | 1.375 - 1.385 | ≤ 0.04 | ≤ 2
 | 1.60 - 1.62 | ≤ 0.08 | ≤ 2
 | 2.24 - 2.27 | ≤ 0.06 | ≤ 2
IR | 3.75 - 3.95 | ≤ 0.50 | ≤ 1
 | 5.10 - 5.20 | ≤ 0.20 | ≤ 1
 | 6.05 - 6.45 | ≤ 1.20 | ≤ 2
 | 6.90 - 7.00 | ≤ 0.50 | ≤ 2
 | 7.27 - 7.43 | ≤ 0.60 | ≤ 2
 | 8.44 - 8.76 | ≤ 0.50 | ≤ 2
 | 9.55 - 9.70 | ≤ 0.50 | ≤ 2
 | 10.3 - 10.5 | ≤ 0.90 | ≤ 2
 | 11.1 - 11.3 | ≤ 1.00 | ≤ 2
 | 12.25 - 12.55 | ≤ 1.20 | ≤ 2
 | 13.2 - 13.4 | ≤ 0.70 | ≤ 2
Observing Area | Minimum Coverage | Interval
Full Disk |  | 10 min
Japan | EW 2500 km x NS 2000 km | 2.5 min
Target Area1 | EW 1000 km x NS 1000 km | 2.5 min
Target Area2 |  | 2.5 min
Target Area3 |  | 2.5 min
Target Area4 |  | 2.5 min
Target Area5 (*) | EW 1000 km x NS 500 km | 30 sec
GHMI Spectral Band Characteristics
GHMI Observing Area & Interval
*Mainly used for CAL/VAL activities

## Slide 20: Geostationary HiMawari Sounder (GHMS)
L3Harris’s new infrared FTS based on the same concept with its GeoXO Sounder (GXS) proposed to NASA
Observing sequence changed for Himawari-10
Values in the tables show JMA requirements
GHMS Spatial & Spectral Characteristics
GHMS Observing Area & Interval
Observing Area (minimum coverage) | Interval
Sounding Disk (LZA ≤ 60 deg) | 60 min
Japan (EW 2500 km x NS 2000 km) | 15 min*
Target Area (EW 1000 km x NS 1000 km) | 15 min
Spatial (horizontal) Resolution |  | ≤ 4.2 km
Spectral Coverage | LWIR | 680 - 1095 cm-1 (14.7 - 9.13 µm)
 | MWIR | 1689 - 2250 cm-1 (5.92 - 4.44 µm)
Spectral Resolution (FWHM) |  | ≤ 0.754 cm-1
Spectral Sampling Distance |  | ≤ 0.625 cm-1
* Sounding Disk observation over Japan area is regarded as one of the "Japan" observations in the 60-min repeat cycle (i.e., three "Japan" observations to be conducted in 60 minutes).

## Slide 21
Thanks for your attention!

## Slide 22: Potential Root Causes for Phase Angle Dependence in AHI VIS Bands
Lack of radiance integration over dark portion of the Moon
  Current calibrated DC thresholds (~30) are higher than zero radiance DC (20) to avoid the following noise
    Out-of-Field Anomalous Response (Griffith 2017) is seen AHI B01 (0.47), B02 (0.51) and B03 (0.64)
    Coherent Noise
Radiance integration of over navigated lunar area + pixels exceed the higher DC threshold is tested
Out-of-Field Anomalous Response
(color scale: 0.1–30% of reflectivity)
H-8 B01 (0.47 μm)
2016-08-19
H-9 B01 (0.47 μm)
2023-01-13T08:00:31Z
DC threshold = 20
DC threshold = 33 (current threshold)
Light blue: < DC threshold
Black/White: >= DC threshold
Yellow: navigated lunar area
Black/White (threshold=33) and yellow pixels are used for irradiance calculation

## Slide 23: Preliminary Result on Update of Moon Pixel Selection
Phase Angle [deg]
Phase Angle [deg]
Relative Calibration Bias (%)
Relative Calibration Bias (%)
Normalized ΔIrr
Normalized ΔIrr
Normalized ΔIrr
Normalized ΔIrr
Phase Angle [deg]
Phase Angle [deg]
H-8 B01 (0.47 μm)
H-8 B01 (0.47 μm)
H-8 B06 (2.25 μm)
H-8 B06 (2.25 μm)
Radiance integration over the dark portion of the Moon reduce the phase angle dependence (but too much?) – Further investigation is planned. ce DC (20) to avoid the
DC threshold (=33) only
Navigated lunar pixels + DC threshold (=33)
DC threshold (=33) only
Navigated lunar pixels + DC threshold (=33)
DC threshold (=33) only
Navigated lunar pixels + DC threshold (=33)