## Slide 1
Impacts of Orbital Drift on the MODIS Lunar Calibration
Truman Wilsona, Amit Angala, and Xiaoxiong Xiongb
aScience Systems and Applications, Inc.
bSciences and Exploration Directorate, NASA/GSFC
Fourth Joint GSICS/IVOS Lunar Calibration Workshop, 4-8 December 2023, Darmstadt, Germany

## Slide 2
Outline
2
Lunar Observation Geometry
Satellite Orbit Drift and It’s Impacts
Lunar Calibration Phase Angle Correction
Predicted Impact on the Lunar Calibration Trends

## Slide 3
Instrument Operation
Double-sided scan mirror with alternating Views
  Earth – EV
  Solar Diffuser – SD
  SRCA
  Blackbody - BB
  Space View - SV
Earth view imagery:
  Bands at 250-m (2),
  500-m (5), and 1-km (29) nadir resolution
Views of the Moon through the SV after roll maneuvers.
3
Notes: MODIS combines EV imagery with OBC observations each scan.
Main RSB calibrator is the SD.
Degradation of SD measured by the SDSM.
SV primarily used for BG, but can view the Moon
<click>
The Moon is at a different AOI, used for RVS.

## Slide 4
MODIS Lunar Observations
Lunar observations are made through the SV port.
The Terra/Aqua can be rolled about the x’-axis during scheduled observations
  Target phase: + 55.5°.
The SV sector FOV is narrow but is replaced by the EV sector.
Unscheduled observations can occur if the Moon is within 1.2° of the SV center.
  Observations between: + (50° – 80°)
4
ẟ = -8.425°
Roll Range – [0°, -20°]
+ 1.2°
Notes: MODIS combines EV imagery with OBC observations each scan.
Main RSB calibrator is the SD.
Degradation of SD measured by the SDSM.
SV primarily used for BG, but can view the Moon
<click>
The Moon is at a different AOI, used for RVS.

## Slide 5
Lunar Irradiance Measurements
5
Parameter | Definition
ESun/𝜋 | Solar Spectral Irradiance (RSR Integrated)
Ω | Pixel Solid Angle
m1 | Calibration Coefficient (SD AOI)
RVS | Response Versus Scan Angle
dn | Background-Subtracted Counts
Moon Shadow off FPA
Use Scan and Mirror-Side Averages
Use on-orbit m1 and RVS to assess calibration stability
Offsets with ROLO are well known.
The trends are normalized to the early mission.
Measured
ROLO
Measured/ROLO
Aqua Band 8
Aqua Band 8
*ROLO Developed by USGS

## Slide 6
ROLO Model Phase Dependence
6
Our existing unscheduled Moon data shows a strong phase dependence for some bands.
  Can be different between instruments
The scheduled Moon data is historically kept in a narrow range.
  This is now changing due to orbit drift. (next slides)
Aqua
Band 8
Terra
Band 8
Aqua
Band 19
Terra
Band 19

## Slide 7
Satellite Orbit Drift
Terra Aqua
Terra Aqua
Terra Aqua
7
Orbit simulations provided by Earth Science Mission Operations (ESMO) Flight Dynamics System (FDS) at NASA/GSFC

## Slide 8
Satellite Orbit Drift
8
Terra
Aqua
Orbit simulations provided by Earth Science Mission Operations (ESMO) Flight Dynamics System (FDS) at NASA/GSFC

## Slide 9
Satellite Orbit Drift
9
Terra
Aqua
Year | Terra | Aqua
Before 2023 | 55° to 56° | -55° to -56°
2023 | 50° to 51° | -50° to -51°*
2024 | 44° to 45° | -44° to -45°
2025 | 39° to 40° | -39° to -40°
2026 | 30° to 31° | -30° to -31°
*Close to the VIIRS Phase Angle Range
Observations at the historical target phase are lost by late 2024.
The current proposed angles are listed below. The actual angles are subject to change.

## Slide 10
ROLO Model Phase Dependence
10
Terra Band 8
Aqua Band 19
Where we’ve been
Where we’re going
Where we’re going
Where we’ve been
History
2023
2024
2025
2026
History
2023
2024
2025
2026
To help characterize the new phase angle range, special data collects have been performed in the new phase angle range.
These are paired with a range of unscheduled Moon events.
These opportunities will be available 2-4 times per year going forward.

## Slide 11
*Coordinates for the observer
Moon Cycles
A few times each year, unscheduled Moon data is available near the same time as a scheduled Moon.
Special data collects to extend the phase range (blue).
Single Moon Cycle -> No significant changes to the gain.
Aqua MODIS
Aqua MODIS
Band 3
11

## Slide 12
Developing a Phase Correction
12
Use the unscheduled Moon data to derive slopes.
  The magnitude of the slope for each cycle is dependent on the libration angles.
  Require a phase angle range > 12°, at least 6 unscheduled Moon events.
    87 cycles for Terra, 70 for Aqua.
    Thresholds are adjustable if needed.
Extrapolate to arbitrary phase angles using a weighted-average approach.
x

## Slide 13
Developing a Phase Correction
13
Example correction for data from Nov. 2007.
Example weighting using 3 Moon Cycles:
  May 2005
  December 2008
  May 2020
Uncorrected
Corrected
Fit Lines
Aqua Band 3
+ 55.5°
Phase Angle

## Slide 14
Application to MODIS Unscheduled Moon Data
14
Use unscheduled Moon as a test of the correction.
The correction brings the unscheduled Moon back in line with the scheduled Moon Data.
For cycles where the phase range or number of events did not meet the criteria, the correction still works well.
Terra MODIS Band 8
Aqua MODIS Band 19

## Slide 15
Test: Application to N20 VIIRS
15
VIIRS unscheduled Moons occur over a wider phase angle range.
VIIRS and MODIS have several spectrally matched band pairs.
VIIRS narrow SV FOV prevents having many unscheduled Moons in a single cycle for a given band.
  The same methodology to derive the correction from VIIRS data is not possible.
We see a reduction in the standard deviation for many of the tested bands.
N20 Band M1

## Slide 16
Predicting the Future Impact
16
Year | Terra | Aqua
Before 2023 | 55° to 56° | -55° to -56°
2023 | 50° to 51° | -50° to -51°
2024 | 44° to 45° | -44° to -45°
2025 | 39° to 40° | -39° to -40°
2026 | 30° to 31° | -30° to -31°
Using predicted observation geometries, we derive correction factors through the end of 2026.
Drifts of a few percent can be seen for some bands and will impact the calibration if left uncorrected.

## Slide 17
Predicting the Future Impact
17
The magnitude of the impact shows a strong wavelength dependence.
  Biggest impact: Terra at short wavelengths, Aqua at long wavelengths.
This impact matches what we’ve seen in previous analysis.

## Slide 18
Conclusions
18
Orbit drift causes a phase angle change in the lunar calibration.
Phase dependence of the ROLO model view geometry correction is expected to cause a drift in the lunar calibration.
Using unscheduled Moon data, we developed a correction methodology based on the phase dependence at different observation geometries.
Using predicted orbits, we calculated the future view geometries and predicted the magnitude of the expected drift.
For short wavelength bands in Terra, the change can be a few percent by 2026. For long wavelength bands in Aqua, the change can be greater than 1%.
The correction will need to be monitored as the mission continues.

## Slide 19
Backup Slides
19

## Slide 20
Lunar Geometry Definitions
20
The ROLO model is used to account for geometric differences in the lunar observations.
  The geometric differences can be described using 6 parameters.
  Selenographic Coordinates refer to locations (projections) on the lunar surface.
Parameter | Definition
dSat-Moon | Distance between the satellite and the Moon
dSun-Moon | Distance between the Sun and the Moon
Libration Angles | 
 | Selenographic Longitude of the Observer
 | Selenographic Latitude of the Observer
 | Selenographic Longitude of the Sun
 | Selenographic Latitude of the Sun
Parameter | Definition
dSat-Moon | Distance between the satellite and the Moon
dSun-Moon | Distance between the Sun and the Moon
Libration Angles | 
 | Selenographic Longitude of the Observer
 | Selenographic Latitude of the Observer
 | Selenographic Longitude of the Sun
 | Selenographic Latitude of the Sun
Example shadow image produced with the SP Model developed by AIST, Japan.
The angle between the observer and solar coordinates is the lunar phase angle. (Aqua MODIS observation at -50.3°, right)

## Slide 21
MODIS Lunar Observation Range
21
Moon albedo map produced by the LROC.
Example shadow image produced with the SP Model developed by AIST, Japan.
Terra MODIS
Aqua MODIS
Observer
Sun