## Slide 1: Inter-Calibration of Infrared Imagers Using Observations of Venus
Presenter: Martin Burgdorf
with contributions by D. Taniguchi
Dec 7, 2023

## Slide 2: Agenda
“Third Point“ for Calibration of Infrared Imagers
What about Venus?
First Results From Inter-Calibration
Conclusions

## Slide 3: Celestial Targets Considered Fit for Calibration
Moon (Used With Solar Bands)
Temperatures 100 - 400 K on surface
Model needed close to New ☾
Inconsistent spatiotemporal sampling in data stitching
Mercury (Bremer, SPIE, 2010)
Large dynamic range needed
Exact knowledge of PSF and pointing essential
Fulbright et al., 2023

## Slide 4: Venus: a Possible Radiometric Calibrator?
Venus has an atmosphere, so…
Q: Its Tb is variable?
A: Reproducible diurnal variations
Q: There are spectral features – availability of model?
A: No model needed for inter- and cross-calibration!
Q: Spatial variations?
A: Average over large fraction of disk!
PSG spectrum from Angerhausen et al. (2023)

## Slide 5: Observing Strategy: Inferior Conjunctions of Venus
Date and Time | Dec | Diameter
2007 Aug 18 | +5 | 60“
2009 March 27 | +10 | 59“
2015 Aug. 15 | +6 | 58“
2017 March 25 | +9 | 59“
2023 Aug. 13 | +7 | 58“
2025 Mar 23 | +8 | 60“
Date and Time | Dec | Diameter
2007 Aug 18 |  | 60“
2009 March 27 |  | 59“
2015 Aug. 15 |  | 58“
2017 March 25 |  | 59“
2023 Aug. 13 |  | 58“
2025 Mar 23 |  | 60“

## Slide 6: Observations of Venus with SEVIRI (uncalibrated)
Signal from Meteosat 8 – 11
Channels max(counts)>170
Channels max(counts)<160

## Slide 7: Inter-Calibration of SEVIRI on METEOSAT-8…-11
Satellite and Date | Counts (8.7 m) | Counts (9.7 m) | Counts (13.4 m)
METEOSAT-11 / MSG4, 2023/08/13 | 89.8 | 113.2 | 156.8
METEOSAT-10 / MSG3, 2023/08/30 | 87.5 | 111.9 | 154.0
METEOSAT-10 / MSG3, 2017/03/30 | 93.1 | 112 | 153.30.6
METEOSAT-9 / MSG2, 2017/04/02 | 89.2 | 114.8 | 152.60.9
METEOSAT-9 / MSG2, 2015/08/21 | 97.2 | 121.8 | 152.40.6
METEOSAT-8 / MSG1, 2017/04/11 | 84.3 | 111.9 | 156.7.3
Satellite and Date |  |  | 
METEOSAT-11 / MSG4, 2023/08/13 |  |  | 
METEOSAT-10 / MSG3, 2023/08/30 |  |  | 
METEOSAT-10 / MSG3, 2017/03/30 |  |  | 
METEOSAT-9 / MSG2, 2017/04/02 |  |  | 
METEOSAT-9 / MSG2, 2015/08/21 |  |  | 
METEOSAT-8 / MSG1, 2017/04/11 |  |  | 
Counts had background of 51 or 102 subtracted, therefore they scale directly with radiance.

## Slide 8: Observations of Venus with AHI (calibrated)
Radiance from Himawari-8 and -9
Local minimum of TB just below 10
Close to CO2 15 fundamental band

## Slide 9: Inter-Calibration of AHI on Himawari-8 and -9
Phase angle range 155 - 165 covered three times
Examples: AHI Channels 12 (9.63 or 1040 cm-1) and 16 (13.3 or 750 cm-1)
H-8, 2015: 2.087 0.011 W m-2 sr-1 -1, 1.948 0.008 W m-2 sr-1 -1
H-8, 2017: 1.938 0.016 W m-2 sr-1 -1, 2.005 0.007 W m-2 sr-1 -1
H-9, 2023: 1.871 0.01 W m-2 sr-1 -1, 1.993 0.01 W m-2 sr-1 -1
Agreement between Himawari-8 and -9 a few % or better
2015: TB in most channels of AHI and SEVIRI => ♀︎ atm. Changed

## Slide 10: Summary and Conclusions
Venus‘ night side: a homogeneous extended source with a radiance slightly lower than Earth
STDEV in radiance < 1% at 8 m during one inferior conjunction => Venus is suitable for inter-calibration
Inter-calibration of Himawari-8 and -9: agreement within 0.5% in radiance / 0.3 K in brightness temperature, six years apart (13.4 m)
Spot checks of radiometric stability in different years: SEVIRI on METEOSAT-9 and -10 better than 0.5 K on counts level (13.4 m)
Venus well suited for inter-calibration, check stability at 13.4 .