## Slide 1: Inter-Calibration of CrIS on SNPP and NOAA-20 Using Lunar Observations
Presenter: Martin burgdorf, universität hamburg
CrIS observations of Moon: yong cheN, nOAA
Model of moon: Thomas Müller, MPI extraterrestrische physik

## Slide 2: Introduction
The Moon was used for the characterisation of HIRS in flight (Burgdorf et al., 2020, Seibert, 2022)
A model for the disk-integrated thermal infrared is available (Müller et al., 2021)
Many disk-integrated spectra of the Moon provided by Y. Chen
What opportunities for (inter-)calibration do they offer?

## Slide 3: Available infrared observations of the moon
Thousands of spectra with CrIS on SNPP and NOAA-20 (3.9 - 4.6, 5.7 – 8.3, 9.1 – 15.4)
SNPP since Oct 2011, NOAA-20 since November 2017
667 events with SNPP, 326 events in NOAA-20
No direct SNOs or matchups => Moon is common target

## Slide 4: CROSS-TRACK INFRARED SOUNDER SCAN PATTERNS
9 FOVs with 2 sweep directions.
The 9 FOVs form one FOR. Each scan includes 30 FORs.
3 wavenumber ranges: 650 – 1095 cm-1, 1210 – 1750 cm-1, 2155 – 2550 cm-1
3 x 3 14 km (0.96IFOV, sampling distance: 16 km at nadir.
A typical CrIS lunar event has several observations in two to four FOVs.
From Yong Han et al. (2014)

## Slide 5: Comparison between Lunar Model and Observation
Reflected sunlight at shortest wavelengths
Christansen feature at 8 m (?)
Choose spectral region without anomaly in each spectral range

## Slide 6: Brightness temperature = f(phase angle)
Moon in > 25 consecutive orbits
TBN-20 – TBSNPP = 0.42 0.03 K (SW)
LW range:
TBN-20 – TBSNPP = 0.14 0.06 K
Salisbury et al. (1997)

## Slide 7: Brightness temperature = f(Distance🌞🌜)
Dist. Sun-Moon = 3.8106 km (2.5%)
Brightness Temp. = 4.0 0.1 K
LW Range:
Brightness Temp. = 5.0 0.4 K
Salisbury et al. (1997)

## Slide 8: Lunar TB from SNPP and N-20 in sw
TB(2020 - 2015) = -0.520.07 K
TB(2020 - 2017) = -0.100.04 K
Salisbury et al. (1997)
TB(2020 - 2015) = -0.460.07 K
TB(2020 - 2017) = -0.260.20 K

## Slide 9: Summary of Results
Model in good agreement with spectrum from CrIS, but some (spurious) features
Very consistent radiances for phase angles between 50 and 90 (consecutive orbits)
Very accurate difference in radiance between perihelion and aphelion (0.3% in radiance, SW)
TB from NOAA-20 significantly higher than from SNPP in SW (and MW? And LW??)
TB from 2015 significantly higher than from 2017 and 2020 in SW (and MW/LW?)
Occasional inconsistencies between radiances from consecutive orbits

## Slide 10: perspectives
A model of the IR irradiance of the disk-integrated Moon is being validated.
Random uncertainty of single observation (avg 100 0.15 K in SW (0.5 % in radiance)
Systematic uncertainty due to uncertainty in diameter of FOV?
Agreement with HIRS within uncertainties of that instrument
Next steps -
  Check radiometric stability
  Compare model to IASI spectra of the Moon – features?
  Get lunar spectra from NOAA-21

## Slide 11: disclaimer
The scientific results and conclusions, as well as any views or opinions expressed herein, are those of the author(s) and do not necessarily reflect those of NOAA or the Department of Commerce.