## Slide 1
Alternative Applications of Lunar Observations
Fangfang Yu
4th GSICS/IVOS Lunar Calibration Workshop

## Slide 2: Alternative Applications of Lunar Observations
Scope of the session
  Applications of lunar images for instrument characterization, such as MTF, RVS, and aerosol retrieval, etc
Goals for the session
  Straylight
    Recommendations to improve the lunar irradiance measurements
  MTF
    Approaching the best practice method for MTF with the Moon
  Skynet
    Discussion on the collaboration between L2 + and model development communities

## Slide 3: Toward the best practice method for MTF with the Moon
Three talks on MTF assessment with different fitting functions
  PROBA-V (Stafen Adriaensen)
  MTF/FCI (Christoph Straif)
  MODIS/VIIRS (Truman Wilson)
Recommendation
  EUMETSAT and VITO to test more fitting functions and share the results with the community.

## Slide 4: Toward the best practice method for MTF
Standard procedure
  Lunar image edge selection -> ESF -> LSF -> MTF
Best practice for each step, after the exercise results reported in the Xi’an workshop (LCWS2), 6 GEO instruments,
  Lunar Image selection
    Instrument data: L1b or L1alpha, Phase angle -> standard or typical lunar images
  Edge selection
    near middle and avoid edge with large slant angle, avoid terminator
    Oversampling handling?
    Two sides of the moon?
  Edge spread function (ESF)
    Padding lunar pixels
      Signal-Noise evaluation for screening pixels into the moon, Normalization
      Albedo flattening with SP model result, which makes fitting more straight forward and easier for automation.
      Minimum pixel s for fitting?
    Subpixel alignment
      Midpoint
    Fitting function
      Fermi, Cauchy, no-fitting, …
      Instrument dependent fitting?
  Line spread function (LSF)
    Derivative of ESF
  MTF
    FFT
  Evaluation
    Up to 1 Nyquist or go beyond?
Recommendation: Continue the exercise.

## Slide 5: Straylight correction
Fangfang Yu presented the straylight corrections for ABI VNIR bands to improve the measured irradiance for accurate RVS interpretation.
Technical discussion/recommendations for the high spatial resolution lunar images, per ABI experience
  Integrating: Negligible error at sample level may be accumulated to be a significant contribution in the measured irradiance
  Lunar irradiance measurement: include the lights originated from the Moon, otherwise, remove them.
  Moon schedule: use the scans which is calibrated with un-contaminated spacelook
    e.g. spacelook near the Equator, thus not affected with the possible scattered light near the polar region
  Image collection: the Moon should be collected at least certain distance from the illuminated Earth limb or at the dark side to the Earth
  Data processing of subset lunar images: cover the moon and the vicinity area where lights is scattered or leaking from the Moon, but ensure the area is not too large so as to amplify the potential calibration error in the irradiance values.

## Slide 6: Skynet Network
Skynet network for aerosol retrieval from the moon irradiance (Monica Campanelli)
  Network of sun-sky photometers, dedicated to study columnar aerosol properties.
Discussion
  The POM-2 instruments, although not calibrated, could be good data source for model development
Recommendation
  GDWG to review how to host the new lunar irradiance data such as air-LUSI, skynet lunar irradiance data