GSICS Product Acceptance Form

Version 1.2

GSICS Coordination Center

May 2010

Please remit completed form and supporting documents to:

Bob Iacovazzi, Jr.

GSICS Coordination Center, Deputy Director

E-Mail: Bob.Iacovazzi@noaa.gov

Address: NOAA Science Center, Room 712, Camp Springs, MD, USA  20746

Phone: 1-301-763-8346 x358

GSICS Product Acceptance Form

Document ID: GSICS_GCC_GPAF_V01.2

Change History

| Version | Date (MM/DD/YYYY) | Point of Contact | Change |
| --- | --- | --- | --- |
| 1.0 | 30/11/2009 | Bob Iacovazzi, GCC | Baseline |
| 1.1 | 29/03/2010 | Bob Iacovazzi, GCC | Changed the ordering of the product form elements to better align with the GPPA workflow plan. |
| 1.2 | 04/05/2010 | Bob Iacovazzi GCC | Clarifications and grammatical edits |

Form Overview.

The GSICS Procedure for Product Acceptance (GPPA) is the

- GSICS product developers pathway to obtain a “Stamp of Approval” for a potential product;

- GSICS data users window to GSICS product quality and “fitness for purpose”;

- GSICS governing body reference for judging GSICS product fitness.

The GPPA was inspired by the need to find a mechanism to assess GSICS product quality, as well as by the Quality Assurance Framework for Earth Observations (QA4EO) spearheaded by the Committee on Earth Observation Satellites (CEOS) Working Group on Cal/Val (WGCV).  To aid in understanding of the GPPA, the most recent version of the procedure and its workflow milestones can be found at the GSICS Wiki at the following URL: https://cs.star.nesdis.noaa.gov/GSICS/GppaWorkflow.

The GSICS Product Acceptance Form (GPAF) is designed to help the GSICS product developers and governing body evaluate and track product quality through the product acceptance procedure.  Furthermore, it allows a data user to clearly understand what product quality measures are in place once a product has been accepted as a GSICS product.  Finally, the GPAF can be used as a product quality maintenance tool, since product quality assurance is a living process requiring updates to product quality indicators and their associated documentation.

Directions.

Fill out blanks in the form as directed from the GPPA Workflow found at https://cs.star.nesdis.noaa.gov/GSICS/GppaWorkflow.  If a supporting document can be found on-line, then giving a link to the document is acceptable.  If a supporting document cannot be found on-line, then electronic copies of the document can be attached along with the submission of the GPAF.  Remit the GPAF electronically to the e-mail address given on the cover page of this document.

Also, for further ideas about implementing the GPPA, please see the Quality Assurance Framework for Earth Observations web site at http://qa4eo.org/.

SECTION I.  Product Provider Information

| I.1. Proposed Product Name | GSICS Re-Analysis Correction and GSICS Bias Monitoring for MTSAT IR channels |
| --- | --- |
| I.2. Submitting Organization Name | Japan Meteorological Agency/Meteorological Satellite Center |
| I.3. Point of Contact of Product Provider |  |
| I.3.A. Name | Hiromi Owada |
| I.3.B. E-Mail Address | howada@met.kishou.go.jp |
| I.3.C. Physical Address | 3-235 Nakakiyoto, Kiyose-shi, Tokyo 204-0012 JAPAN |
| I.3.D. Phone | +81-42-493-7452 |
| 1.3.E. FAX (Optional) | +81-42-492-2433 |
| 1.3.F. URL (Optional) | http://mscweb.kishou.go.jp/index.htm |

SECTION II.  Product Information

II.1.  Brief Product Description (1 page or less)

The GSICS Re-Analysis Correction for MTSAT IR channels is a dataset that can be applied by users to obtain corrected satellite radiances. These data are based on the results of inter-calibration of the MTSAT IR channels with reference low-earth-orbiting (LEO) satellite hyperspectral sounding instruments. They consist of coefficients and their uncertainties of a linear regression formula to associate observations of MTSAT IR channels (Monitored instrument; MON) with ones of the hyperspectral sounder (Reference instrument; REF).

The inter-calibration process is based on the comparison of thousands of observations of the two instruments, collocated in space, time and viewing geometry, taken for one day or 30 days. These observations are transformed spatially and spectrally to allow direct comparison by linear regression to estimate the coefficients, a and b, required to convert MON digital counts, CMON, to the REF radiances, IREF :

Equation 1: 
This relationship can be inverted to apply the regression coefficients, a and b, to convert MON digital counts, CMON, into radiances consistent with the REF, ,
Equation 2: , 
together with the estimated uncertainty:
Equation 3: ,

The regression coefficients, a and b, and their uncertainties, and are given in the netCDF files as GSICS Correction for each MTSAT IR channel. The GSICS Re-Analysis Correction is computed for every day and its regression period is 30 days centered on the observational date. The GSICS Bias Monitoring is the results of inter-calibration for one day. This is not a product but is generated for the routine bias monitoring.

The reference instruments are AIRS and IASI. The comparison of MTSAT IR-AIRS, and MTSAT IR-IASI, are performed and the collocation dataset is generated. MTSAT IR GSICS Correction is calculated from this collocation dataset. The three types of GSICS Correction –MTSAT IR-AIRS, MTSAT IR-IASI and MTSAT IR-AIRS+IASI – are available.

For the MTSAT HRIT data users, the corrected calibration table is also stored in the GSICS Correction file as optional information for converting disseminated digital counts to corrected brightness temperatures directly.

II.2. What is the product scope within GSICS? (Describe the general significance and purpose of the product to the GSICS mission.)

The GSICS Re-Analysis Correction for inter-calibration of MTSAT IR channel renders the infrared data from MTSAT compatible with the reference instrument. This allows the MTSAT infrared data to be interoperable with data from other geostationary satellite instruments maintained and distributed by NOAA, EUMETSAT and CMA, when their data have been likewise inter-calibrated with respect to the same reference instrument. Thus GSICS Re-Analysis Correction for inter-calibration of MTSAT IR channel supports the GSICS goal of cross-calibration of IR channel data from entire constellation of geostationary weather satellites.

II.3. What are the general product function and performance specifications? (These are the high-level design requirements of the product, which include what the product will do and how well it will do it.)

The GSICS Re-Analysis Correction for inter-calibration of MTSAT IR channel shall make the IR channel data from MTSAT compatible with the reference instrument, and be updated once per day based on the 30 days on collocations of MTSAT and the reference instrument.  As a by-product of the process of generating the GSICS Re-Analysis product, GSICS Bias Monitoring data shall be made available using the one-day collocation data.

The GSICS Re-Analysis Correction shall have uncertainty, given by , less than or equal the values given in Table II.1 and II.2.

Table II.1. Maximum uncertainty requirements for the GSICS Re-Analysis Correction for MTSAT-1R.  The uncertainty is given by , is defined in Equation 3 in Section II.1.

| Channel | IR1 (10.8m) | IR2 (12.0m) | IR3 (6.8m) | IR4 (3.8m) |
| --- | --- | --- | --- | --- |
| Standard Radiance Tb (K) | 286.67 | 285.91 | 238.37 | 286.51 |
| MTSAT IR-AIRS+IASI | Uncertainty (K) | 0.020 | 0.020 | 0.010 | 0.100 |
| MTSAT IR-AIRS | Uncertainty (K) | 0.020 | 0.020 | 0.010 | 0.100 |
| MTSAT IR-IASI | Uncertainty (K) | 0.020 | 0.020 | 0.010 | 0.100 |

Table II.2. Maximum uncertainty requirements for the GSICS Re-Analysis Correction for MTSAT-2.  The uncertainty is given by , is defined in Equation 3 in Section II.1.

| Channel | IR1 (10.8m) | IR2 (12.0m) | IR3 (6.8m) | IR4 (3.8m) |
| --- | --- | --- | --- | --- |
| Standard Radiance Tb (K) | 286.70 | 285.94 | 239.17 | 286.53 |
| MTSAT IR-AIRS+IASI | Uncertainty (K) | 0.020 | 0.020 | 0.010 | 0.100 |
| MTSAT IR-AIRS | Uncertainty (K) | 0.020 | 0.020 | 0.010 | 0.100 |
| MTSAT IR-IASI | Uncertainty (K) | 0.020 | 0.020 | 0.010 | 0.100 |

SECTION III.  Product Documentation

III.1  Product Development

Product providers, evaluators, and users all need to know the detailed physical basis of the product, and the basic structure of the product data files.  The documentation created for this section will be evidence of fulfillment of this goal.

III.1.A  Product Output Adherence to GSICS Standards

This documents that the product output is designed to meet GSICS accepted file naming and format conventions.

III.1.A.1. Product is designed to have data output files that meet GSICS file naming conventions documented on the GSICS Wiki at https://cs.star.nesdis.noaa.gov/GSICS/FilenameConvention?

| x | Yes | Please write a sample file name below: W_JP-JMA-MSC,SATCAL+RAC,MTSAT1R+JAMI-Aqua+AIRS-MetopA+IASI_C_RJTD_2010060200000_demo_01.nc W_JP-JMA-MSC,SATCAL+RAC,MTSAT2+Imager-Aqua+AIRS_C_RJTD_2010060200000_demo_01.nc W_JP-JMA-MSC,SATCAL+RAC,MTSAT1R+JAMI-Aqua+IASI_C_RJTD_2010060200000_demo_01.nc |
| --- | --- | --- |
|  | No | When is this to be completed and available? |
|  | Not /Applicable | What is the justification? |

III.1.A.2. Product is designed to have data output files that meet GSICS file format conventions documented on the GSICS Wiki at https://cs.star.nesdis.noaa.gov/GSICS/NetcdfConvention?

| x | Yes | Please electronically submit a sample data file to be scanned by the GCC for adherence to the GSICS file format convention. Some sample data are available on the following web site. https://cs.star.nesdis.noaa.gov/GSICS/MaterialMTSAT |
| --- | --- | --- |
|  | No | When is this to be completed and available? |
|  | Not /Applicable | What is the justification? |

III.1.B  Algorithm Theoretical Basis Document (ATBD)

Discussion of physical principles supporting the product.  In its preliminary draft, this could be in the form of references to journal article(s), or stand-alone technical information. Needs to include an algorithm flowchart, including data I/O and logic, and process element descriptions.

| Is the ATBD completed? |
| --- |
| x | Yes | Document found ( ) GPAF Package (x) Web Site ( ) FTP Site |
|  |  | Web or FTP Site Location: https://cs.star.nesdis.noaa.gov/GSICS/MaterialMTSAT |
|  | No | When is it to be completed and available? |
|  |  | Document will be found ( ) GPAF Package, or ( ) Web Site / ( ) FTP Site with the following address: |
|  | Not /Applicable | What is the justification? |

III.1.C  Plan to Establish Measurement Traceability to Reference Standards

Describes the traceability chain to reference standards (preferably international measurement standards).  If the measurement reference standard is not traceable to international standards, this clearly needs to be stated and justified.

| Is the measurement traceability plan completed? |
| --- |
| x | Yes | Document found ( ) GPAF Package (x) Web Site ( ) FTP Site |
|  |  | Web or FTP Site Location: AIRS validation http://cimss.ssec.wisc.edu/itwg/itsc/itsc13/proceedings/session5/5_11_revercomb.pdf AIRS calibration PAGANO Thomas S. and Co-Authors, 2008: Absolute Radiometric Calibration Accuracy of the Atmospheric Infrared Sounder (AIRS). Proceedings of SPIE, the International Society for Optical Engineering Earth observing systems XIII : ( 11-13 August 2008, San Diego, California, USA ) ISSN 0277-786X IASI Level 1 CalVal Plan http://smsc.cnes.fr/documentation/IASI/Documents/Technical/IASI_L1_CalVal_Plan_2597_1_0.pdf |
|  | No | When is it to be completed and available? |
|  |  | Document will be found ( ) GPAF Package, or ( ) Web Site / ( ) FTP Site with the following address: |
|  | Not /Applicable | What is the justification? |

III.2 Product Implementation

Procedures that meet current "best practices" in regards to establishing analysis software, harnessing radiative transfer models, and making calibration/validation measurements that are fundamental to implementing theory to create products.

III.2.A Harnessing Radiative Transfer Models

III.2.A.1. Model Description

| Does the model contain a detailed model description? |
| --- |
| x | Yes | Document found ( ) GPAF Package (x) Web Site ( ) FTP Site |
|  |  | Web or FTP Site Location: LBLRTM Description http://rtweb.aer.com/lblrtm_description.html |
|  | No | When is it to be completed and available? |
|  |  | Document will be found ( ) GPAF Package, or ( ) Web Site / ( ) FTP Site with the following address: |
|  | Not /Applicable | What is the justification? |

III.2.A.2. Model Users’ Guide.

| Does the model come with a users’ guide? |
| --- |
| x | Yes | Document found ( ) GPAF Package (x) Web Site ( ) FTP Site |
|  |  | Web or FTP Site Location: LBLRTM home http://rtweb.aer.com/lblrtm.html |
|  | No | When is it to be completed and available? |
|  |  | Document will be found ( ) GPAF Package, or ( ) Web Site / ( ) FTP Site with the following address: |
|  | Not /Applicable | What is the justification? |

III.2.A.3. Model Input Description.

| Is there a description of data or input atmospheric soundings and boundary conditions used by the model? |
| --- |
| x | Yes | Document found ( ) GPAF Package (x) Web Site ( ) FTP Site |
|  |  | Web or FTP Site Location: http://mscweb.kishou.go.jp/monitoring/gsics/ir/msctechrep52-1.pdf |
|  | No | When is it to be completed and available? |
|  |  | Document will be found ( ) GPAF Package, or ( ) Web Site / ( ) FTP Site with the following address: |
|  | Not /Applicable | What is the justification? |

III.2.A.4.  Model Verification and Validation.

| Is there documents that report model verification results or test studies? |
| --- |
| x | Yes | Document found ( ) GPAF Package (x) Web Site ( ) FTP Site |
|  |  | Web or FTP Site Location: Shephard, M.W., S.A. Clough, V.H. Payne, W. L. Smith, S. Kireev, and K. E. Cady-Pereira, Performance of the line-by-line radiative transfer model (LBLRTM) for temperature and species retrievals: IASI case studies from JAIVEx, Atmos. Chem. Phys. Discuss., , 9, 9313-9366, 2009. Mlawer, E.J., P.D. Brown, S.A. Clough, L.C. Harrison, J.J. Michalsky, P.W. Kiedron, and T. Shippert, Comparison of spectral direct and diffuse solar irradiance measurements and calculations for cloud-free conditions, Geophys. Res. Lett., 27, 2653-2656, 2000. Mlawer, E.J., S.J. Taubman, P.D. Brown, M.J. Iacono, and S.A. Clough, Radiative transfer for inhomogeneous atmospheres: RRTM, a validated correlated-k model for the longwave. J. Geophys. Res., 102, 16,663-16,682, 1997. |
|  | No | When is it to be completed and available? |
|  |  | Document will be found ( ) GPAF Package, or ( ) Web Site / ( ) FTP Site with the following address: |
|  | Not /Applicable | What is the justification? |

III.2.B Making Measurements to Support Cal/Val  (For example, measurements made to characterize a calibration target, such as monitoring platinum resistance thermometer temperatures of an external blackbody in thermal vacuum or making sea surface temperature measurements for SST validation.)

During the cal/val process, supporting measurements are sometimes made to assess or ensure the quality of the calibration activity. To properly record these measurements, in addition to documenting the data, a measurement procedure outline needs to be written that gives a description of the instruments involved, as well as information needed to know how the measurement(s) was taken and under what conditions.

| Are there documents available that outline the process of taking measurements that support cal/val, as well as summarize the results of these measurements? |
| --- |
|  | Yes | Document found ( ) GPAF Package ( ) Web Site ( ) FTP Site |
|  |  | Web or FTP Site Location: |
|  | No | When is it to be completed and available? |
|  |  | Document will be found ( ) GPAF Package, or ( ) Web Site / ( ) FTP Site with the following address: |
| x | Not /Applicable | What is the justification? It is not relevant to this product. |

III.2.C Establishing Analysis Software

Software documentation - consists of flow charts, module descriptions, revision descriptions, and programmer contact information.

| Is the software documentation complete? |
| --- |
|  | Yes | Document found ( ) GPAF Package ( ) Web Site ( ) FTP Site |
|  |  | Web or FTP Site Location: |
| x | No | When is it to be completed and available? |
|  |  | Document will be found ( ) GPAF Package, or ( ) Web Site / ( ) FTP Site with the following address: |
|  | Not /Applicable | What is the justification? |

III.2.D  Version Control Plan

A configuration management plan, or version control strategy, for documents, software, models, and measurements is a key activity in preserving product institutional memory and communicating product release characteristics to users?

III.2.D.1.  Documents

| Is there a version control plan for documents? |
| --- |
| x | Yes | Document found ( ) GPAF Package (x) Web Site ( ) FTP Site |
|  |  | Web or FTP Site Location: Subversion is used for the version control. http://subversion.tigris.org/ |
|  | No | When is it to be completed and available? |
|  |  | Document will be found ( ) GPAF Package, or ( ) Web Site / ( ) FTP Site with the following address: |
|  | Not /Applicable | What is the justification? |

III.2.D.2.  Software

| Is there a version control plan for software? |
| --- |
| x | Yes | Document found ( ) GPAF Package (x) Web Site ( ) FTP Site |
|  |  | Web or FTP Site Location: Subversion is used for the version control http://subversion.tigris.org/ |
|  | No | When is it to be completed and available? |
|  |  | Document will be found ( ) GPAF Package, or ( ) Web Site / ( ) FTP Site with the following address: |
|  | Not /Applicable | What is the justification? |

III.2.D.3.  Models

| Is there a version control plan for models? |
| --- |
| x | Yes | Document found ( ) GPAF Package (x) Web Site ( ) FTP Site |
|  |  | Web or FTP Site Location: Doxygen is used as the documentation generator. The information of model version is described in source codes. http://www.stack.nl/~dimitri/doxygen/ |
|  | No | When is it to be completed and available? |
|  |  | Document will be found ( ) GPAF Package, or ( ) Web Site / ( ) FTP Site with the following address: |
|  | Not /Applicable | What is the justification? |

III.2.D.4.  Measurements

| Is there a version control plan for supporting cal/val measurements? |
| --- |
|  | Yes | Document found ( ) GPAF Package ( ) Web Site ( ) FTP Site |
|  |  | Web or FTP Site Location: |
|  | No | When is it to be completed and available? |
|  |  | Document will be found ( ) GPAF Package, or ( ) Web Site / ( ) FTP Site with the following address: |
| x | Not /Applicable | What is the justification? It is not relevant to this product. |

III.3  Product Quality Assessment and Operations/Distribution

Product quality assessment documents the estimated product uncertainty, and its sources, in the product.  Product operations and distribution describes the process of product creation and dissemination to users.

III.3.A Product Quality Documents

These documents describe and quantify, as much as possible, the one-sigma uncertainties related to each product error source, as well as the product root-sum-square uncertainty.  These documents also give results of product validation studies, and a clear description of the quality indicator – preferably traceable to SI standards - to be assigned to the product.

| Are there product quality document(s)? |
| --- |
|  | Yes | Document found ( ) GPAF Package ( ) Web Site ( ) FTP Site |
|  |  | Web or FTP Site Location: |
| x | No | When is it to be completed and available? |
|  |  | Document will be found ( ) GPAF Package, or ( ) Web Site / ( ) FTP Site with the following address: |
|  | Not /Applicable | What is the justification? |

III.3.B Operations/Distributions Plan

Outlines how the data or results are to be stored and shared through GSICS network computers.  Statements about the level of access need to be included here.

| Is there an Operations/Distribution Plan? |
| --- |
|  | Yes | Document found ( ) GPAF Package ( ) Web Site ( ) FTP Site |
|  |  | Web or FTP Site Location: |
| x | No | When is it to be completed and available? |
|  |  | Document will be found ( ) GPAF Package, or ( ) Web Site / ( ) FTP Site with the following address: |
|  | Not /Applicable | What is the justification? |

III.3.C Data User’s Guide

Documents detailed data format, quality flag and parameter descriptions.  It must identify how data format meets GSICS standards, and the limitations of product use.

| Is there a Data Users Guide? |
| --- |
|  | Yes | Document found ( ) GPAF Package ( ) Web Site ( ) FTP Site |
|  |  | Web or FTP Site Location: |
| x | No | When is it to be completed and available? |
|  |  | Document will be found ( ) GPAF Package, or ( ) Web Site / ( ) FTP Site with the following address: |
|  | Not /Applicable | What is the justification? |