## Slide 1: GSICS Impacts on Applications Reporting works by some GSICS Users Fred Wu NOAA/NESDIS/STAR

## Slide 2: Outline
Some work by colleagues are presented
  T. Omai (JMA)
  T. Zhu (NOAA)
  X. Hu (CMA)
Some work will be presented separately
  A. Mitra (CIMSS)
  T. Schreiner (CIMSS)
Some work are still in progress
  R. Allegrino (NOAA)
  B. Rossow (ISCCP)
My fault if mispresented

## Slide 3: GSICS Impacts on MTSAT-2 WV CSR
Takahito Omai and H. Owada (JMA)
GSICS Correction for MTSAT-2 water vapor channel clear sky radiance …
… and comparison with JMA NWP monitoring

## Slide 4
MTSAT-2 WV Channel’s Clear Sky Radiance (CSR)
WITHOUT GSICS Correction

## Slide 5
MTSAT-2 WV Channel’s Clear Sky Radiance (CSR)
WITH GSICS Correction
Slightly more coverage
Slightly warmer …

## Slide 6
MTSAT-2 WV Channel’s Clear Sky Radiance (CSR)
DIFFERENCE of (with) – (without) GSICS Correction
Slightly more coverage
Slightly warmer …
… by ~0.5K …

## Slide 7
MTSAT-2 WV Channel’s Clear Sky Radiance (CSR)
BIAS as monitored by JMA NWP
Slightly more coverage
Slightly warmer …
… by ~0.5K …
… confirmed by JMA NWP bias monitoring
Illustrates the sophistication of the users and, therefore, the challenges to calibration. These motivated the GSICS.

## Slide 8: GSICS Impact on Global Forecast System (GFS)
T. Zhu and F. Weng (NOAA)
GSICS Correction for SEVIRI and GOES-12 Imager radiances reduced the O-B biases.

## Slide 9: Impact of GSICS Correction on GOES-12 Imager radiance
Compared to CRTM, GOES-12 Imager Channel 6 bias was reduced from -2.55K before GSICS correction to -0.11K after

## Slide 10: Global Forecast System (GFS)
What does that mean to GFS?
  In various time scale
  Tropics vs. NH
  For SEVIRI and GOES

## Slide 11: Experiments Design
GDAS FY09 with T382 resolution
GFS one month simulations: 20 May – 20 June, 2008
Control run: conventional data + all current sensors (e.g. AMSU-A/B, HIRS, AIRS, SSMI, MHS, GOES sounder)
Exp1 run: Control run + GOES-12 imager
Exp2 run: Control run + GOSE-12 imager + GSICS correction.

## Slide 12: Experiments Design
GDAS FY09 with T382 resolution
GFS one month simulations: 1-30 November 2008
Control run: conventional data + all current sensors (e.g. AMSU-A/B, HIRS, AIRS, SSMI, MHS, GOES sounder)
Exp1 run: Control run + SEVIRI CSR
Exp2 run: Control run + SEVIRI CSR + GSICS correction.

## Slide 13: Impacts of GSICS Correction for GOES-12 Imager on GFS Forecast
GOES-12 imager with and without GSICS bias correction
Anomaly Correlation for 500 mb height over tropics (left) and NH (right)

## Slide 14: Impacts of GSICS Correction for SEVIRI on GFS Forecast
MSG SEVIRI CSR with and without GSICS bias correction
Anomaly Correlation for 500 mb height over tropics (left) and NH (right)

## Slide 15: Summary
GSICS Correction for SEVIRI and GOES-12 Imager radiances reduced the O-B biases.
One-month GFS simulation experiments found that the GFS were improved
  For 5-7 day forecast
  In both tropics and NH
  For both GOES-12 and SEVIRI

## Slide 16: GSICS Impact on FY-2X IR Channel Radiances
X. Hu, P. Zhang, Y. Zhang (CMA)
Dramatic improvements

## Slide 17: FY-2 IR Calibration BEFORE GSICS

## Slide 18: FY-2 IR Calibration AFTER GSICS
Probably due to navigation anomalies

## Slide 19: Still in progress
A. Allegrino and J. Daniels (NOAA)
  Apply GSICS Correction to GOES
  Evaluate the impact on GOES retrieval of TPW
  Validate with ground-based GPS retrieval of TPW
W. Rossow and J. Ferrier (GISS)
  Apply GSICS Correction to selected period of time
  Evaluate the impact on ISCCP products

## Slide 20: Summary
Users start to be interested in GSICS Correction
Impacts are generally positive
  Some are quite significant
Need to help users
  To know about GSICS Correction
    Many users did not learn about it from us – good or bad
  To use GSICS Correction
    Learn about user service
  To design tests for evaluation
    Inappropriate tests may end up with misleading results