## Slide 1: NOAA’s Satellite Climate Data Record Program
Jeffrey L. Privette
CDRP Chief Scientist
NOAA’s National Climatic Data Center
Asheville, North Carolina

## Slide 2: Sustained Climate Information Flow Emerging International Architecture
Satellite & In Situ
Observations
Satellite data
Environmental
Data Records
Long-term Information Preservation
Interim
Climate Data
Records
(ICDRs)
Climate
Information
Records
Short scale
physical phenomena
monitoring
Operational Climate
Monitoring supporting
Climate Services
Longer term climate variability
& climate change analysis
Adaptation
+ mitigation planning
(decision making)
Sustained Applications
Major
model-based
Reanalysis
Near Real Time
Re-calibration
Inter-calibration
Reprocessing
Observing system
performance
Monitoring
and automated
corrections
Data conversion
User Services
Archives
Inter-calibration
Sustained Coordinated Processing
SCOPE-CM
Essential
Climate Variables
[Thematic
Climate Data
Records 1,2,…
(TCDRs)]
Fundamental
Climate Data
Records
(FCDRs)
2

## Slide 3: CDRs Require Consistent (Re-)Application of Advanced Algorithms Over Many Satellites and Situations
Operational weather and hazard products are produced rapidly to potentially save life and property
Climate Data Records (CDRs) provide long term product consistency through rigorous reprocessing with advanced algorithms, ancillary data and evolved instrument understanding.
Climate Information Records (CIRs) provide specific information about environmental phenomena of particular importance to science and society (e.g., hurricane trends, drought patterns)
Vegetation Greenness Index
Uncorrected Data Time Series Contain Both Environmental Information and Satellite-induced Artifacts
New satellite launched
Time (year)
Top of Atmosphere Vegetation Index
Top of Canopy Vegetation Index

## Slide 4
Merging NASA/NOAA/USGS Data Will Provide Information at Climate Time Scales and Quality
4

## Slide 5
Maturity Matrix Identifies Milestones and Research-to-Operations Transition Points
Level | Sensor Use | Code Stability | Metadata & QA | Documentation | Validation | Public Release | Science & Applications | MilestoneReviews
1 | Research Mission | Significant changes likely | Incomplete | Draft ATBD | Minimal | Limited data availability to develop familiarity | Little or none | 
2 | Research Mission | Some changes expected | Research grade (extensive) | ATBD Version 1+ | Uncertainty estimated for select locations/times | Data available but of unknown accuracy; caveats required for use. | Limited or ongoing | ATBD Review
3 | Research Missions | Minimal changes expected | Research grade (extensive); Meets international standards | Public ATBD; Peer-reviewed algorithm and product descriptions | Uncertainty estimated over widely distribute times/location by multiple investigators; Differences understood. | Data available but of unknown accuracy; caveats required for use. | Provisionally used in applications and assessments demonstrating positive value. | NOAA Operations Review
4 | Operational Mission | Minimal changes expected | Stable, Allows provenance tracking and reproducibility; Meets international standards | Public ATBD; Draft Operational Algorithm Description (OAD); Peer-reviewed algorithm and product descriptions | Uncertainty estimated over widely distribute times/location by multiple investigators; Differences understood. | Source code released; Data available but of unknown accuracy; caveats required for use. | Provisionally used in applications and assessments demonstrating positive value. | 
5 | All relevant research and operational missions; unified and coherent record demonstrated across different sensors | Stable and reproducible | Stable, Allows provenance tracking and reproducibility; Meeting international standards | Public ATBD, Operational Algorithm Description (OAD) and Validation Plan; Peer-reviewed algorithm, product and validation articles | Consistent uncertainties estimated over most environmental conditions by multiple investigators | Source code portable and released; Multi-mission record is publicly available with associated uncertainty estimate | Used in various published applications and assessments by different investigators | CDR Certification Review
6 | All relevant research and operational missions; unified and coherent record over complete series; record is considered scientifically irrefutable following extensive scrutiny | Stable and reproducible; homogeneous and published error budget | Stable, Allows provenance tracking and reproducibility; Meeting international standards | Product, algorithm, validation, processing and metadata described in peer-reviewed literature | Observation strategy designed to reveal systematic errors through independent cross-checks, open inspection, and continuous interrogation | Source code portable and released; Multi-mission record is publicly available from Long-Term archive | Used in various published applications and assessments by different investigators | 
v. June 2010

## Slide 6: 18 Development Efforts Funded Since 2009 (+7 smaller efforts continued from prior years – SDS)
AVHRR (VIIRS)
Cloud Properties (Kato)
Snow/Ice (Key)
VNIR Cal./Clouds (Minnis)
Thermal Calibration (Mittaz)
Land/Carbon (Vermote)
Ocean Fluxes (Clayson)
Visible Calibration (Stone)
SBUV (OMPS)
Ozone (Flynn)
DMSP: SSM/I, /IS (AMSR2)
Calibration (Kummerow)
Snow/Ice (Key)
Water Vapor (Luo)
GPCP (Adler)
SORCE, Glory (TSIS)
Solar Irrad. (Pilewskie)
GOES: Imager (ABI)
VNIR Cal./Clouds (Minnis)
ISCCP Fluxes (Zhang )
AMSU (ATMS)
Hydro Cycle (Ferraro)
Upper Air Temp (Ho)
Water Vapor (Luo)
Temp. Profile (Zou)
Other Satellites
Arrows identify key climate sensor on NOAA polar platform (POES)
HIRS (CrIS)
FCDR/Intersensor calibration (Cao)
Water Vapor (Luo)
Cloud Properties (Menzel)
ERBS: ERBE (CERES)
Radiation Budget (Kato)
GPS RO (Various)
Temp. Profiles (Ho)
NOAA POES Satellite Platform
Altimeters (Jason 3)
Calibration (Callahan)

## Slide 7: CDR Developers Organizing Into Thematic Teams For Production Efficiency & Coherent Products
Clouds
Clouds
Clouds
Sensor (Level 1) Calibration Teams
Radiation Budget
Solar Irradiance
Ozone & Trace Gases
Precipitation
Clouds & Aerosols
Land
Atmospheric Profiles
Cryosphere
Ocean
Thematic CDR Teams
Fundamental CDR Teams

## Slide 8: Possible CDRP – GSICS Interaction Areas
Extend modern sensor calibration backwards (e.g., Heidinger using MODIS to start of AVHRR record)
Develop routine calibration comparison processes for Interim CDRs
Address multiple approaches to same product (anti-”consensus coding”!)
  Intercomparison guidelines and studies
  Helping define ‘acceptance’
Build consistent and readily useable Level 1 (RDR) data sets (e.g., AVHRR; SSM/I; NPP/JPSS)
Guidelines on static ancillary data sets (e.g., land-water masks at different scales) – toward product suite consistency

## Slide 9: Concerns
“This paper should clearly state … future efforts to incorporate [GSICS] results.”
“Why is the Global Space-based Inter-Calibration System (GSICS) not front and center in this paper?”
Some scientists reporting that some peer reviewers are requiring that GSICS
  Work be described
  Articles be referenced
  Data sets be used for comparison and assessment
  Submission to GSICS acceptance tests, or use of GSICS-approved data sets, must not become a litmus test for publication
A GSICS education campaign may be needed (Fred helped greatly in most recent dust-up… where a relevant GSICS product did not yet exist!)