## Slide 1: GSICS Product Development
Tim Hewison1
EUMETSAT
On behalf of GSICS Research Working Group

## Slide 2: Global Space-based Inter-Calibration System
What is GSICS?
  Global Space-based Inter-Calibration System
  Initiative of CGMS and WMO
  Effort to produce consistent, well-calibrated data from the international constellation of Earth Observing satellites
What are the basic strategies of GSICS?
  Improve on-orbit calibration by developing an integrated inter-calibration system
        Initially for GEO-LEO Inter-satellite calibration
        Being extended to LEO-LEO
        Using external references as necessary
  Best practices for prelaunch characterisation (with CEOS WGCV)
This will allow us to:
  Improve consistency between instruments
  Reduce bias in Level 1 and 2 products
  Provide traceability of measurements
  Retrospectively re-calibrate archive data
  Better specify future instruments
EUMETSAT | CNES | JMA
NOAA | CMA | KMA
ISRO | NASA | WMO
USGS | NIST | JAXA
ROSHYDROMET | IMD | ESA
Notes: Well, what is GSICS?
The Global Space-based Inter-Calibration System (GSICS) is an initiative of CGMS and WMO, which aims to ensure consistent calibration and inter-calibration of operational meteorological satellite instruments.
One of the basic strategies of GSICS is to develop an integrated on-orbit cal/val system - initially by LEO-GEO Inter-satellite/inter-sensor calibration.
This will then allow us to provide corrections to improve the consistency between instruments, produce less biased level 1, and therefore, level 2 data, and ultimately, retrospectively re-calibrate archive data, which is of great interest in the climate monitoring community

## Slide 3: GSICS Principles
Systematic generation of inter-calibration products
  for Level 1 data from satellite sensors
  to compare, monitor and correct the calibration of monitored instruments to community references
  by generating calibration corrections
  with specified uncertainties
  through well-documented, peer-reviewed procedures
  based on various techniques to ensure consistent and robust results
Delivery to users
  Free and open access
  Adopting community standards
To promote
  Greater understanding of instruments’ absolute calibration, by analysing the root causes of biases
  More accurate and more globally consistent retrieved L2 products
  Inter-operability for more accurate environmental, climate and weather forecasting products
TRACEABILITY / UNBROKEN CHAINS OF COMPARISONS

## Slide 4: Who are the targeted users?
FCDR
TCDR
GSICS
SCOPE-CM
Statement of Needs
Level 1b/c Data
(Radiances)
GOS
Corrections
Any activity requiring well calibrated Level 1 data acquired by the satellites covered by GSICS
Level 2 products (geophysical parameters)
Climate applications
Example of user = the SCOPE-CM initiative (Sustained Coordinated Processing of Environmental Satellite Data for Climate Monitoring)
Scope  generate multi-mission and global satellite climate data records (Fundamental CDRs & Thematic CDRs)
 The way toward operational production of high quality ECVs on a global scale
Notes: GSICS provides corrections (with respect to selected references) that can be applied to generate FCDRs
SCOPE-CM generates FCDRs and related TCDRs

## Slide 5: GSICS User Community
Satellite Application Community
  CDR generation for climate monitoring “SCOPE-CM” framework, national/international programs WCRP/ISCCP - (Planned beta-testing of GEO GSICS Corrections)
  Reanalysis community for climate modelling (ECMWF reanalysis – 2012/15)
  Operational NWP: direct radiance assimilation
  Other users interested in accurate/consistent calibration
Satellite Operators
  Prelaunch instrument characterization guidelines
  Cal/Val Plans
  Best practices for instrument monitoring and improved calibration
Affiliation with partner programmes
  CEOS WGCV, GPM X-cal, GHRSST, GRUAN, etc...

## Slide 6: GSICS Products
GSICS Bias Monitoring
  Routine comparisons of satellite radiances against reference
GSICS Correction
  Function to correct issued radiances
  For consistent calibration with reference
GSICS Reports & Guidelines
  Recommendations to modify practices
  Design and Operation of future satellite instruments
For Operational Environmental Satellites
   Infra-red recalibration (GEO and LEO)  Pre-Operational & Demo status
  (current operational satellites)  Near real-time and re-analysis
   Visible and near-infrared recalibration (GEO and LEO)  In development within GSICS
   Microwave – Conical & Cross-track Scanners (LEO)  In development with GPM XCAL
   Historic Instruments  In development at EUMETSAT…

## Slide 7: GSICS Procedure for Product Acceptance
Products progress from
  Demonstration Mode
Through
  Pre-Operational Mode
To
  Operational Mode
By a series of reviews
Over period of ~1.5yr
Subject to meeting acceptance criteria

## Slide 8: GSICS Products
Developed by GSICS:
  GEO-LEO IR – Prototype-Demonstration-Pre-Op
  GEO-LEO VIS – In Development
  GEO-LEO Archive Re-Calibration – In Development
Developed by 3rd parties:
  PATMOS-X
  AMSU-MSU
  GPM XCAL?

## Slide 9: GEO-LEO IR Product Status 2013-04
GPRC | Monitored Instrument | Reference Instrument | GSICS NRT Correction | GSICS Re-Analysis Correction | GSICS Bias Monitoring
EUMETSAT | Meteosat-10} Meteosat-9 } -- Meteosat-8 } Meteosat-7 } | IASI | Pre-operational Demonstration | Pre-operational Demonstration | Prototype
JMA | MTSAT-1R } MTSAT-2 } | IASI (+ AIRS) | Demonstration | Demonstration | Prototype
NOAA | GOES-13 & -15 Imager GOES-11 & -12 Imager | IASI (+ AIRS) | Pre-operational | Pre-operational Demonstration | Prototype
 | GOES Sounder | IASI (+ AIRS) | In development | In development | In development
CMA | FY2C } FY2D } -- FY2E } | IASI (+ AIRS) | In development | In development | Prototype
KMA | COMS | IASI (+ AIRS) | In development | In development | In development
Full GSICS Product Catalog available at http://www.star.nesdis.noaa.gov/smcd/GCC/ProductCatalog.php

## Slide 10: Comparison of Collocated GEO-LEO Radiances
Simultaneous near-Nadir Overpass
of GEO imager and LEO sounder
Collocation Criteria:
ΔLat<35° ΔLon<35°
Δt < 5 mins
Δsecθ < 0.01 (Atmospheric path diff.)
Concentrated in tropics
~1000 collocations/orbit
~1 orbit/night
Schematic illustration of the geostationary orbit (GEO) and polar low Earth orbit (LEO) satellites and distribution of their collocated observations.

## Slide 11: Data Transformations (Spectral and Spatial)
Spectral Convolution:
Convolve LEO Radiance Spectra with GEO Spectral Response Functions
to synthesise radiance in GEO channels
Spatial Averaging:
Average GEO pixels in each LEO FoV
Estimate uncertainty
  due to spatial variability
  as Standard Deviation of GEO pixels
Use in weighted regression
LEO FoV~10km
~ 3x3 GEO pixels
Example radiance spectra measured by IASI (black) and modeled by LBLRTM (grey), convolved with the Spectral Response Functions of SEVIRI channels 3-11 from right to left (colored shaded areas). n.b. The IASI observations (645 – 2760 cm-1) do not quite cover the full spectrum observed by SEVIRI.
Illustration of spatial transformation. Small circles represent the GEO FoVs and the two large circles represent the LEO FoV for the extreme cases of FY2-IASI, where nxm=3x3 and SEVIRI-IASI, where nxm=5x5.
Notes: The next step is to transform the collocated data to allow direct comparisons between the instruments.
Firstly, the IASI radiance spectra is convolved with the Spectral Response Functions of the Meteosat channels, to calculate the expected radiance in each Meteosat channel.
Then the Meteosat pixels within each IASI iFoV are averaged.
Their variance is also calculated to quantify the uncertainty due to spatial variability and
is used to weight each collocation in a linear regression …

## Slide 12: Comparison by Regression
Compare collocated obs:
GEO radiance
  Spatially averaged
Regressed against
LEO radiance spectra,
  convolved with GEO SRF
Using Variance of GEO radiances + Noise
  to estimate uncertainty on each collocation
Weighted linear regression of LGEO|REF and <LGEO> for Meteosat-9 13.4μm channel based on single overpass of IASI

## Slide 13: GSICS Products: (1/3) Bias Monitoring
Comparing samples of xMON , xREF
  − Over fixed domain
  − Period (e.g. 1 orbit/1 day)
  − Typically ~ 1000 comparable samples/day
Regression
Calc bias, ∆x=xMON-xREF
  − ∆x at standard scene, xSTD
  − with uncertainty
Plot time series of bias ∆x
  − Compare recent results with long-term trend
  − Valuable for instrument monitoring
xREF
xMON
∆x
t
∆x
xSTD
Notes: 13

## Slide 14
Example of GSICS Bias Monitoring
From EUMETSAT: Time Series of Meteosat10-IASI Standard Biases [K]

## Slide 15: GSICS Products: (2/3) GSICS Correction
Compare all xREF , xMON samples
  − over smoothing period (e.g. 2 weeks)
Regression coefficients
  with uncertainty (covariance)
Provide a function users can apply
  to convert level 1 data, xMON
  to be consistent with calibration of reference, xREF
Two versions:
  Near Real-Time (asymmetric time window)
  Re-Analysis (symmetric time window)
xREF
xMON
GSICS Correction function

## Slide 16: GSICS Products: (3/3) Guidelines
Underlying assumption of GSICS Correction:
  Small errors (e.g. SRF errors, blackbody temperature, ...) introduce small departures from ‘true’ calibration
  If these are linearly related to a predictor (radiance, time, ...) we can apply empirical correction based on inter-calibration
Guidelines can analyse GSICS products
  to diagnose root causes of calibration errors
Can derive recommendations to modify
  operating practices (e.g. adopt new SRF definition),
  pre-launch characterisation, etc.
These GSICS Guidelines are distributed as written reports

## Slide 17: Quality Indicators in GSICS Products
GSICS Correction Coefficients include
  Estimates of uncertainties and covariances
  For GEO-LEO IR:
    From weighted linear regression
    Using spatial variance and radiometric noise of each collocated observation as weighting
Shown as error bars in GSICS Bias Monitoring plots
But many other processes introduce uncertainty
  Systematic and Random
Need to validate these quality indicators

## Slide 18: GSICS Product Developments 2012
GSICS Corrections for GEO-LEO IR
  Now Pre-Operational for Meteosat (EUMETSAT) & GOES (NOAA)
  Nearly Pre-Operational for MTSAT (JMA)
  Using MetopA/IASI as reference
Developing GSICS Products for GEO-LEO VIS:
  Deep Convective Clouds (DCC)
  Ocean Targets (Rayleigh Scattering)
  Lunar & other methods (deserts, liquid water cloud, …)
Special Issue

## Slide 19: Special Issue on Satellite Inter-Calibration
IEEE Transactions on Geoscience and Remote Sensing
On inter-calibration of satellite instruments
5 Guest GSICS/IVOS Editors
40 papers – incl. 13 Open Access
  From CAS, CMA, CNES, ESA, EUMETSAT, ISRO, JAXA, KMA, JMA, MIT, NASA, NOAA, SDSU, USGS, etc.
  Covering AVHRR, AMSU, (A)ATSR, CLARREO, ETM+, FY-2 & -3B, GOES, HIRS, Hyperion, IASI, Jason-2/OSTM, MODIS, PROBA, SCAIMACHY, Sentinel-2, etc.
Published March 2013

## Slide 20: GSICS Correction for GEO-LEO IR

## Slide 21: GSICS Product Development Plan 2013
GSICS Corrections for GEO-LEO IR:
  Operational Mode for Meteosats, GOES & MTSAT
  Prototype for other GEOs
  Delta Correction to transfer MetopA/IASI to MetopB/IASI
  Quantifying diurnal cycle uncertainties
GSICS Products for GEO-LEO VIS:
  Deep Convective Clouds (DCC) -> Demonstration Mode
  Lunar -> Prototype
  Ocean Targets (Rayleigh Scattering) + LEO-LEO -> Prototype
  Other methods -> continue developments
GSICS Guidelines:
  How to select a reference instrument
  How to specify Spectral Band Adjustment Factors (IR+VIS)

## Slide 22: EUMETSAT’s GSICS Product Development Plan
DRAFT
GEO-LEO IR

## Slide 23: Where to get the data?
GSICS Bias Monitoring (prototype)
  Hosted on websites of GSICS Processing & Research Centres (GPRCs)
GSICS Corrections
  GSICS Data & Products Servers
  THREDDS-based system
  − NetCDF format
  − WMO GTS standard file names
  − Unidata & CF conventions
  See gsics.wmo.int for links
GTS = Global Telecommunication System
CF = Climate and Forecast

## Slide 24: Thank You