## Slide 1: The PROBA-V Mission
Sindy Sterckx, Wouter Dierckx, Tanja Van Achteren, Stefan Adriaensen and the PROBA-V team
GSICS Users' Workshop, 2013

## Slide 2: Content
The PROBA-V mission
  Objective
  Design
User involvement
CAL/VAL

## Slide 3
Belgian-ESA mission
Mission objective :
  Continuity of SPOT VEGETATION data
    4 spectral bands: B, R, NIR, SWIR
  Daily global coverage of land masses
    Total swath width 2295 km
    14 near polar orbits per day @ 820 km
Launch :
  End of April 2013, Kourou
  VEGA launcher

## Slide 4
global world archive since 1998 www.spot-vegetation.com
P-product (segment)
daily synthesis
10-daily synthesis
15 years SPOT VEGETATION
Daily global vegetation monitoring (1 km)

## Slide 5
CONTINUITY (1km and 330m)
Daily global vegetation monitoring

## Slide 6: PROBA-V is not SPOT
 | SPOT-4 | SPOT-5 | PROBA-V
volume | 2x2x5.6 m3 | 3.1x3.1x5.7 m3 | 0.8x0.8x1 m3
mass | 2760 kg | 3 000 kg | 160 kg
power | 2100 W | 2100 W | 153 W
> 200 x smaller
> 20 x lighter

## Slide 7: And the instruments are not the same
The PROBA-V Payload
Mass: 33.3 kg [20% of total]
Dimensions: 0.2x0.8x0.4 m³
Three imagers, TMA concept
No active thermal control
No on-board calibration lamp

## Slide 8: User involvement
Through the PROBA-V Preparatory Programma
Purpose:
  to asses PROBA-V as a continuity mission to VGT1/2
  to get future users acquainted with the data of the PROBA-V “continuity mission” by using simulated data
  to prepare the full exploitation of Proba-V data sets
22 teams involved
    Thematic (Change detection, Crop monitoring, …)
    Methodological (Data fusion, impact studies, …)

## Slide 9: User involvement
Through the Proba V International Users Committee - IUC
What : Group of experts with expertise in global monitoring, image analysis, ground segment operations, calibration
Purpose : assist the project team in refining and adapting the characteristics of the system
Topics : Products, Geolocation budget, straylight, compression, atmospheric correction, cloud detection, PROBA-V – VGT spectral response differences, ….

## Slide 10
Interband
Sun Glint
Oceans
Deserts
DC Clouds
Antarctica/Greenland
Multi Angular
Temporal
RC – IQC: Vicarious Calibration Concept

## Slide 11
RC- Image Quality Center: HM
fully automated image workflows and statiscal processing
View at the database using Graphical User Interface
Full traceability new instrument calibration parameters updates
Automated distribution towards production

## Slide 12
Method validation activities on VGT data
Rayleigh Calibration DCC calibration
Sterckx S., Adriaensen S., Livens S.,TGARS, 2013

## Slide 13
CEOS method intercomparison activity
Calibration over stable desert sites
Govaerts, Y., Sterckx S. and Adriaensen S., 2013, Remote Sensing Letters.
LIBYA 4

## Slide 14: Launching soon…
Launch
20 april
Start of in-flight calibration End of June
Data service operational Beginning of November
First Proba-V Conference
4 -5 July, 2013

## Slide 15: Thank you for listening!
The VITO PROBA-V team