## Slide 1: GOES-R Program Instrument and L1b Product Calibration/Validation GSICS Users’ Conference April 8, 2013
Bob Iacovazzi, Jr.
GOES-R Program Systems Engineering (PSE) Cal/Val Lead
Notes: To-Do:

## Slide 2: Importance of Calibration & Validation
Calibration: The process to determine factors for converting and correcting raw detector measurements into science data units (e.g., radiance) with the specified level of accuracy.
  Calibration is applied to GOES-R raw instrument data to transform them into L1b measurements … the fundamental building blocks for all L2+ products.
  Validation provides user confidence that GOES-R data can be used for their intended purpose, e.g., weather forecasting or numerical weather prediction.
Validation: The process of determining that the deliverable item satisfies its intended use in its intended environment.
GOES-R cal/val requirements are integrated into mission requirements!
Notes: To-Do:

## Slide 3: GOES-R Cal/Val Scope
  Pre-launch calibration/L1B validation
    Observe, and validate results of, pre-launch instrument-level calibration tests
    Evaluate instrument performance risks and waiver requests
    Provide subject matter expert (SME) review of L1b algorithm design and implementation
    Develop Cal/Val related Post-Launch Test (PLT) planning
    Develop tools for post-launch validation and anomaly resolution of L1b science data quality
  Validate expected results from pre-launch system level testing of L1b algorithm using synthetic L0 data
  Analyze PLT cal/val data results and provide SME support of science data anomaly resolution
  Coordinate cal/val activities through PLT and Handover
  Prepare NOAA satellite calibration scientists and engineers for monitoring, analyzing and maintaining GOES-R series instrument calibration and product integrity after Handover
GOES-R cal/val enhances understanding of data quality, and encourages “Day-1” operational readiness and long-term user confidence.
Notes: To-Do:

## Slide 4
GOES-R Program Cal/Val Documents
Calibration and Product Validation Strategy
Cal/Val Plan Vol. 1: L1b Data
Cal/Val Plan Vol 2: L2+ Product Val
All documents at CDR-level - Scope defined, technical methods mature, organizational role and responsibilities and processes defined, resources allocated, and schedules defined.
Cal/Val Methods and Processes
Scope, Organizations & Working Groups, Roles & Responsibilities, Resources, and Schedules
Notes: To-Do:

## Slide 5: Instr Cal and Cal Test Report Review: ABI
CWG conducted detailed data analysis on pre-launch tests for proto-type model (PTM)
Emissive (top) and Reflective (bottom) channel calibration test arrangement
Anomalies caused by not using actual scan mirror reflectance value
Reflective and emissive channel calibration
Coherent noise
Irradiance calibration
MTF-Focus-Registration
Emissive (left) and reflective (right) channel calibration test results - ratio of CWG to Exelis cal coefficient
Coherent noise test results
Exelis
CWG
Government analysis of vendor cal testing reports scrutinizes reproducibility of results and provides valuable feedback to the testing process.

## Slide 6: Instr Cal and Cal Test Report Review: NIST support for ABI and EXIS
Witness filter characterization (ongoing)
Reflective channel radiance scale validation via visible transfer radiometer (VXR) (planning)
FEL-based irradiance scale validation: uniformity test (completed)
Spectral response and irradiance characterization via SIRCUS (completed)
Characterization of external blackbody via thermal transfer radiometer (TXR) (completed)
EXIS testing at Synchrotron Ultraviolet Radiation Facillity-III (completed)
Traveling SIRCUS (Spectral Irradiance and Radiance Responsivity Calibration Using Uniform Sources)
Spatial uniformity results at three distances, z.
Spatial uniformity setup
0.1% contours
NIST testing provides independent validation of instrument performance and in some cases traceability to international standards.

## Slide 7
Post-launch Testing On-orbit Checkout
GOES-13 Hemispheric Image Tiles
KPP product quality evaluation
Calibration input parameter evaluation
GOES-10 Ch. 4A Corrected and uncorrected Radiance vs. scan angle. (Beaucom et al., Proceedings of SPIE, 1999)
On-board calibration system evaluation
Instrument Noise, Blackbody Temp and Cal Slope Monitoring
LEO Hyperspectral Sounder vs. GEO Inter-comparison (Courtesy of Wu et al.)
Radiance [mW/(m^2-sr-cm^-1)]
Notes: To-Do:

## Slide 8
Post-launch Anomaly Resolution
GOES-13 Eclipse Season Stray Light
GOES-13 Eclipse Season Stray Light Before Fix (Top) and After Fix (Bottom) (Courtesy of J. Paul Douglas, OSPO)
Stray Light
Strongly coordinated efforts between Cal Collaborators will be essential to success of post-launch instrument and L1b performance anomaly resolution efforts.

## Slide 9
Post-Launch Testing Environmental Calibration Initialization
GEO-LEO ABI and GLM Radiometric Cal and INR
Vicarious Calibration
Moon ABI Radiometric Cal, MTF and Band-to-band Registration
Desert and Instrumented Sites ABI Radiometric Cal
White Sands Missile Range
Sonora Desert
Deep Convective Clouds ABI and GLM Radiometric Cal
Satellite Inter-Calibration
Stars ABI Radiometric Cal
Activity near the end of PLT for L1b validation and creating a “state-of-the-cal” snapshot for long-term calibration trending
GEO-GEO ABI and GLM Radiometric Cal and INR
ARM and SURFRAD

## Slide 10
Mission-life sensor parameter and derived product trending
GOES-10
Application of ABI Long-term Radiometric Performance tool to GOES-10. (Wu et al., GSICS Monthly Web Seminar, Dec. 2011, https://gsics.nesdis.noaa.gov/wiki/ Development/20111213)
Tropical Rainfall Measurement Mission Lightning Imaging Sensor (LIS)
Application of GLM Long-term Radiometric Performance tool to LIS (Buechler et al., Atmos. Res., 2012)
Application of ABI Co-Registration Validation tool to the GOES Imager. (Grotenhuis, Proc. SPIE 8510, 85101T 2012.)
Cal activities required during GOES-R acquisition enables long-term monitoring, analysis and maintenance of GOES-R product quality after Handover.

## Slide 11
GOES-R Program Calibration and Validation
Robert A. Iacovazzi, Jr.* (1), Edward C. Grigsby (1), Steve Goodman (2), Changyong Cao (3), Jaime Daniels (3), and Kathleen McIntyre (1)
NASA (1), NOAA/NESDIS/GOES-R (2), and NOAA/NESDIS/STAR (3)
E-mail-Robert.A.Iacovazzi@nasa.gov Physical Address - NASA GSFC, Code 410.0, 8800 Greenbelt Rd, Greenbelt, MD 20771
  Pre-launch Cal/Val
    Vendor instrument calibration testing
    Government team validation of testing results
    L1b algorithm design and implementation
  Post-Launch Testing (PLT) Cal/Val
    GOES-R observatory cal/val assets
    Product quality evaluation
    On-board calibration system evaluation
    On-orbit calibration and L1b product anomaly resolution
Example comparison between GOES-R CWG and Vendor cal test analyses: Ratio of CWG to Exelis cal coefficients for ABI reflective channels.
Before (left) and after (right) Government-Vendor reconciliation of scan mirror reflectance value used in ABI test data analysis.
GOES-13 Hemispheric Image Tiles
Determine and Correct Scan-Angle Dependent Radiance (e.g., Beaucom et al., Proceedings of SPIE, 1999)
Instrument Noise, Blackbody Temp and Cal Slope Monitoring
GOES-10 Ch. 4A
GOES-13 eclipse season stray light before fix (left) and after fix (right)
(Courtesy of J. Paul Douglas, OSPO)
Focus on GOES-R Instrument Calibration/ Validation (Cal/Val) and L1b Product Val
Poster Session I: 10:15 am Tuesday April 9.
Notes: To-Do:

## Slide 12
Development Integration and Testing
GOES-R Pre-Launch Milestones
Program/System |  |  | 
Flight Segment |  |  | 
Ground Segment |  |  | 
System Design Review complete
All instruments have passed CDR
100 % delivery of baseline product algorithms
Spacecraft
Instruments
S/C SDR complete
ABI Delta CDR complete
Core GS PDR completed
Antenna System PDR completed
GS Project PDR complete
 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015
Mission PDR Part I
Mission PDR Part II
S/C PDR complete
S/C CDR
ABI Delivery
SEISS Delivery
EXIS Delivery
SUVI Delivery
GLM Delivery
Mission CDR
Antenna System CDR
GS Project CDR
ESPDS CDR
CLASS CDR
RBU/NSOF/WCDAS installation
WCDAS complete
Launch Readiness Oct. 2015
RBU complete
NSOF complete
Core GS CDR
MAG Delivery
Notes: To-Do: