## Slide 1: Vis/NIR Inter-Calibration Product Announcements
David Doelling
(NASA) (GRWG Vis/NIR Sub-Group Chair)
Special Issue of the IEEE TGRS on “Inter-Calibration of Satellite Instruments”:
Special Issue of the IEEE TGRS on “Inter-Calibration of Satellite Instruments”:

## Slide 2: Overview
GSICS VIS/NIR calibration strategy
Lunar Calibration status
DCC Calibration status
Discussion

## Slide 3: GSICS VIS/NIR calibration strategy
Use lunar and Deep Convective Clouds (DCC) calibration to determine the stability of the sensor and to tie the calibration to an absolute reference
  All GEOs can observe moon and DCC without special operations and with the same earth viewing optics, therefor all GEO calibration centers can uniformly apply the same calibration techniques
  All 1st and 2nd generation GEOs lack un-board calibration

## Slide 4: GSICS VIS/NIR calibration strategy
Combine lunar and DCC visible calibration gains as the final GSICS calibration
  Consistent multiple calibration results validates all techniques
  The combined gain will have a smaller uncertainty than any individual method gain
  Individual method gains will be made available so that the user may determine calibration method best suited for the application

## Slide 5: GSICS VIS/NIR calibration strategy
Use Aqua-MODIS Band 1 Collection 6 radiances as the absolute reference
  Migrate to NPP-VIIRS
  Have an unbroken chain of traceable calibration reference records
  The reference record chain is then tied to an SI-traceable on-orbit calibration system sensor, such as CLARREO or TRUTHS

## Slide 6: GSICS VIS/NIR calibration strategy
Use SCIAMACHY based spectral band adjustment factors (SBAF) to take into account spectral differences between the reference and target instrument
  If there were a well-calibrated hyper-spectral sensor there would be no need for SBAF
  The SBAF need to be unique to the spectra used over the GEO and reference sensor intercalibration site

## Slide 7: Lunar Calibration Status
GIRO algorithm and GLOD dataset
  Initiated at the GSICS lunar calibration workshop at EUMETSAT, Dec 1-4 , 2014
  Have a follow on GSICS lunar workshop before May 2016
  GIRO is the GSICS implementation of the USGS ROLO model provides uniform implementation across GEO calibration centers

## Slide 8: Lunar Calibration Status
GLOD dataset
  GLOD is the GISCS Lunar Observation dataset designed to improve the ROLO model
  EUMETSAT, CNES, NOAA, JMA, KMA, NASA have provided many lunar images
  Recently ISRO, JMA and KMA presented updated results using GIRO.
  Very large amount of Himawari-8 acquisitions
    Useful for preparing MTG/FCI

## Slide 9: Lunar Calibration Next Steps
Uncertainty Estimation
  Accurate estimation of the over-sampling factor
  Benchmarks to access improvements of GIRO
Accounting for spectral differences between instruments
  using hyper-spectral instruments with Moon observations (GOME-2, Hyperion, SCIAMACHY
Establishing an absolute scale for lunar calibration
  using Aqua MODIS / NPP VIIRS as references)

## Slide 10: DCC Calibration Status
NASA DCC calibration algorithm implementation is underway across GEO calibration centers
  NASA provided test datasets for uniform implementation
  EUMETSAT has written the DCC calibration ATBD
  Visible calibration file format and plotting discussed
Preparing for Demo product in 2016

## Slide 11: DCC Calibration Plans
DCC observed reflectances have GEO domain specific seasonal cycle that needs to be removed
Apply algorithm to other GEO visible channels
Estimate the DCC calibration uncertainty
  Need to estimate the GEO domain DCC reflectance inter-annual variability
  Need to estimate the reference sensor calibration transfer error to tie GEO domain DCC reflectance

## Slide 12: Spectral Band Adjustment Factor (SBAF)
Web site available for SBAF over many SCIAMACHY based Earth reflected spectra
  http://www-angler.larc.nasa.gov/cgi-bin/site/showdoc?docid=223
  Maybe down due to scheduled maintenance
Future Plans
  Incorporate Hyperion, and GOME-2 observations
  Incorporate ROLO model observations

## Slide 13
Thank You
Any thoughts for Discussion
Notes: 13