## Slide 1: How to access GSICS data products? Servers, Catalogs, and Tools
Manik Bali, Tim Hewison, Lawrence.E. Flynn
GSICS Users Workshop
Sept 22, 2015, Toulouse, France

## Slide 2: Outline
Introduction-GSICS Products.
How do we access GSICS products
GSICS Products Types.
How is it hosted (servers, mirroring etc).
GSICS Product standards and maturity.
Tools- Plot a Product.
Apply GSICS correction in two easy steps.
Glimpse into the future

## Slide 3
GSICS has 37 Inter-calibration products spanning IR and VIS wavelengths.
Products have bias, offset and uncertainty estimates.
Introduction- GSICS Products
Before Correction 3K Bias
After Correction ~ 0K Bias
Example of application of GSICS Correction on GOES-12 ( Goldberg et. al., 2012)
Products helpful in reducing bias w.r.t stable reference
Applied on GEO( AHI, GOES, MTSAT, SEVIRI, FY-3, INSAT) and LEO (AVHRR)

## Slide 4: How do we access the GSICS product
GSICS Products are accessed via the GSICS Product Catalog go to http://www.star.nesdis.noaa.gov/smcd/GCC/ProductCatalog.php
New (Beta) Version Product Catalog http://www.star.nesdis.noaa.gov/smcd/GCC/GCCBeta/index.php [Which one do you prefer ?]
On a scale of 1-10 rate this. Simple or complex

## Slide 5: GSICS Product Types
NRT ( Near Real Time) Corrections
Re-Analysis Correction (Archive Recalibration Products).
GSICS Correction is computed for every day. To reduce the random component of uncertainty, correction is derived from data over 29- and 15-day time periods for Re-Analysis Correction (RAC) and Near Real Time Correction (NRTC), respectively. The smoothing period for RAC is t - 14 days to t + 14 days, and that for NRTC is t - 14 days to t + 0 days (where t is the date of validity).
Is this classification of Types relevant to you ?

## Slide 6: GSICS Product Maturity and Standards
GSICS Products are presented in NetCDF format.
Easy to read by any high level language ( IDL, FORTRAN, MATLAB)
The contents of data file are mainly bias and offset, Uncertainity.
The file contents follow CF 1.6 metadata standards.
Some agencies (eg. EUMETSAT) have included GSICS Coeff. ( bias, offset and uncertainty )
in their L1B data file.
GSICS Procedure for Product Acceptance is a scale used to assign maturity to GSICS Products
Do you need a maturity scale ?

## Slide 7: GSICS IR METADATA STANDARD: Global Attributes:
:Conventions = "CF-1.6" ;
:Metadata_Conventions = "Unidata Dataset Discovery v1.0" ;
:standard_name_vocabulary = "CF Standard Name Table (Version 19, 22 March 2012)" ;
:project = "Global Space-based Inter-Calibration System <http://gsics.wmo.int>" ;
:title = "MSG2+SEVIRI vs MetOpA+IASI GSICS Near Real-Time Correction" ;
:summary = "Coefficients of the GSICS Correction for the infrared channels of a GEOstationary imager using a LEO hyperspectral reference instrument"
:institution = "EUMETSAT" ;
:date_created = "2015-01-09T13:16:55Z" ;
:date_modified = "2015-01-09T13:16:55Z" ;
:license = "Calibration information delivered as a GSICS operational product is generated in accordance with GSICS principles and practices.;\n",
"GSICS operational and demonstration products may be used and redistributed freely. Scientific publications using GSICS operational or demonstration products should however acknowledge both GSICS and the relevant producer organization.;\n",
"There is no warranty on the data express or implied, including warranties of merchantability and fitness for a particular purpose, or any assumed legal liability for the accuracy, completeness, or usefulness, of this information. The user of the data do so at their own risk." ;
:naming_authority = "int.eumetsat.gsics" ;
:creator_name = "EUMETSAT - European Organization for the Exploitation of Meteorological Satellites" ;
:creator_email = "ops@eumetsat.int" ;
:creator_url = "http://www.eumetsat.int" ;
:references = "ATBD, Unidata NetCDF, Climate Format Conventions, EUMETSAT IASI 1C Native Format Guide" ;
:
Meta data aims to answer the 6W’s about the data
Who What Where When Why How
Do you need this level of detail in the meta data to use the product
Or simply the bias offset and uncertainty good enough ?

## Slide 8: Plot a GSICS Product
A Plotting tool has been developed at EUMETSAT. The tool enables on to get a measure of bias and offset computed
Go To: http://gsics.tools.eumetsat.int/plotter/
Do you have any suggestions by which we can improve this tool?

## Slide 9
Meteosat-7 clear sky water vapor radiances in bufr format, from EUMETSAT ( www.eumetsat.int) )
METEOSAT7-MVIRI-MTPCSKR-NA-1-20140731030259.000000000Z-1145972.bfr
GSICS correction coefficients in netcdf format, from EUMETSAT (www.eumetsat.int)
W_XX-EUMETSAT-Darmstadt,SATCAL+NRTC+GEOLEOIR,MET7+MVIRI MetOpA+IASI_C_EUMG_20140703000000_demo_03
Courtsey: Randhir Singh, ISRO
Meteosat-7 Water vapor radiances and GSICS coefficients
Apply correction in two easy steps GSICS Product
Step 1. Select the correct combination of GSICS Product data file and L1 data

## Slide 10
Step 2. Apply the formula to get the corrected radiances
L(LEO)=-offset/slope+(1/slope)*(L(GEO))
GSICS
Apply correction in two easy steps GSICS Product
Rate the ease of use on a scale of 1 -10

## Slide 11: Upcoming Products Deliverables
VIS – Lunar Calibration Products submitted for GPPA
ISRO product in GPPA ( Kalpana IASI ) cross calibration.
Primary reference product in GPPA
User guides for these products to be available soon
via the product catalog soon.
GSICS is working on making available SNO algorithms , reference data sets and components of FCDR as deliverables.
Take the Survey and help us frame our future to server you better

## Slide 12: Summary
37 GSICS Inter-Calibration Products
  Available online free via the product catalog
  Easy to use ( two simple steps)
  Matured User guides available for each product
Products Undergo Stringent/Efficient maturity process.
Easy to Visualize via online plotting tool.
Calibration coeff. also available in L1data file ( EUMETSAT)