## Slide 1: Preliminary SCIAMACHY Lunar observations as intercalibration source
That’s no moon,
It’s a calibration source
Ralph Snel
Matthijs Krijger

## Slide 2
SCIAMACHY
SCIAMACHY Lunar Observations
SCIAMACHY Degradation
SCIAMACHY Calibration
Future

## Slide 3: SCIAMACHY on ENVISAT

## Slide 4: Primary purpose
The main objectives of the SCIAMACHY mission are
to improve our knowledge of global atmospheric composition,
its change in response to both natural and anthropogenic activity and the processes associated to it, as well as
the related global issues of importance to the chemistry and physics of our atmosphere
Monitor the Earth atmosphere (gases, aerosols, clouds) in reflected sunlight

## Slide 5: The instrument
Imaging spectrometer
Spatial dimensions through scan mirror(s):
  IFoV: 0.045 degrees by 1.8 degrees
Spectral dimension through 8-channel spectrometer, 8192 wavelengths:
  214 nm to 1773 nm
  1934 nm to 2044 nm
  2259 nm to 2386 nm
Nadir, Limb, sub-solar, solar occultation and lunar occultation views
Many in-flight calibration and monitoring modes

## Slide 6: SCIAMACHY viewing modes

## Slide 7: Lunar observations
2 types of lunar observation:
Lunar pointing using sun/moon follower (state ID 56 and 57)
Lunar scanning, using sun/moon follower + superimposed scan of 0.66 degrees edge to edge (state ID 54)
State IDs 56 and 57 show only a slice of the moon, not suited for this study
State ID 54 shows the entire moon in the scans, 1-dimensional “image” in elevation direction:
  2 pixels high in 8192 wavelengths
  80 pixels high in 7 Polarisation Measurement Devices (PMDs), broadband linear polarisation, 6 wavelengths, 2 polarisation directions (90 and 45 degrees)

## Slide 8: Number of lunar spectra
1112 orbits with State ID 54 (between 2002-12-16 and 2012-04-07)
Focus here on 400 orbits between beginning 2003 and beginning 2008
Dedicated lunar calibration campaign mid to end 2006 included
Total number of spectra over the 400 orbits about 26000 spectra, 1 second per spectrum

## Slide 9: Lunar phase angle coverage (1)

## Slide 10: Lunar phase angle coverage (2)

## Slide 11: Lunar libration angle coverage

## Slide 12: SCIAMACHY lunar albedo (1)

## Slide 13: SCIAMACHY lunar albedo (2)

## Slide 14: SCIAMACHY lunar albedo fit RMS

## Slide 15: SCIAMACHY Degradation

## Slide 16: SCIA Lunar Degradation (1)

## Slide 17: SCIA Lunar Degradation (2)

## Slide 18: SCIA Lunar Degradation (3)

## Slide 19: SCIA Lunar Degradation (4)

## Slide 20: SCIA Lunar Degradation (5)

## Slide 21: SCIA Phase Angle (1)

## Slide 22: SCIA Phase Angle (2)

## Slide 23: SCIA ASM Angle (1)

## Slide 24: SCIA ASM Angle (2)

## Slide 25: SCIA ASM angle (3)
On-ground
Calibrated

## Slide 26: Future
SCIAMACHY ASM-dependence
SCIAMACHY Polarization
SCIAMACHY Absolute Calibration
Put the moon to good use

## Slide 27
Potential uses:
SBAFs:
MSG1 Vis 006 –
Aqua Ch 1

## Slide 28: Summary
SCIAMACHY
  High (0.25nm) resolution lunar spectrum
  Precise (<0.5%) lunar spectrum
  Many (~1100) lunar measurements
  Different geometries
  New improved calibration (mirror model)
Good (relative) agreement ROLO/GIRO (<0.5%)

## Slide 29
Thank you