## Slide 1
Sterna Constellation Inter-Calibration Implementation Plan
Tim Hewison

## Slide 2: Introduction to EPS-Sterna Inter-Calibration
EPS-Sterna = first EUMETSAT large constellation – (subject to approval)
  Consistency amongst the constellation is important for users
In addition to requirements on bias, temporal and spatial stability,
  STERNA-EURD-00025 requires Level 1b data from instruments of the constellation shall be characterised by cross-calibration against a reference, throughout the mission lifetime
Inter-calibration* algorithms under development:
  SNO, GNSSRO – in cooperation with USC
  OCTM (“Warm SNO”), Vicarious – Study with Indra/UPC
  NWP Double-differencing – through ECMWF WO
  See Presentation 7k from 2025 Annual GSICS meeting
* “Inter-calibration" does not necessarily imply calibration corrections are actively applied,
  just that the calibration of the instruments is assessed by comparison with an external reference
  allowing adjustments to be made where necessary
Currently developing plan to implement inter-calibration operationally in constellation
  Approach may be applicable to other constellations

## Slide 3: Initial Inter-calibration across Sterna Constellation
Perform comparisons of each member of constellation using inter-calibration algorithms With what?
  Reference instrument(s) defined by Community consensus (GSICS)
  Reference instrument(s) defined by EUMETSAT (may be same as above) – e.g. MWS (+ICI)
  Selected member of Sterna constellation (not applicable to first satellites)
  All other members of operational Sterna constellation (circular argument)
  NWP model background (inter-dependence + susceptible to changes) or Re-analysis (timeliness?)
During Commissioning: Analyse relative biases:
  As function of date / time / latitude / solar angle / geometry / radiance / scene type, …
  Fit calibration parameters to minimise biases – e.g. OBCT temp + emissivity, mirror reflectivity + temperature, Antenna Pattern Correction, nonlinearity
  Apply in Updated SCDB before going Operational (n.b. need traceability in L1B)
Need to automate process
  Can test with AWS data

## Slide 4: Ongoing Inter-calibration across Sterna Constellation
During Operational lifetime of each Sterna satellite:
  Monitor calibration using same inter-calibration algorithms
  Analyse residual biases
If calibration corrections are needed to achieve required bias levels – options to be discussed:
Repeat process used during commissioning and update SCDB - depending on calibration stability, as required to fulfil requirements: yearly/monthly/daily?
  Risks generating jumps in time series & consistency between global and local processors – not favoured approach
Develop empirical corrections – e.g. linear function of Tb, with time-varying coefficients – options:
  GSICS-like Corrections, distributed via Data Store (Can integrate via SatPy)
  GSICS-like Corrections, distributed as AUX files with L1
  Integrated into L1 products
    - implies interface requirements to ground segment + PFS Changes + Need to ensure consistency between global and local products
  Generate “L1G” product of all instruments in constellation, with calibration corrected to reference – where possible
    + Advantage: easy to use - but - Doubles data volume for constellation
    Could also be integrated into L1C (remapped L1B)
    – or other global grid – timeliness TBC – critical for nowcasting users!
    – ask users (if it is feasible!)

## Slide 5
Thank you!
Questions are welcome.