## Slide 1: Computing Lunar Geometry for CrIS Observations
Likun Wang
Cooperative Institute for Satellite Earth System Studies (CISESS)
Earth System Science Interdisciplinary Center (ESSIC),
University of Maryland, College Park, Maryland
Email address: wlikun@umd.edu

## Slide 2: Summary
Under current orbital configuration, the Moon enters the CrIS Space View every ~27.3 days.
It is very interesting to see how the CrIS space view spectra in three bands response differently when the Moon passes over the Space View.
  Now we treat it as lunar intrusion contamination
It should be realized that the IR sounder have relatively large filed of view.
  CrIS FOV size: 0.963 Degree
  Moon Angular Diameter : 0.54 Degree
  CrIS FOV cannot resolve the Moon, and the Moon cannot fully cover the FOV
However, how this data can help for current calibration is not clear yet.

## Slide 3: CrIS Scan Patterns and Specification
1.5 km (1 sigma)
Percentage of FOV size
FOV 5 size change with Scan

## Slide 4: Moon in Space View
70.3±0.04
CrIS Space View FOV Aperture ~ 0.968
FOR Aperture: 3.3 Degree
Xorb
Yorb
Zorb
Yaw
Roll
Pitch
Modified from Patt et al. (2005)

## Slide 5: Lunar intrusions in SPV
Celestial Equator
Ecliptic Equator
SPV
Circle
Space views project circles around celestial equator.
The lunar views occur when the Moon’s position falls between the two circles, dependent on seasons
70.3±0.04 Space View Angle

## Slide 6: CrIS Geometric Calibration Algorithm
Sensor Specific Algorithm
Common Geo Algorithm
Compute the LOS relative to S/C for each FOV (3x3) at each scan position (30)
Resolve LOS intersection with Earth Ellipsoid (LOS, mounting matrix, satellite attitude and ephemeris)

## Slide 7: CrIS Geometric Calibration Algorithm Sensor Specific Algorithm
SDR Algorithm Process
LOS in IOAR coordinate = ILS parameters (3x3)
Convert from IOAR to SSMF coordinate
3) Compute normal to SSM mirror in SSMF (30 Scan Pos)
4) Apply SSM mirror rotation to get LOS in SSMF coordinate
5) Convert from SSMF to SSMR coordinate
6) Convert from SSMR to IAR coordinate
7) Convert from IAR to SAR
8) SAR coordinate = SBF coordinate

## Slide 8: NOVAS Library
The Naval Observatory Vector Astrometry Software (NOVAS) is a software library for astrometry-related numerical computations. It is developed by the Astronomical Applications Department, United States Naval Observatory. Currently, NOVAS has three different editions, for C, Fortran, and Python.
Using for NOAA JPSS satellite geometry and geolocation calculations

## Slide 9: Calculate Lunar Vector
Using NOVAS library to compute Lunar Vector in ECI coordinate (time, x, y, z)
Convert Lunar Vector in ECI to one in the orbit coordinate using satellite position and speed (time, x y, z)
Convert Lunar Vector in the orbit coordinate to one in the spacecraft coordinate using satellite attitude (time, x y, z)

## Slide 10
FOV vectors in SSMF
Lunar vector in ECI
Lunar vector in S/C
SSM normal vector
at space view (SPV)
SPV FOV vectors in SSMF
SPV FOV vectors in SSMR
SPV FOV vector in IAR
FOV vectors in IOAR
IET
2 angles
Sat POS, VEL, ATT
70.3±0.04
3 angles
3 angles
3 angles
Reflected from SSM mirror
SPV FOV vector in SAR/SBF
SPV FOV vector in S/C
Check angle between two vectors
3x3 2 angles
<= FOV angle or FOR
mounting matrix
Yes
No
Moon in FOVs or FORs
New codes
Old procedures
Common Geo
CrIS SDR

## Slide 11: Geometric calculation
Space View Vector
Moon Vector
Sun Vector
α
β
α: the separation angle between space view
and moon vector. (<3.3 Degree in FOR, < 0.963
In FOV)
β : the separation angle between sun and moon vector, which can be converted into lunar phase or lunar illumination

## Slide 12: Model Predicted Lunar Intrusion: 2013
Lunar phase
Angle between SPV and moon
Periodic fitting line

## Slide 13: Pattern (1)
space view
Moon Trajectory

## Slide 14: Pattern 2
space view
Moon Trajectory

## Slide 15: Lunar Intrusion Animation in LWIR Space View: Spectrum changes with Moon moving in and out
Channel number
Counts

## Slide 16: Lunar Intrusion Animation in MWIR Space View: Spectrum changes with Moon moving in and out
Channel number
Counts

## Slide 17
Geometric Calculation
Space View counts
LWIR
MWIR
SWIR
Angles between
FOV and lunar vectors
At specific channel

## Slide 18
Geometric Calculation
Phase of Space View
Angles between
FOV and lunar vectors
LWIR
MWIR
SWIR
Im
Re
Normal SPV
Lunar contaminated
SPV
At specific channel

## Slide 19: Discussion
How can the lunar calibration help for IR calibration?
  Radiometric calibration: compared to the inter-calibration
  Spectral calibration: compared to the model calculations
  Geometric calibration: compared to the imager inter-calibration
What IR lunar models are needed?
  Band models? Spectral models? Different geometric configurations?
What lunar data are needed collected for IR sounders?
  Geometric? Counts? blackbody? Telemetry data?