## Slide 1: GSICS Agency Report 2025
Eun-Jeong Cha, Euidong Hwang, Hanbyul Lee, Daehyeon Oh
Korea Meteorological Administration

## Slide 2: Presentation Overview
GSICS Activities, Actions, and Achievements
Support to GDWG Activities
Support to GRWG Activities
Instruments Updates & Planned launches that are relevant to GSICS (stress new programs and significant accomplishments)
Calibration Major Updates

## Slide 3: Summary of KMA’s GSICS Activities, Actions, and Achievements
Achievements Summary
  Uncertainty Evaluation for AMI – IASI RAC product
Activities summary
  GK2A AMI IR channels
    Review the AMI IR products (NRTC, RAC) for MetOp-B/-C, NOAA-20/-21
    Updated the recalibration coefficients of COMS/MI – GK2A/AMI
  GK2A AMI VIS/NIR channels
    Updated Ray-matching (SNPP, NOAA-20 and -21 VIIRS)
    GSICS DCC (SNPP, NOAA-20 and -21 VIIRS)
    Lunar calibration (GIRO)
=> IR session
=> VIS/NIR + Lunar
session

## Slide 4: KMA’s Support to GDWG Activities
KMA GPRC Webpage
  Landing page
    https://nmsc.kma.go.kr/homepage/html/gsics/gsicsIntro.do (Korean, now open)
    http://nmsc.kma.go.kr/enhome/html/main/main.do (English, will be updated soon)
  Event logging: http
    http://nmsc.kma.go.kr/enhome/html/bbs/listNotice.do?bbsCd=00026
  GSICS monitoring pages
    IR (Metop-a/b/c IASI, NOAA-20/21, S-NPP CrIS)
    VIS Ray Matching(Terra MODIS, S-NPP, NOAA-20/21 VIIRS)
    Lunar(GIRO)

## Slide 5: KMA’s Support to GRWG Activities (1)
VIS/NIR
  Monitoring of GEO-LEO using Terra MODIS, S-NPP and NOAA-20/21 VIIRS
    Analyze Ray-Matching and GSICS DCC for long-term variation from September in 2019
※ Ray-Matching calibration data selected for DCC target
-> AMI and VIIRS Reflectance : < 0.8 for VIS band, < 0.6 and < 0.1 for NIR band

## Slide 6: KMA’s Support to GRWG Activities (2)
IR
  Monitoring of GEO-LEO using MetOp-B, -C/IASI, NOAA-20, -21/CrIS
    Application of gap-filling method to inter-calibrate with CrIS
    Demo phase for NRTC and RAC data (MetOp-B, -C/IASI, NOAA-20, -21/CrIS)
  Reprocessing the long-term data from COMS/MI – GK2A/AMI
    Update the recalibration coefficients for 3.8µm channel
      Reduced sensor to sensor jump
Original rad.
COMS
GK2A
Re-cal. rad.
Reduced
sensor to sensor jump
SW038
SW038

## Slide 7: GEO satellite program updates
 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030 | 2031 | 2032 | 2033 | 2034 | 2035 | 2036
GK2A |  |  |  |  |  |  |  |  |  |  |  |  | 
GK5 |  |  |  |  |  |  |  |  |  |  |  |  | 
GEO-KOMPSAT-2A (GK2A)
  AMI started meteorological observations in July 2019 and is scheduled to continue until 2031
  Payloads
    AMI is a meteorological imager that has 16 channels spread over the VIS/IR wavelength
    KSEM is a space weather monitor (Electron/Proton detectors and Magnetometer)
GEO-KOMPSAT-5 (GK5)
  GK5 development started in 2025 and is scheduled for launch in 2031
  Payloads
    GK5 imager has 18 channels spread over VIS/IR wavelength (some channels improved on spatial resolution)
    GK5`s space weather monitor consists of 4 sensors*
    * Electron/Proton detectors, Magnetometer and Satellite Charging Monitor
GK5 Imager | 
Wavelength(㎛) | Resolustion(km)
0.47 | 0.5
0.64 | 0.25
0.86 | 0.5
0.91 | 1
1.38 | 2
1.61 | 1
2.25 | 1
3.9 | 1
5.1 | 1
6.2 | 2
6.9 | 1
7.3 | 2
8.5 | 2
9.6 | 2
10.4 | 1
11.2 | 2
12.3 | 2
13.3 | 2
Main Development Phases
Operation for 10 years
Operation
Extended Op.
Launch
excluded 0.51µm in GK2A

## Slide 8: KMA’s Calibration Major Updates
NOAA21-VIIRS/CrIS as reference has been added
ray_matching(MODIS)
ray_matching(SNPP_VIIRS)
ray_matching(NOAA20_VIIRS)
ray_matching(NOAA21_VIRRS)
ray_matching(MODIS)
ray_matching(SNPP_VIIRS)
ray_matching(NOAA20_VIIRS)
ray_matching(NOAA21_VIRRS)

## Slide 9: KMA’s Calibration Results (VIS/NIR) (1)
January to December 2024
Reference Satellite | Mean Bias (Uncertainty) |  |  |  |  | 
 | VI004_0.47 μm | VI005_0.51 μm | VI006_0.64 μm | VI008_0.86 μm | NR013_1.37 μm | NR016_1.61 μm
S-NPP/VIIRS | -4.20 (±2.21) | -0.71 (±1.15) | 1.07 (±1.07) | 0.04 (±1.14) | -2.11 (±0.74) | 5.20 (±0.98)
NOAA-20/VIIRS | -2.49 (±1.87) | 1.15 (±1.19) | 2.67 (±1.02) | 1.88 (±1.19) | 2.82 (±0.65) | 8.61 (±1.04)
NOAA-21/VIIRS | -2.19 (±1.75) | 1.59 (±1.23) | 2.13 (±1.00) | 2.60 (±1.20) | 0.55 (±0.71) | 6.00 (±0.97)

## Slide 10: KMA’s Calibration Results (VIS/NIR) (2)
GSICS DCC radiance mode and mean time series and histogram in 2024

## Slide 11: KMA’s Calibration Results (IR)
Statistical Summary of GK2A/AMI IR Calibration Performance in Jan. 1 ~ Dec. 31, 2024
GK2A AMI IR channels are stable
GK2A AMI has relatively large negative bias around -0.2K for 6.9µm, while the other channels are blow ±0.1K
Reference Satellite |  | Bias (Uncertainty) |  |  |  |  |  |  |  |  | 
 |  | SW038 (3.8㎛) | WV063 (6.3㎛) | WV069 (6.9㎛) | WV073 (7.3㎛) | IR087 (8.7㎛) | IR096 (9.6㎛) | IR105 (10.5㎛) | IR112 (11.2㎛) | IR123 (12.3㎛) | IR133 (13.3㎛)
CrIS | NOAA-20 | 0.01 (±0.02) | 0.01 (±0.01) | -0.18 (±0.01) | -0.07 (±0.01) | 0.06 (±0.02) | 0.01 (±0.02) | 0.10 (±0.02) | 0.10 (±0.02) | 0.08 (±0.01) | 0.01 (±0.01)
 | NOAA-21 | 0.03 (±0.02) | 0.03 (±0.01) | -0.16 (±0.01) | -0.05 (±0.01) | 0.08 (±0.02) | 0.03 (±0.01) | 0.10 (±0.01) | 0.10 (±0.01) | 0.08 (±0.01) | 0.02 (±0.01)
IASI | Metop-B | 0.05 (±0.01) | -0.01 (±0.01) | -0.19 (±0.01) | -0.07 (±0.01) | 0.01 (±0.01) | -0.09 (±0.02) | 0.07 (±0.01) | 0.07 (±0.01) | 0.06 (±0.01) | -0.02 (±0.02)
 | Metop-C | 0.05 (±0.01) | -0.01 (±0.01) | -0.20 (±0.01) | -0.08 (±0.01) | 0.02 (±0.02) | -0.04 (±0.01) | 0.07 (±0.01) | 0.08 (±0.01) | 0.07 (±0.01) | 0.00 (±0.01)
Standard Temp.(K) |  | 285.9 | 234.9 | 244.1 | 254.5 | 283.7 | 259.1 | 286.1 | 286.0 | 283.8 | 269.4

## Slide 12
Q & A

## Slide 13: KMA’s Calibration Results (IR)

## Slide 14: KMA’s Calibration Results (IR)