## Slide 1: GSICS Lunar Subgroup Session Report
Tom Stone (USGS)

## Slide 2: 2025 Meeting Lunar Session
The session covered 3 topics, plus a brief update on the MLO-LUSI project
  MLO-LUSI project has been discontinued; NIST is looking for another institution to take it over
Lunar calibration of sensors — Meteosat Third Gen Flexible Combined Imager (FCI)
  Challenges to extract complete Moon disk images — the Moon appears in a narrow region surrounding the Earth disk
  Comparisons to 2 lunar models: GIRO and LESSR
    GIRO comparisons for 1.6μm show a phase angle dependence — this is an artefact of GIRO
    results for 1.3μm channel show different trends for the 2 models, but this is preliminary work
LSICS development — the main activity of the GSICS Lunar Subgroup
  LSICS is intended to replace the GIRO, the GSICS lunar calibration reference since 2014
  Active development group: defining specifications, functionalities, requirements, code structure, file formats, interfaces, etc.
  Requirement for back-compatibility with GIRO: I/O and SRF inputs
  Requirement to accommodate different lunar models in the framework — standard interfaces

## Slide 3: 2025 Meeting Lunar Session
New lunar model development — Lunar Extended Satellite Simulation Reflectance (LESSR) model
  Constructed from basis of SCIAMACHY data, v10 calibration
  On-board solar measurements provide lunar reflectance measurements directly
  High-accuracy lunar irradiances from air-LUSI were used to build a correction factor, leading to absolute uncertainties ~0.6% for LESSR v3.0
Discussion question: should lunar calibration work in the VIS/NIR, IR, MW and UVN-S subgroups be consolidated within Lunar Calibration subgroup ?
  The techniques for using the Moon in IR and MW are different from VIS/NIR and UV
  Improved coordination among the subgroups is perhaps the better approach
  Reach out to other SG chairs to gauge interest in consolidating efforts under the Lunar SG
Action: Lunar SG chair (Tom Stone) to coordinate with MW and IR chairs on sharing invitations to web meetings

## Slide 4: 2025 Meeting IR Session
Lively discussion on the usefulness of the Moon for radiometric, spectral, and geometric calibration
  Can the Moon be an accurate enough to replace on-board calibrators ?
  Is the spectral signature well defined enough to enable spectral calibration ?
  Are sensor IFOVs sufficiently well known to enable geometric/geolocation calibration ?
Discussion on best practise for extracting lunar calibration measurements from observations
  Aligns with a recommendation from the LCWS4 (2023 @ EUMETSAT) to prepare a publication on best practises for lunar calibration
Question on availability of lunar observations in IR for sharing
Action: EUMETSAT (S. Wagner) to investigate the status of the IASI lunar dataset and check how to make it available to the community

## Slide 5: Lunar Subgroup Other Business
Web meetings of the Lunar SG to start in 2025
Investigating the use of AI to derive a lunar model using all available sources of lunar irradiance measurements
Refining the scope of the Lunar Calibration SG: cross-cutting with only VIS/NIR and UNV-S subgroups, or bring in IR and MW ?
Action: Lunar SG chair (Tom Stone) to liaise with the other GSICS subgroup chairs to establish a way forward to coordinate lunar activities
Planning for the next Lunar Calibration Workshop
  Desired every 2-3 years, LCWS4 was in December 2023
Action: In coordination with the GSICS subgroups and the lunar calibration community, Lunar Calibration Subgroup to initiate the discussion on the need and the organisation of the next GSICS/IVOS Lunar Calibration Workshop