## Slide 1: VIS/NIR subgroup report 2025 annual meeting
March 21, 2024

## Slide 2: VIS/NIR calibration strategy
The VIS/NIR does not have a hyper-spectral SI traceable instrument to tie the GEO and LEO imagers to a common reference
  The CLARREO (late 2026), TRUTHS (2030), and Libra SW hyperspectral SI traceable observations once available for target sensor radiometric scaling
  Can use HAOC, EMIT, DESIS, etc to prepare
Consistent multiple independent sensor stability monitoring and sensor pair inter-calibration methodologies validates the strategy
Need VIS/NIR subleads to promote calibration strategy
  Determine best practices amongst agencies
  Determine (real-time) sensor stability monitoring plots for web sites
  Determine how to tie the target sensor absolute calibration to CLARREO

## Slide 3: VIS/NIR sensor references
For reflective solar band imagers
  Aqua-MODIS from 2002 to 2018
  NOAA-20 VIIRS from 2018 to present
    VIIRS has both a NOAA and NASA instrument calibration teams and their L1b calibration agrees mostly within 0.2% and the calibration is well documented
    NOAA-21 VIIRS sensor performance is similar to NOAA-20 VIIRS, however, NOAA20 performance has not degraded
For the solar spectra
  TSIS-1 HSRS solar spectra
    Very high spectral resolution anchored to the TSIS-1 solar observations
  Recommend sensor calibration teams that measure reflectances (use of solar diffusers) to use the HSRS spectra for radiance observations
  The future NASA reprocessing of the VIIRS L1b product will use the TSIS-1 HSRS spectra

## Slide 4: VIS/NIR group previous year web meetings
We had 4 monthly web meetings
April 2024,
  Scott discussed the PIPS calibration approach
  Raj discussed the empirical SWIR band BRDFs
September 2024
  Junwei further discussed PIPS calibration,
  Bei Zhang discussed AGRI and MERSI DCC calibration implementation
  Conor and Prathana discussed DCC calibration improvements
November 2024
  Patrice and Beatrice gave an overview of PICSCAR
  Fangfang an update on the GOES-19 ABI performance
  Daisuke used stars to calibrate Him-8 and Him-9
January 2025
  Daile compared lightning mapper products
  Banghua discussed NOAAs effort to monitor sensor stability
  Xi discussed PICS

## Slide 5: VISNIR annual summary
Lightening Mapper participation in the GSICS VIS/NIR community
  Can intercalibrate the reference channel
  The Lightning flash event detection is complicated and beyond the scope of GSICS
DCC calibration progress
  Utilizing the kernel density function to bypass the discretization of histogramming
  Utilizing the right inflection, which seems to be the most stable and best suited for inter-calibration.
  Use seasonal channel specific SWIR channel BRDFs
Desert calibration
  CMA has introduced the pseudo invariant pixel approach
  Ali has gone over the complexity of desert calibration
  Collaborating with the CEOS community, looking into the PICSCAR approach
Harmonization efforts of multiple VISNIR approaches
  SPOT-VGT1, SPOT-VGT2, and PROBA-V Time
  MSG-SEVIRI, Sentinel-3 OLCI, Sentinel-3 SLSTR, and Metop-AVHRR
  MERSI sensors
Ray-matching sensitivity studies

## Slide 6: Future Web Meetings
VIS/NIR meetings are held the 2nd Thursday in the month and are 2 hours.
We would have from 2-4 presentations
The monthly web meetings allow for long discussions for a deep understanding of the concept and formulate solution and best practices.
The following topics have been identified
  Patrice Henry, to discuss the CEOS PICSCAR desert calibration approach
  Masaya Takahashi, to further discuss ray-matching improvements
  Ali Mousivand, to go over his desert (4i) and multiple FCI calibration approaches (4d)
  Dave Doelling to go over the DCC stability and DCC inter-calibration methodology improvements, Raj to go over DCC ATBD
If you would like to present at a future web meeting, please email me your title, anything related to VIS/NIR calibration approaches, sensors, etc. is welcome