## Slide 1
Current Status of Calibration and Validation for GEMS Level 1 Products
Yeeun Lee1), Myoung-Hwan Ahn1), Mina Kang2,3), Mijin Eo1), Jeonghyeon Seo4), Kyounghwa Lee4), Jaehoon Jeong4), Dai Ho Ko5), Jhoon Kim6)
1) Ewha Womans Unversity, Republic of Korea
2) City College of New York, USA
3) NOAA-Cooperative Science Center for Earth System Sciences and Remote Sensing Technologies, USA
4) Environmental Satellite Center, National Institute of Environmental Research (NIER), Republic of Korea
5) Korea Aerospace Research Institute (KARI), Republic of Korea
6) Yonsei University, Republic of Korea
March 19, 2025
[UVN Session, GSICS Annual Meeting 2025]

## Slide 2: GEMS: Five Years of Operation
Air quality monitoring via UV-VIS hyperspectral instrument
TROPOMI (ESA, 2017)
Veefkind et al. (2012)
GEMS (NIER, 2020)
Kim et al. (2020)
TEMPO (NASA, 2023)
Zoogman et al. (2017)
UVN/Sentinel-4 (EUMETSAT, TBU)
Gulde et al. (2017)
OMPS (NOAA, 2011, 2017 & 2022)
Flynn et al. (2014)
2000
2005
2010
2015
2020
2025
...
OMI (NASA, 2004)
Levelt et al. (2006)
Since 2000,
SCIAMACHY: SCanning Imaging Absorption SpectroMeter for Atmospheric CHartographY
OMI: Ozone Monitoring Instrument
GOME-2: Global Ozone Monitoring Experiment-2
OMPS: Ozone Mapping and Profiler Suite
TROPOMI: TROPOspheric Monitoring Instrument
TEMPO: Tropospheric Emissions: Monitoring of POllution
GOME-2 (EUMETSAT, 2006, 2012 & 2018)
Munro et al. (2016)
SCIAMACHY (ESA, 2002)
Bovensmann et al. (1999)
Low Earth Orbit (LEO)
Geostationary Earth Orbit (GEO)

## Slide 3: GEMS: Five Years of Operation
Geostationary Environment Monitoring Spectrometer (GEMS)
E
W
@ 487 nm
L2 | Fitting window [nm] | Retrieval
SFC | - | AC-BRDF-BSR
CLD | 460-486 (O2-O2) | DOAS
AEH |  | 
AOD | 354, 388, 412, 443, 477, 490 | OE
NO2 | 432-450 | DOAS + STS
SO2 | 312-335 | DOAS + PCA
O3P | 310-340 | OE
O3T | 312.34, 317.35, 331.02, 340, 354, 360, 380 | OE
VOC | 329.3-358.6 (HCHO) 433.0-461.5 (CHOCHO) | BOAS
UVI | 354 nm | LUT
East Asia & the Pacific (3.5 7.7 km2)
Every hour during daytime (7~8 times)
300-500 nm (FWHM<0.6 nm)

## Slide 4: GEMS: Five Years of Operation
Level 0-1B Process
Level 0
Co-addition Correction
Pixel Flagging
Crosstalk/
Nyquist Phase Correction
Offset/Linearity Correction
Smear Correction
Gain/
FPE Temperature Correction
Integration Time/PRNU
Dark Correction
Geometric Calibration
Stray Light Correction
Spectral Shift Correction
(Ir)radiance Calibration
2-Pixel Binning
L1B-Earth
Spatial Registration
Diffuser BTDF
Spectral Shift Correction
Spatial Registration
2-Pixel Binning
L1B-Solar
Green Box: updates
BTDF Correction
Degradation Correction
Empirical correction
(On-going update)

## Slide 5: GEMS: Five Years of Operation
Level 0 & observation frequency
Earth
Solar diffusers
LED
Dark
NOR (L0)
Solar Dark
WSD (L0)
RSD (L0)
LED Dark
LED (L0)
Onboard
Calibration System
2 times a day
8 times a day during daytime (mostly 23, 00-07 UTC)
Every day (right before solar observation)
Every day (mostly 13-14 UTC before local midnight)
2 time a year (near the Equinox)
Every week (right after LED observation)
Every week (17 UTC)
Level 0
: To monitor sensor response changes and channel band centers.
Frequency
: To verify pixel aliveness and monitor non-linearity.
Long-term observation data have been accumulated - over 4.5 years

## Slide 6: Long-term Monitoring: Telemetry (related to temperature)
Temperature variations - FPA & FPE (Close to CCD)
Courtesy: J. Seo (NIER)
-21.248
-21.251
-21.251
-20.903
-20.896
-20.901
-21.244
-20.906
Requirement: 20.5 1
Focal Plane Array (FPA)
Focal Plane Electronics (FPE)

## Slide 7: Long-term Monitoring: Level 0 calibration data
Dark currents & LED
Mean LED relative signals
Mean dark signals (SDK)
Fluctuations having similar patterns with the FPE Temp.
Increase by 9.3%
~0.3% increase

## Slide 8: Long-term Monitoring: Level 0 (solar observations)
Digital counts of WSD & RSD
300 nm (North)
300 nm (South)
500 nm (North)
500 nm (South)
Courtesy: J. Seo (NIER)
North
South
500 nm
300 nm
~12 times of observations since 2020
RSD (on Equinox)
WSD (every day)

## Slide 9: Long-term Monitoring: Level 1 (solar observations)
Solar irradiance (w/o BTDF update)
Spatial anomaly [%]
Temporal variations at each spatial index [%]
@ 305 nm
@ 480 nm
* BTDF: Bi-directional Transmittance Distribution Function

## Slide 10: Long-term Monitoring: Level 1 (solar observations)
Solar irradiance (w/ BTDF update)
Spatial anomaly [%]
Temporal variations at each spatial index [%]
Major calibration issues:
Diffuser degradation
Stripe-like artifacts along N-S direction
Discontinuity with GEMS reboot
Kang et al. (IEEE TGRS 2024)
Degradation over 12% @ 305 nm
@ 305 nm
@ 480 nm

## Slide 11: Current Level 1 Calibration Issues
1) GEMS diffuser degradation
z
Scan mirror
Solar diffuser
Solar Irradiance
Earth Radiance
Telescope
Spectrometer
Detector
Electronics
…
WSD:
RSD :
: Total degradation
: Diffuser contribution
: Degradation from common parts
: Temporal variations
Fitting function
:
Ludewig et al. (AMT 2020) & Larry Flynn (NOAA)
Similar degradation approach
for TROPOMI using WSD & RSD

## Slide 12: Current Level 1 Calibration Issues
1) GEMS diffuser degradation
Diffuser degradation correction:
Ratio to the initial observation

## Slide 13: Current Level 1 Calibration Issues
2) Stripe-like artifacts along north-south direction on the CCD
  Clearly appear in weak signals about 2% variations (i.e., dark ocean)
Radiance
March 20, 2022
* Potentially by non-linearity correction in the ADC process
Reflectance =

## Slide 14: Current Level 1 Calibration Issues
3) Instrument reboot
  Occurs when GEMS is rebooted after entering survival mode, potentially related to electronic chain
@ 480 nm (Nadir)
% depending on WV
5/9, 2021

## Slide 15: Validation Results – after BTDF update
Collocation w/ TROPOMI BD3-4 and OMPS/SNPP NM
  January 2021 – February 2025, five-days interval
DCCs
SSP
Irradiance Radiance Reflectance
Irradiance Radiance Reflectance

## Slide 16: Validation Results – after BTDF update
Collocation w/ AMI/GK-2A and TROPOMI
Condition | All scenes | Ocean | Cloud
General | Elimination of sun-glint, land, and bad pixels SZA & VZA < 40 Longitude > 100 |  | 
Scene specific | < 5% | < 1% IR10.5 > 280 K R0.47 < 0.15 | < 3% IR10.5 < 220 K R0.47 > 0.7
Condition | All scenes | Ocean | Cloud
General |  |  | 
Scene specific |  |  | 
* Re-gridding (0.25)
Linear regression (weighted) Bias [%]
Lee et al. (GRL 2024)

## Slide 17: Summary & Future Works
Remaining GEMS calibration issues
Issue (prominent) | Irradiance (IRR) | Radiance (RAD) | Reflectance (REF) | Effect | EOSRL 2024 (Research purposes)
North-South dependence | O | X | O (inverse) | Systematic bias along the N-S direction | Reduced (<1%, REF)
Diffuser degradation | O | X | O (inverse) | Higher degradation in ~300 nm | On-going
Sensor degradation (post diffuser) | O | O | X | Degradation | -
BTDF Negative bias | O | X | O | Systematic bias | Increase by 10% on IRR
Stripping | O | O | X | N-S spatial discontinuity | -
Reboot discontinuity | O | Potential | Potential | Temporal discontinuity | -
Radiometric calibration coefficient | O | O | X | Systematic bias | On-going
* Updated only for IRR